## Slide 1: ELECTRIC STUMULATION OF NERVE AND MUSCLE

## Slide 2: Stimulation Of A Nerve

## Slide 3: A Nerve Impulse
When a nerve fiber is in resting state there is a difference of potential between the outer and inner surface of plasma membrane. The outer surface bear a positive charge, the inner a negative charge.
In this state plasma membrane is not permeable to sodium ions, these positive ions accumulate on its outer surface, and there is an associated arrangement of other ions, following a definite pattern, inside and outside the membrane.
if potential difference falls below a certain level, the membrane becomes permeable to sodium ions.

## Slide 5
A nerve impulse is initiated if any factor causes the p.d. across the plasma membrane of the nerve cell or fiber to fall below this level.
When sodium ions begin to enter the axon, causing a further fall in p.d. and increase in the permeability of the membrane to the ions.
There is also rearrangement of other ions, and the process builds up until there is a reversal of the outer surface of membrane becoming negative, the inner one positive
currents are now set up between this activated part of the nerve and the adjacent area, which is still in its resting state.
The currents result in restoration of the resting p.d. in the activated part of the nerve fiber and a fall in that across the plasma membrane of the adjacent area
The sequence of events describe above then takes place in this area. Thus reversal of p.d. is transmitted along the nerve, and is an essential feature of a nerve impulse

## Slide 7: Electrical Stimulation
If an electric currents of sufficient intensity is applied to the body, a nerve impulse can be initiated.
The plasma membrane of the nerve fiber forms a resistance, which lies in series with the other tissue, so a p.d. is set up across it as the current flows.
The surface of membrane near the cathode become negative in relation to the opposite surface
On the side of the nerve near the anode, this increase the resting p.d. across the membrane, but on the side near the cathode additional charges are of opposite polarity to those present on the resting membrane and so reduce the p.d. across it.
if the p.d. falls below the level at which the membrane becomes permeable to sodium ions, these ions begins to enter the axon and series of events takes place. Thus a nerve impulse is initiated

## Slide 10
An impulse is initiated if the p.d. falls sufficiently across any part of plasma membrane of the nerve cell or fiber.
If the cathode is applied over the superficial nerve, the side of the nerve nearer to the cathode is activated.
But if anode is applied, it also can cause the initiation of the nerve impulse. In this case it is the aspect of nerve farther from the electrode that is activated.
The current spread in the tissue, so the current density is rather less on the farther surface of the nerve than the nearer one, and in consequence the anode is less effective than the cathode in initiating an impulse

## Slide 11: Accommodation
When a current flows at the constant intensity the nerve adapts itself, to the altered condition, this is being known as accommodation
So an unvarying current is not effective in initiating an impulse.
When the current rises in intensity the impulse is initiated, but a fall in current intensity can also initiate an impulse.
While the current flows at constant intensity, accommodation of the nerve takes place and the p.d. resulting from the current flow no longer affects the excitability of nerve fiber, which has adapted itself to the altered condition
When the current ceases the p.d. which it caused across the plasma membrane suddenly disappears, so altering the total p.d. across the membrane

## Slide 12
On the aspect of nerve nearer to the anode the extra p.d. was augmenting that that across the resting membrane, and its sudden loss causes a fall in the p.d. if this fall is to the level at which the membrane becomes permeable to sodium ions, an impulse is initiated.
A fall in intensity of current is less affective than a rise in initiating an impulse. It is the side nearer to the anode that is affected, as the nerve has the property of accommodation a current which rises or falls suddenly in intensity is more effective in initiating an impulse than one which changes slowly.
If variation in current is gradual there is time for accommodation to take place, and a greater intensity is needed to be effective, than if the variation is sudden
A current that change very slowly does not initiate a nerve impulse

## Slide 13: Effect of the nerve impulse
When nerve impulse is initiated at a nerve cell or end organ, there is only one direction in which it can travel along the axon, but if it is initiated at some point on the nerve fiber it is transmitted in both directions from the point of stimulation.

## Slide 15
When a SENSORY NERVE is stimulated the downward travelling impulse has no effect, but the upward travelling impulse is appreciated when it reaches conscious levels of brain.
If impulse of different durations are applied, using the same intensity of current for each, it is found that the sensory stimulation experienced varies with the duration of impulses.
The impulse of long duration produce an uncomfortable, stabbing sensation, but this becomes less as the duration of impulses are reduced.
Until the impulses of 1 millisecond and less, only a mild, prickling sensation is experienced

## Slide 16
When a MOTOR NERVE is stimulated, the upward travelling impulse is unable to pass first synapse, as it is travelling in the wrong direction, but downward travelling impulse passes to the muscle supplied by the nerve, causing them to contract

## Slide 17: Stimulation of Innervated Muscle

## Slide 18
When a stimulus is applied to a motor nerve trunk, impulses pass to all the muscles that the nerve supplies below the point at which it is stimulated, causing them to contact.
When the current is applied directly over an innervated muscle the nerve fibers in the muscle are stimulated in the same way.
The max response is over the motor point( the point at which the main nerve enters the muscle)
Or in case of deep muscles, the point where the muscle emerges from under the cover of more superficial ones

## Slide 19: Type of Contraction
When a single stimulus is applied, impulses pass simultaneously to a number of motor units so that , there is sudden brisk of contraction, followed by immediate relaxation
If a succession of stimuli are applied at infrequent interval, e.g.one stimulus per second, each produces an isolated muscle contraction and there is time for complete relaxation between the impulses.
Increase in the frequency of the stimuli shortens the periods of relaxation, and when frequency exceeds 20 per second, there is no time for complete relaxation between contraction so partial TETANY occur
At the frequency 60 per second, no relaxation at all, contraction is fully tetanic

## Slide 20: Strength of Contraction
This depends on the number of motor units activated, which depends on the intensity of the current applied

## Slide 21: Rate of Change of Current
A current which changes suddenly in intensity is found to be more effective in stimulating the innervated muscle than gradually changing currents
As the later provide time for accommodation of the nerves.
If the intensity rises suddenly as in rectangular impulses, there no time for accommodation to take place, and a muscle contraction take place.
If current rises slowly, trapezoidal, triangular & saw tooth impulses, there is some accommodation and greater intensity of current is required to produce contraction
Slower the rate of change of the current, the greater is the intensity needed to be effective, and a current which rises and fall very slowly does not produce a muscle contraction

## Slide 22: Duration of Stimulus
Effects of stimuli of different durations,
Current is interrupted D.C. rectangular impulses
Duration is 0.01. 0.03, 0.1, 0.3, 1, 3, 10, 30, 100 milliseconds
Current is applied to the normally innervated muscle, impulse 100 millisecond and increase the intensity so that minimal contraction is obtained,(note intensity)
Then shorten the duration and observe intensity needed to produce contraction
It is found that the stimuli of longer duration i.e. down to variable point, usually 10 to 1 or between 1 or 0.1 milliseconds produces a muscle contraction with same intensity
But when the impulse is shortened beyond this level, a greater intensity of current is required each time the duration of impulse is reduced.

## Slide 23
So with the impulses of shorter duration, the briefer the period for which the current flow, the greater is the intensity needed to cause the p.d. across the plasma membrane of the nerve to fall to a critical level at which the nerve is initiated.
With the impulses of longer duration, the time for which the current flows does not affect the response obtained. This is because there is time for accommodation of the nerve, which takes place before the flow of current is completed, so that only the first part of each stimulus is effective.

## Slide 24
Strength duration curve:
“A graph is plotted of intensity of curve (effective voltage) against the duration of stimulus, such a graph is termed as strength duration curve”
A logarithmic scale is used as it magnifies the part of the curve showing the effects of the stimuli of shorter duration.
The chronaxie and rheobase can be read from the strength duration curve.

## Slide 27
The Rheobase
Is the minimum intensity of current that will produce a response if the stimulus is of infinite duration.
The Chronaxie
Is the minimum duration of the impulse that will produce a response with a current of double the rheobase.
For example: if rheobase 6 milliamperes, the chronaxie is the duration of shortest impulse that will produce a muscle contraction with a current of 12 milli amperes
Chronaxie of normally innervated muscle is short, often being less than 1 milliseconds

## Slide 28: Pole Used for Stimulation
A nerve impulse is initiated by either a rise or a fall in the intensity of currents, but the former is the more effective and is commonly used for nerve stimulation.
When the current rises in intensity, the cathode is more effective than the anode in initiating a nerve impulse.
So, provided that the intensity of current is not altered, the contraction obtained when the cathode place over a nerve or muscle is stronger than that obtained by when the anode is used

## Slide 29: STIMULATION OF DENERVATED MUSCLE

## Slide 30
When a current is applied to denervated muscles, the muscle fibers can be stimulated directly.
The manner in which this is brought about is similar to that in which a nerve fiber is stimulated, there being changes in the potential difference across the plasma membrane of muscle fiber.
Denervated muscle does not react to the electrical electrical stimuli of shorter duration so readily as does the motor nerve, provided that the intensity of the current and duration of stimuli is adequate, contraction of muscle results.
As each fiber must be stimulated directly, the maximum response occurs when the current passes throught the greater number of fibers,
So it is usually obtained with a longitudinal application, one electrode being placed over each end of muscle belly

## Slide 31: Type of Contraction
A single stimulus causes an isolated muscle contraction, but this contraction along with relaxation is more slow than motor units, so called as “sluggish” contraction
Impulse with duration ___ 100milliseconds
Repeated with frequency that not produce tetany

## Slide 32: Strength of Contraction
Depends on
No. of muscle fiber stimulated
And so the intensity of current
Other factors described further…………..

## Slide 33: Rate of Change of Current
Property of accommodation is less marked
Currents of sudden increase in intensity are as affective as currents of gradual increase in intensity
Impulses like trapezoid, triangular, and saw tooth are termed as “selective impulses” as they can produce contraction in denervated muscles with lower intensity than that required for innervated muscle

## Slide 34: Duration of Impulses
Effects of stimuli of different duration is same as that of innervated muscles.
The Strength Duration Curve:
Different in shape as that of innervated muscles
The intensity of current has to increase each time the duration is reduced.
This is because the denervated muscle has not the same property of accomodation as has the motor nerve.
So longer the duration less is the intensity of current required for denervated muscles
Muscle contraction are not obtained with impulses of shorter duration
Rheobase may be less than the that of innervated muscle, but the chronexie is longer , often being more than one millisecond

## Slide 35: Pole used for Stimulation
The contraction produced when anode used as stimulating electrode is stronger than the cathode, while current of same intensity is used.
Reason is not known.
As the practice proves this so anode is used as active electrode

## Slide 36: Thanks