## Slide 1: The Faradic and Sinusoidal Currents

## Slide 2: The Body as a Conductor of Electricity

## Slide 3: Physiological Effects of Faradic Type of Currents

## Slide 4: 1. Stimulation of Sensory Nerve
When faradic type of current is applied to the body, a mild prickling sensation is experienced.
That is due to the stimulation of sensory nerves.
The sensory stimulation causes a reflex vasodilatation of the superficial blood vessels, so that there is slight reddening of the skin, or erythema.(But not have practical value)

## Slide 5: 2. Stimulation of Motor Nerve
The current of faradic type stimulates the motor nerve,( use sufficient intensity), causes the contraction of muscles which they supply.
Stimuli are repeated 50 times/sec or more, the contraction is tetanic.
Muscle fatigue is produced.
So current is commonly surged or interrupted to allow for muscle relaxation.
When current is surged the contraction gradually increases and decreases in strength,( natural manner of muscle contraction)
When current is interrupted the contraction commences and ceases suddenly, being maintained during the period of current flow

## Slide 6: 3. Effects of Muscle Contraction
When a muscle contract as a result of electric stimulation, the changes taking place with in the muscle are similar to those associated with voluntary contraction.
There is increased metabolism, with a consequent increase in the demands O2 and food stuff, and increased output of metabolites.
Metabolites cause dilatation of capillaries and arterioles, considerable increase in blood supply.
Contraction and relaxation of muscle exert pumping action on the veins and lymphatic system lying around it. Increase venous and lymphatic returns.

## Slide 7: 4.Effects on Denervated Muscle
Not satisfactory
As intensity of current required to produce a contraction of denervated muscle for impulse of 1 millisecond is usually too great to be tolerable for treatment.

## Slide 8: 5. Pole Used for Stimulation
With faradic coils no polarity is marked as current is alternating.
Muscle contraction should be produced most easily if the active electrode is connected to terminal that is negative during the high peak of current
cathod

## Slide 9: 6. Chemical Effects
Chemical formation due to DC
Electolytic burns
Alternating currents: changes neutralise each other effects if forward waves equals the back wards
If not then chemicals are formed but too little to produce electrolytic burns
Faradic current duration of impulse is too little to produce chemical change

## Slide 10: PHYSIOLOGICAL EFFECTS OF SINOSUIDAL CURRENTS

## Slide 11: 1. Stimulation of sensory nerves

## Slide 12: 2. Stimulation of motor nerves
Frequency 100/sec
Surged
But marked sensory stimulation so not suitable

## Slide 13: Effects of muscle contraction

## Slide 14: Effects on denervated muscles

## Slide 15: Chemical effects and pole used for stimulation
No chemical effects
Both phases of each cycal are identical

## Slide 16: THERAPEUTIC EFFECTS OF FARADIC AND SINUSOIDAL CURRENTS

## Slide 17: Muscle Contraction
Both faradic and sinusoidal
Innervated muscle
Surged
Faradic is better! Y?????

## Slide 18: Facilitation of Muscle Contraction
Unable to produce muscle contraction, pain or recent injury
Muscle spindle machanism ( normal mechanism)
pain; inhibition of large AHC
Eg; contraction of quards in painful RA

## Slide 19: Re-education of Muscle Fiber
Prolonged disuse or incorrect use
Eg; 1. intrisic muscle of foot in long standing flatefoot.
2. abductor hallucis in hallux valgus
Brain appreciated movement not the muscle action

## Slide 20: Training of New Muscle Action
After tendon transplant
Other reconstruction operation
Faradic current
Pt concentrate the movement and attempt to assist the movement
Longer to achieve than re-education

## Slide 21: Exercise for Paralysed Muscle
Neuraparaxia: until the regeneration completed
Severed nerved; until that muscle responds to faradic
Incomplete nerve lesion; faradic is little indicated

## Slide 22: Strengthening and Increased Bulk of Muscle
Condition;
Infalammation
Injury to joint concerned
i.e. active movt is not possible
But
Active & resisted exercise are the best choice of treatment

## Slide 23: Increased Blood Supply
Vasodilatation
Reflex effect of sensory stimulation
Effective when large area is involeved
Bath application and sinusoidal is prefered to faradic
Circulatory deffects

## Slide 24: Improved Venous and and Lymphatic Drainage

## Slide 25: Prevention and Loosening of Adhesions

## Slide 26: TECHNIQUE WITH FARADIC AND SINUSOIDAL TREATMENT

## Slide 27: Preparation of Apparatus
An electronic stimulator with automated surger
Smart Bristow Faradic coil
Testing of apparatus
Test the apparatus by attaching the leads and electrodes to the terminals
Holding the two electrode to the moistened hand
Inserting the core if smart Bristow coil is being used
Turning up current until a mild prickling sensation is experienced and muscle contraction is produced
If surging is automated, duration and frequency of surged should also be tested

## Slide 28
Active electrode:
Disc electrode/ small lint pad with a flat plate electrode(for larger muscle, quards, mold to make good contact)
Indifferent electrode:
Flat plate and lint pad
The pad consist of at least 8 layers of lint, so that thick enough to make good contact with tissue and electrode, absorb any chemical that might be formed
Folded evenly, no creases, or there with be uneven distribution of current and consequent discomfort,
Pads and lint covering the disc electrode are soaked in warm 1% saline
Tape water can be used but addition of salt can reduce the resistance of tissue
Electrode, 1cm smaller than pad, reduce the danger of coming in contact with skin
Corners of electrode should be rounded as points may become bent dig into the pad again causing concentration of current

## Slide 29: Preparation of Patient
Clothing is removed from the area to be treated
Pt is supported comfortably in a good light
Pt should be warm, muscle will not respond well to the stimulus
Muscle contraction are good if part is supported, muscle in shortened position
If re-education of muscle is required, position the pt so that movt can be achieved, as in case of quards, limb is placed in slight flexion,
Sling can also be used to support the limb, as in cases of deltoid.
The joint Movt should be avoided if it causes pain.

## Slide 30: Application of Electrodes
The skin has high resistance to an electric current, as the superficial layer is dry, contain few ions.
Wash with soap, removes natural oils, moistened with saline.
Breaks in skin, decrease resistance, increase current density, discomfort.
So apply petroleum jely, cover with non absorbent cotton wool o protect the electrode
Indifferent electrode:
place in the area where no other muscle contraction can be produced especially that of antagonist
Best place is the main trunk of the nerve that supplied to the muscles to be treated, i.e. medial epicondyle of humerus for flexors of forearm.

## Slide 31
3. Not cover the motor point
Where not convenient to place on nerve trunk, any suitable area is choosen, for shoulder girdle, upper part of anterior chest wall
Indifferent pad should be large enough to reduce the current density to minimum
Ind. Electrode may be fixed properly with bandage or rubber strap.
Cover it properly, not to wet the patients clothes

## Slide 32: Application of current
Active electrode on the Motor point
MOTOR POINT: def
Point of Best contraction
Location: frequently at the junction of upper and middle one third of the flashy belly of muscle
Exceptions are always there;
Vastus medialis; lower part of muscle
Extensor hallucis longus; deep muscle

## Slide 33
Active electrode must be held firmly.
Firm contact ensures minimum of dis comfort.
Intensity of current should be increased gradually, until a good contraction is obtained.
Surging must allow the more rhythmical contraction and relaxation of muscles
Voluntary contraction at the same time as those with stimulator is produced
DURATION OF TREATMENT;
depends on condition of muscle and purpose
For re-education: length of time for which the patient concentrate to the movement and assist in its production
To Strengthen the muscle: so long as satisfactory muscle contraction is obtained in order to ensure that each muscle can perform as many contraction as ppossible
Muscle fatigue: weakening of muscle contraction: not rapidly with faradic current
20-30 min of treatment to give 90 contraction of each muscle, min treatment time
20-30 contraction at one motor point, then move to next, complete all motor points and restart from the first one, until to complete 90 contraction for each point.

## Slide 34: METHODS OF APPLICATION

## Slide 35: 1. STIMULATION OF MOTOR POINT
Advantage;
Each muscle performs it own function
Optimal contraction of each muscle can be obtained
Disadvantage;
If there are many muscle to be stimulated, it is impossible to produce a large no of contraction of each muscle

## Slide 36: 2. STIMULATION OF MUSCLE GROUP
In this method all muscle of a group work together
Two fixed electrodes are used
One place either over the nerve trunk that supplies the muscles or on their origin
Other is so that it cover the motor points of all, or over the lower part of the fleshy belly of those muscle
ADVANTAGES
Re-education of muscle that work in group like quardriceps or small of foot
Permits many more contraction of each muscle
Used for large muscle with multiple nerve supply, abdominals or longitudinal back muscles
NOT USED FOR
if muscle contract less strongly because it is placed deeply or are weaker

## Slide 37: 3. LABILE TREATMENT
An indifferent electrode is placed for the stimulation of motor point
The second electrode move over the area to be treated
The active electrode may either be a disc or a small pad with plate electrode.
The current is not surged but the electrode move towards and away from the motor point, and muscle contract and relaxed.
ADVANTAGES
Treating large muscle that have multiple nerve supply, as longitudinal back muscle
DISADVANTAGES
Difficult to gauge the required intensity of current
Sensory stimulation is more marked

## Slide 38: 4. NERVE CONDUCTION
If a motor nerve trunk is stimulated, contraction of all the muscles are produced to which it supplied beyond the point of stimulation
Indifferent electrode is placed over some convenient area
Active electrode to the area where nerve trunk is superficial
ADVANTAGES
Where motor point is inaccessible, like
Pop
Wound
Splinting
Edematous area
Most comfortable method for the stimulation of muscles of facial expression,
Three points of branches of facial nerve are stimulated
Behind the lateral corner of eye
In front of ear
Just above the angle of jaw

## Slide 39: 5. BATH TREATMENT
Both faradic and sinusoidal currents may be applied in bath. (surged and of adequate intensity to produce the muscle contraction)
Sinusoidal current is some times unsurged and used with very low intensity to avoid muscle contraction.
There are different methods for bath treatment
BIPOLAR BATH
MONOPOLAR BATH
FARADIC FOOT BATH

## Slide 40: I. Bipolar Bath
Limb is immersed in water in which two electrodes are placed, one at each end of the bath.
The current has alternative pathways through the water and through the patient tissues, so only a part of that applied passes through the tissues.
Salt should not be added(reduces skin resistance, inc. proportion of current that pass through)
Those muscle whose motor points are covered by water are stimulated.
The contractions obtained may be modified by altering the position of electrode
Example;
In bipolar arm bath;
If electrodes are placed opposite to the dorsal aspect of the limb, the extensor muscle contracts, vice versa

## Slide 41: II. Mono Polar Bath
One electrode is placed in the bath opposite to the distal part of the limb and the circuit completed either by another mono polar bath or by a pad and electrode.
In the bath some current passes through the water and some through the patient tissues, and above the water line all current passes through the tissue
Stimulation of muscle whose motor points are covered by the water and also possibly other muscles in the path of current.
Like bipolar bath, it is possible to modify the effect of current by altering the position of electrode.
The current that passes through the water enter the tissue at the water line, possibly cause some discomfort, that can be reduce by a layer of petroleum jelly on the skin at water line.
Salt as rule should not be added to the water

## Slide 42: III. Faradic Foot Bath
Although the bath treatment is not satisfactory for local treatment, but it is valuable method to treat flat foot.
One method suitable for the stimulation of the muscles of longitudinal arch is to place two electrodes transversely across the bottom of the bath.
One under the heel and other under the anterior part of foot
The muscles of the anterior transverse arch may be stimulated by placing the electrodes one on each side of the foot, levels at the metatarsals shaft, with ends of the electrodes just under the lateral borders of the feet.
In both cases water in the bath should just cover the toes
An alternative method of treatment is to place one electrode under the heel and other opposite to the motor points of various muscles, so that they are stimulated individually

## Slide 43
ADVANTAGES;
Water make good contact with tissue than electrodes
Prolonged soaking reduce skin resistance
Widespread effects can be produced, like increase in blood circulation

## Slide 44
DISADVANTAGES;
Treatment is not lacalized.
Muscles that are being stimulated, not all contract to the same degree, those are stronger & more superficial respond readily
Limb is dependent so gravity oppose the drainage of fluid from the part.
Danger of electric shock are more
Soaking in water reduces the skin resistance, so there may be great variation in the intensity of current so intensity should be increases/ decrease gradually.
PRECAUTIONS;
Washing of the part is unnecessary, but skin breaks must be covered with petroleum jelly.
Metallic objects removed from the area to avoid concentration of the current
Water of the bath should be comfortably warmth, not too hot as soaking in hot water may be exhausted for patient

## Slide 45: 6. FARADISM OR SINUSOIDAL UNDER PRESSURE
This method is used to increase the venous and lymphatic drainage from an edematous area.
Contraction of many muscles are required, and may be obtained either by placing large pads so that they cover the motor points of the main muscle group, or by nerve conduction method.
FOR NERVE CONDUCTION METHOD; main nerve trunks supplying the limb are stimulated above the edematous area.
The limb is supported in elevation, so that gravity assist the venous and lymphatic drainage.
Also limb is encased in elastic bandage, which is most effective if applied over a thick layer of brown wool.
The bandage increases the pressure on the vessels when the muscle contract, and its recoil on muscle relaxation exerts a further pumping action.
Current is applied and surged very slowly, in order to obtain a good pumping effect.
Faradic and sinusoidal both can be used, faradic more comfortable.
TREATMENT TIME; 20 min( with frequent rest as it is fatiguing)

## Slide 46: 7. FARADISM TO MUSCLE OF PELVIC FLOOR
Faradic stimulation is of considerable assistance in early re-education of muscles of pelvic floor.
IN FEMALES;
Prolapse of pelvic organs
Stress incontinence (following childbirth)
A vaginal electrode is used to get good contraction of the muscle.
Voluntary contraction must be attempted at the same time as the electric stimulation,
Electric stimulation is an accessory while exercise are the essential part of treatment.
IM MALES;
Suffer from Similar disabilities following prostatectomy.
Rectal electrode is used

## Slide 47: THANKS!