## Slide 1: THE MODIFIED DIRECT CURRENT

## Slide 2: Modification of Direct Current
INTERRUPTED DIRECT CURRENT
Interruption is most usual form of modification.
Rectangular impulses
Trapezoid, triangular and saw tooth impulses.
Selective impulses
Duration; 100 millisecond___________ 600 millisecond
Frequency; 100 millisecond_ 30 cycles/min

## Slide 3: PHYSIOLOGICAL EFFECTS

## Slide 4: Stimulation of Sensory Nerves
Impulses are of fairly large duration, so sensory effect is rather marked
Reflex dilatation of the superficial blood vessels
Erythema of skin

## Slide 5: Stimulation of Motor Nerve
Muscle contraction is produced by the stimulation of motor nerve with direct current
Stimuli are infrequently repeated, so brisk of contraction is produced, followed by immediate relaxation
Little beneficial effects
If current rises gradually and slowly, accommodation takes place

## Slide 6: Stimulation of Denervated Muscles
Capable of producing contraction of denervated muscles.
Intensity of current and duration of impulse is adequate.
Contraction are sluggish in nature, ie. Contraction and relaxation being slower than when the motor nerve is stimulated.
As denervated muscle has not the property of accommodation so the impulses rises very slowly is as effective as that rises suddenly.
With the slowly rising currents, the contraction of denervated muscle can be produced with an intensity of current that is insufficient to stimulate the motor nerve, so termed selective.
An impulse of 100 millisecond is the shortest that is generally considered satisfactory to treat denervated muscles.
And is often necessary to increase it, to eliminate the contraction of innervated muscles

## Slide 7: Poles Used for Stimulation
Anode (denervated muscles)

## Slide 8: Chemical Effects
Chemical changes in the passage of a current
Danger of chemical burns
Less with modified D.C than constant D.C.
When depolarized impulses are used the reverse wave of current between the impulses reduces the chemical formation.
If reverse waves is equal to the forward one any chemical formed are neutralized and the danger of burn eliminated.

## Slide 9: THERAPEUTIC EFFECTS AND USES

## Slide 10: Contraction of Denervated Muscles
Produce contraction of denervated muscles.
Following changes occur in the structure and function, when muscle is deprived of nerve supply
Marked wasting of muscles fibers
Tend to fibrose with long standing denervation
Loos their properties of irritability, contractibility, extensibility and elasticity.
Electric stimulation may retard these changes to occur
However it is sometimes impossible to restore these properties, once they have been lost.
It is only way to produce the contraction of denervated muscles, and by this way maintaining the vascularity of muscles and so retarding the degeneration of fibers.
300 contraction of each muscle is desirable,not possible y????
90 is the minimum no. that can be effective.
Stop the stimulation after the time of regeneration, and voluntary action is obtained, progress towards exercise

## Slide 11: CHOICE OF CURRENT

## Slide 12: Type of Impulse
Good contraction are obtained with rectangular impulses but selective impulses prove more satisfactory
ADVANTAGES;
Less sensory stimulation
Denervated muscles respond to slow intensity.
Motor nerve remain spare.
Long standing denervated only responds to slowly rising intensities

## Slide 13: Duration of Impulses
Minimum duration of 100 millisecond:
In order to ensure that all muscle fibers are stimulated
300 to 600 milliseconds :
In order eliminate contraction of innervated muscle and to stimulate the long standing denervated muscles

## Slide 14: METHODS OF APPLICATION

## Slide 15: Method 1.
One pad is fixed over the origin of the muscle group
Active electrode is a disc or small pad: either held on the lower end of fleshy belly of muscle to be stimulated.
Or stroked slowly down it.
Moving the electrode over the muscle ensures that current is passing through the maximum no. of fibers.
ADVANTAGES;
Current can be regulated to produce the optimum contraction of each muscle
Each muscle is rested, while other muscle of the group are being stimulated.
DISADVANTAGES;
Not practicable to produce large no. of contraction.
Also when large no. muscles to be treated

## Slide 16: Method 2.
Two disc may be used.
One placed over each end of the muscle to be stimulated.
Useful for the stimulation of deeply placed muscles, which are difficult to isolate
Example;
Extensor pollicis longus muscle
But difficult to hold the both electrodes and regulate the intensity

## Slide 17: Method 3.
Two pads may be fixed, one over the origin and other over the lower end of the muscle group to be stimulated.
ADVANTAGES;
Allow all muscle to contract equally.
Large no. of contraction can be elicited.

## Slide 18: Method 4.
Apply large active pad that completely cover the muscle or group of muscles to be stimulated.
The circuit being completed with large indifferent electrode.
Satisfactory and convenient method.
Example;
Muscles of shoulder girdle
Indifferent electrode on the anterior chest wall
Pad and plate electrode held over each of muscle.

## Slide 19: Method 5.
Bath method
Not satisfactory

## Slide 20: If modified D.C. in not available.
Constant current may be used, with active electrode stroked rapidly over each muscle
Stroking must be firm, rapid and rhythmical.
Muscle is stimulated as electrode pass over the muscle( discomfort and irritation of skin)

## Slide 21: TECHNIQUES

## Slide 22: Preparation of Equipment
Electronic apparatus is most satisfactory.
If D.C. used is without the reverse wave___ chemical formation____ to prevent the skin___ covering of disc electrode must be of adequate thickness.
Avoid the metals to come in contact with the pt tissue

## Slide 23: Preparation of the Patient
Wash the skin
Protect abrasions
Soak in warm water before treatment to lower resistance of skin.
If there is extensive loss of sensation care must be taken that the water is not too hot.
Best contraction is obtained when muscle is in shortened position.
But when joint movement is to be achieved, current can be applied in partially lengthened position, e.g. for small muscles like wrist.
For larger ones support the limb in sling

## Slide 24: Application of Current
Usually the active electrode is ANODE.
Ideally each patient should be tested to determine weather the anode or cathode produces the better response.
When electrodes have been applied, INTENSITY of current is increased until a good contraction is desirable.
Large no. of contraction are desirable until the sign of FATIGUE.
Limit the length of treatment.
Contractions are divided into groups, allowing rest periods between.

## Slide 25: Frequency of Treatment
For retarding the ATROPHY and MAINTAINING PROPERTIES OF MUSCLES;
Frequent intervals and adequate no of contraction.
Daily treatment is more satisfactory.(not tolerable to skin)
5-6 days a week
Skin care: washed after treatment, powder and soothing cream applied

## Slide 26: THANKS!