## Slide 1: MEDICAL IONIZATION
IONTOPHORESIS

## Slide 2: MEDICAL IONIZATION
“MEDICAL APPLICATION OF IONTOPHORESIS”
“APPLICATION OF IONTOPHORESIS TO TREAT MADICAL CONDITIONS”
Examples: wound healing, inflammatory conditions< infections etc.

## Slide 3: IONTOPHORESIS
“ IONTOPHORESIS IS A THERAPEUTIC TECHNIQUE WHICH INVOLVES THE INTRODUCTION OF IONS INTO THE BODY TISSUES THROUGH PATIENTS SKIN ( BY USING CURRENTS)”

## Slide 4
The basic principal is to place the ion under an electrode with the same charge, i.e.
Negative ion placed under cathode
Positive ions placed under anode
This technique is also known as “technique of ion transfer” into the body tissues by using electrical current as a driving force.
The electrode under which ions are placed is therefore called
ACTIVE ELECTRODE.
Type of current used______ CDC
Reason for using CDC_____ ????

## Slide 6: ADVANTAGES
PAINLESS
STERILE
NONINVASIVE

## Slide 7: DISADVANTAGES
CHEMICAL BURN
Due to direct current itself.
Not because of the ions being used.

## Slide 8: QUANTITITY OF IONS TRANFEREED INTO THE TISSUES
Depends upon
INTENSITY OF CURRENT/ CURRENT DENSITY
DURATION OF CURRENT FLOW
CONCENTRATION OF IONS AT THE ACTIVE ELECTRODE OR IN THE SOLUTION

## Slide 9: TYPE OF ELECTRODE
SIZE AND SHAPE OF ELECTRODE CAN CAUSE A VARIATION IN CURRENT DENSITY AT THE SITE OF TREATMENT.
LESS THE SIZE OF ELECTRODE MORE WILL BE THE CURRENT DENSITY AND MORE IONS WILL BE TRANSFERRED.
INCREASING THE SIZE OF ELECTRODE WILL DECREASE THE CURRENT DENSITY THUS REDUCES THE CONCENTRATION OF IONS AT THE ELECTRODE.

## Slide 10: CURRENT INTENSITY & DURATION OF TREATMENT
LOW INTENSITY CURRENTS ______ MORE EFFECTIVE
INTENSITY OF CURRENTS ______ 5mA TO 12mA
DURATION _______ 15_ 20 MINUTES

## Slide 11: METHODS OF TREATMENT
Skin cleaned with soap.
Hairy skin must be shaved.
Electrodes at proper contact with skin. Use straps.
Ions __ ointment __ a layer is applied at the site to be treated.
Ions __ solution __ lint pad of absorbent material, soaked in ionic solution.
Appropriate ions are used specific condition.
The intensity of current & duration must be regulated appropriately.
Precautions to prevent burning.
Use telcum powder if erythema is seen after treatment.

## Slide 12: COMMONLY USED IONS AND THEIR INDICATIONS

## Slide 13: POSITIVE IONS
IONS | USES
HYDROCORTISONE | Anti inflammatory: RA, Tendinitis, Bursitis
CALCIUM CHLORIDE | (calcium ion is used): Effective in joint stiffness & Post traumatic pain
ZINC OXIDE | Healing properties: Ulcers, Open lesion
MAGNESIUM | An excellent muscle relaxant, Good Vasodilator, Mild analgesic: Arthritis
DEXAMETHASONE | Anti inflammatory: Musculoskeletal conditions

## Slide 14: NEGATIVE IONS
IONS | USES
IODINE | Effective sclerolytic agent, An excellent bacteriocidal & Fair vasodilator: Adherent scars, Adhesive capsulitis.
CHLORIDE | Effective sclerolytic agent: Scars, Keloides, Burns.
SALICYLIC ACID | A general decongestant, Sclerolytic & Anti inflammatory.
SODIUM OR POTASSIUM CITRATE | RA
EITHER +/_ TAPE WATER | Hyperhidrosis, Glypyronium bromide is also used along with tape water in the cases of Hyperhidrosis.

## Slide 15: SAFTEY AND PRECAUTIONS
ANTICHOLINERGIC COMPOUNDS HAVE AN ATROPINE_ LIKE ACTION THERFORE PATIENTS MAY FEEL DRYING OF MOUTH AND THROAT.
THE PATIENT MAY FEEL RESTRICTION OF GENERAL BODY SWEATING AND THEREFORE ADVISED NOT TO GO FOR ANY STRENOUS ACTIVITIES, WHICH MAY REQUIRED SWEATING.

## Slide 16: THANKS