## Slide 1: Techniques of ultra violet irradiation

## Slide 2: Assessment of dose
The only satisfactory method is
DEGREES OF ERYTHEMA
1st degree
2nd degree
3rd degree
4th degree

## Slide 3: Factors
Factors that effects the assessment and calculation of dose
1. THE ARC LAMP
2. THE DURATION OF EXPOSURE
3. PREVIOUS EXPOSURE TO AREA
4. DISTANCE BETWEEN PATIENT AND LAMP
5. THE ANGLE OF RAYS STRIKE
6. SENSITIVITY OF SKIN

## Slide 4: The arc lamp
The out put of lamp varies according to the type of lamp and also with different lamps of the same type
The new lamp is tested and average dose for certain reaction is recorded
1 meter distance is suitable
Out put changes with time
Lamp should be tested at regular interval
It is advisable to use the same lamp throughout a course of treatment .

## Slide 5: The duration of the exposure
Longer the exposure, stronger is the reaction produced
If the dose for 1st degree erythema is known, dose for other degrees can be calculated as
2nd degree requires 2.5times the 1st degree
3rd degree _____ 5 times
4th degree______ 10 times
5th degree______ 20 times(assumed)
Suberythema dose_____ ½ or 2/3rd of 1st degree

## Slide 6: Previous exposure of the area
UV exposure should not be repeated until the erythema caused by previous dose has faded
Thickening of epidermis occurs that requires stronger dose to repeat the same reaction
To repeat
1st degree___ 25% of previous dose
2nd degree___ 50%
3rd degree___ 75%
4th degree___ 100%
Sub erythema dose is increased by 12.5%

## Slide 7
Once free peeling occurs, increased resistance is lost, dose reduced to that of first attendance
Fine peeling __slight reduction in resistance, reaction can repeat without increasing exposure
1st degree erythema or sub erythema___ imperceptible peeling___ take 3 weeks___ after 3 week dose reduce to 1st attendance ___ after 10 day dose without increasing exposure

## Slide 8: Distance between the lamp and patient
Rays from UV lamp obey “law of inverse squares”
Intensity of the rays varies inversely as the square of the distance from the burner
Thus intensity of the radiation is 4 times at 1 meter than at 2 meter, 9 times than at 3 meters
Formula old dose * new distance2
New dose= ________________________
old distance 2

## Slide 9: The angle at which the rays strike the skin
Max absorption at right angle

## Slide 10: Sensitiveness of the patient
Complexion
Fair people more sensitive than darker one
Age
Children dose not show erythema reaction, excess dose is indicated by irritability and vomiting
Children under 2 yrs should receive half the adult dose, and 2___ 6 two thirds the adult dose
Parts of body
Extensor surface is less sensitive than flexor
most exposed are less sensitive than area mostly covered with clothing, exception is the face
Dorsum of the hand 5 times, palm 15 and sole 25 times the normal dose
Mucous membranes need twice as long exposure as the skin
Sensitizers
IR
Before uv ____ increase the reaction
After uv ( erythema) ____ reduce the effects
Simultaneous _____ no effect

## Slide 11: Test dose
TECHNIQUE:
Suitable area is chosen
Clean with ether soap or water and dried
Cut 3 holes in a thick paper, placed over area and stick with plaster
The central hole exposed to the expect time required for a reaction
Other with slightly longer and slightly shorter time
Three holes respectively
Irradiate the area, cover the 1st one, continue exposure then after 1 or half min cover 2nd and so on

## Slide 12
OUT PUT OF THE LAMP
it is necessary to test the out put of a every new lamp, also on some intervals
Object is to asses average dose require for a certain reaction, usually 1sr degree erythema at 1 meter distance
Abdomen is a suitable area
3 hole should be 6 cm square in size
When test on different individuals average is taken as standard dose for that particular lamp

## Slide 13
SENSITIVITY OF THE PATIENT
When test dose precedes the general irradiation fairly large area 12cm square should be exposed
Abdomen being the good area to be tested
Washing is not required, so omit in test dose too
When test dose precedes the local irradiation, smaller area should be exposed, 6cm or 3cm square
Area tested must be the one, that requires treatment
face___ flexor surface of fore arm
Always calculate dose for 1st degree erythema and others are calculated from it

## Slide 14: Techniques of general irradiation

## Slide 15: Choice of lamp
Centrosol or group model of fluorescent tube:
If a Group of patients is to irradiated
Air cooled mercury vapour lamp or tunnel model of flourescent tube
Individual treatment

## Slide 16: Preparation of apparatus
MVL :
Lit 5 min before
Rays do not shine on others
FTM :
No special preparation
Plinth is in correct position below the center of the lamp

## Slide 17: Preparation of patient
Hypersensitive to sunlight?
Taking sensitizer?
Explanation of procedure and erythema reaction( after 4 – 12 hrs)
A test dose should precede the treatment
Large area to be exposed, so wear slip
Same area should expose on each occasions
Operators and patients eyes must be protected

## Slide 18: Arrangement of lamp and patient
IF CENTROSOL LAMP IS USED
circle is painted on floor with 1m radius
Patients sit on chairs around lamp
Patient is seated so that arc is opposite to the middle of the body.
Lamp must be turned on 5 min before

## Slide 19
IF GROUP MODEL OF FLUORESCENT TUBES IS USED
Circle arrangements like centrosol
Ideally patients should be treated in standing
So that full use of 4 feet tube can be made
But it is uncomfortable for pt
No warm up time is required

## Slide 20
IF AIR COOLED MERCURY VAPOUR LAMP IS USED
Pt position: oblique side lying(fully supported)
Position of lamp: rays strike at right angle( arc tube at the center of the body)
Distance between patient and burner must be measure accurately
TUNNEL MODEL OF FLUORESCENT TUBE IS USED
Patient lies either prone or supine
Lamp is 45cm above the patient
Pt is warned not to move from position or touch the lamps

## Slide 21: The treatment
Lamps are turned on or uncovered
Time is kept accurately
Group therapy, each pt different time, so make the list of name and time
Inform the pt when to turn(exposure of other part) and when to come away
Flourescent model and mercury vapour lamp repositioning of patient must be supervised
Monitor position of the patient
Sitting must be upright
Pt do not remove their goggles or shade
At the end of treatment lamp are switched off or removed

## Slide 22: Records of treatment
Notes of
Date
Lamp used
Part exposed
Time of exposure
Distance of pt and lamp
Effects of rays(erythema reaction)
Other good or ill effectes

## Slide 23: dosage
For general irradiation goal is
1st degree erythema
Sub erythema dose___ old age, debility etc
Usually whole body is treated on each attendance
Better to treat posterior first then anterior
Fractional method is better to adopt
Body is divided into four or six parts
Especially esophylactic effects

## Slide 24: Progression of dose

## Slide 25: Frequency of irradiation
1sr degree______ on alternate days
If fractional method is used ____ attend pt daily
Sub erythema dose can be applied daily

## Slide 26: Techniques for local irradiation

## Slide 27: Choice of lamp
Two lamps are commonly used are
Air cooled mercury vapour lamp
Kromayer lamp
Usually filters are used with these lamps

## Slide 28: Preparation of lamp
Mercury vapour lamp
lighted 5 min before
Karomayer lamp
water must be circulating before the arc is struck
lamp is cleaned with methylated ether

## Slide 29: Preparation of patient
Skin is washed with soap and water
Sometimes Special preparation is required
Liquid paraffin is used in some cases of psoriasis
Pt supported in comfortable position
Not move during the treatment
Part round the Area to be treated must be protected
Eyes must be protected with goggles
Pt education about the erythema reaction and any discomfort

## Slide 30: Arrangement of lamp and patient
Air cooled mercury vapour lamp
Position of lamp is such that rays strike at right angle to the skin
Distance ?
Kromayer lamp
May be used in contact or 5- 10 cm from the skin or with various applicators
Lamp is held by operator so both the operator and pt must be fully supported
Lamp may be supported on pillows
Rays at right angle
Maintain correct
Use of protected cap

## Slide 31: treatment
During contact therapy hold the lamp firmly and steady against the skin
The dose is timed accurately
At the end of treatment, remove the lamp
If intense reaction is expected, steps must be taken to protect the area
When fourth degree erythema is produced on some area, zinc and boric ointment should be applied on a piece of lint to protect the blister from irritation by rubbing of the clothes

## Slide 32: notes
As in general Rx
Diagram of the area

## Slide 33: dosage
Conditions?
Max Area for 3rd degree erythema is 250 cm2
Area for 4th degree erythema is 2.5 cm2
A wound can be treated with 4th as well as 5th degree erythema

## Slide 34: Progression of dose
Already discussed

## Slide 35: Special techniques

## Slide 36: Treatment of wounds
PREPARATION OF AREA
Wounds are cleaned in usual way
Crusts on septic wounds should be removed
Scab which may form on healing wound not be removed
After cleaning, surface must be dried
Skin around the wound must be protected
DOSE
4th or 5th degree erythema( infected and indolent wound)
The reason is to provoke strong inflammatory reaction, with subsequent liberation of growth hormone
Irradiation must be confined to the area to be treated

## Slide 37
AFTER THE IRRADIATION
Followed increased discharge
Blistering of the surrounding skin may occur care must be taken)
PROGRESSION OF DOSE
No need to increase the dose
Y?
IRRADIATION OF SORROUNDING SKIN
1st and 2nd degree erytheyma to surrounding skin
To increase blood supply and resistance against infection
Progression of dose is required to this area

## Slide 38
WHEN HEALING STRATS
1st n 2nd degree to increase blood supply and stimulate growth of epidermis
CARE
New epidermis___ petroleum jelly
HARMFUL EFFECTS
Abiotic rays
Use Filters, blue uvoil filter, cellophane or strile oil spray

## Slide 39: Treatment of cavities
INDICATIONS
Deep wounds, sinuses, other cavities
LAMP
Kromayer lamp with suitable quartz applicator
STERILISATION
DOSE

## Slide 40: Treatment with compression
Local UV irradiation with compression to eliminate the blood from area
Deeper penetration of rays
Rays of 3300A
Rx of lupus vulgaris, rays penetrate to site of lesion, which is in dermis
Convex quartz applicator with kromayer lamp

## Slide 41: Dangers and precautions

## Slide 42: conjuctivitis
Delayed onset
Symptoms :
pain, gritty feeling in eyes, photophobia, and lacrimation
Symptoms clear up in some days
No ill effects after one exposure
Rx :
Bath the eyes with boric acid
Drops of liquid paraffin and castor oil
In sever cases, wear dark glass or remain in dark room for two days
Precaution:
Protection with goggles etc

## Slide 43: overdose
Local symptoms:
Red, hot, extremely sore, blister formation
General symptoms:
Headache, vomiting, high temperature, collapse
Precautions:
Check pt hypersensitivity
Dose monitoring carefully
Care in progression of dose
Always the same area to be exposed
Warning to the pt about movement during treatment
Rx:
After overdose apply IR
Erythema of IR over UV erythema will diminishes the intensity of UV
Apply cold cream
If irritation is more apply calamine lotion

## Slide 44: Electric shock

## Slide 45: burns
Touching Hot part of lamp
Hot quartz
Burst of burner
Precaution:
Pt education

## Slide 46: chills
Usually from general treatment
Room is too cold
IR given in conjunction

## Slide 47: thanks