## Slide 2: CONTENTS
Dry milling of rice
Wet milling of rice
Wet milling of corns
Processing of oats
Malting and brewing
Breakfast cereals
Feed and industrial uses

## Slide 3: RHEOLOGY OF DOUGHS AND BATTERS
In baking and cereal science
Rheology is of particular interest. Dough is a viscoelastic material which behaves as both a liquid and a solid
It exhibits a viscous (fluid-like) and an elastic (solid-like) behavior when a force is applied to it
Elasticity, extensibility, viscosity and resistance to deformation are main parameters
Farinograph and extensograph are used to measure rheological properties of dough

## Slide 4: DRY MILLING OF RICE
Rice is best known as a lowland crop grown in flooded fields or paddies
Dry Processing Harvested rice grains are enclosed in glumes that are in close contact with the grain. Prior to consumption as grain, or further processing into flour, snack foods and beverages, the glumes are removed by hulling
Rice polisher is a machine for buffing (or "polishing") kernels of rice to change their appearance, taste, and texture or for transforming brown rice into white rice
Rice polishers are abrasive machines that use talc or some other very fine dust to buff the outer surface of rice kernels

## Slide 5: WET MILLING OF RICE
Parboiling is pre-cooking of rice in water prior to milling
Parboiled rice offers a number of advantages over and above untreated milled rice
Parboiling hardens grain and thereby decreases susceptibility to breakage during the de-husking process and damage by insect pests in store. In addition, it enhances the nutritional quality and value of rice by promoting movement of nutrients from the outer coverings (bran) and into the grain

## Slide 6: WET MILLING OF RICE
Grain to be soaked at a constant fixed temperature for a specific period of time to produce a consistently high quality product of a type required by local consumers • Soaked grains to be steamed for the allotted time • Final grain drying to a moisture content of 12-14 per cent w/w to stop any growth of fungi (mould) and bacteria and to facilitate trouble free de-husking. • From de-husking onwards, it is polished and stored in bags

## Slide 7: WET MILLING OF CORN
Corn wet-milling is a process of breaking corn kernels into their component parts: corn oil, protein, corn starch, and fiber. It uses water and a series of steps to separate the parts to be used for various products

## Slide 8: WET MILLING OF CORN
It consist of following steps
Cleaning
Steeping
Germ recovery
Fiber recovery
Gluten recovery
Starch processing
Co-product manufacturing

## Slide 9: PROCESSING OF OATS
Oats have numerous uses in foods; most commonly, they are rolled or crushed into oatmeal, or ground into fine oat flour
Oatmeal is chiefly eaten as porridge
may also be used in a variety of baked goods
such as oatcakes, oatmeal cookies and oat bread

## Slide 10: PROCESSING OF OATS

## Slide 11: PROCESSING OF OATS
Oats processing is a relatively simple process
Cleaning and sizing
Upon delivery to the milling plant, chaff, rocks, metal, oversized materials and foreign grains are removed from the oats
then they are separated by width and length into different classifications before de-hulling

## Slide 12: PROCESSING OF OATS
Dehulling
Centrifugal acceleration is used to separate the outer hull from the inner oat groat
The lighter oat hulls are then aspirated away, while the denser oat groats are taken to the next step of processing
Kilning
The unsized oat groats pass through a heat and moisture treatment to balance moisture for optimal storage conditions and to deactivate self catalysing enzyme activity

## Slide 13: PROCESSING OF OATS
Final processing
Three methods are used to make the finished product
Flaking to obtain oats flake
Bran milling to separate bran from endosperm
Whole flour milling to get flour

## Slide 14: MALTING AND BREWING
Malt is germinated cereal grain that has been dried in a process known as "malting". The grain is made to germinate by soaking in water and is then halted from germinating further by drying with hot air
Malting grain develops the enzymes (α-amylase, β-amylase) required for modifying the grains' starches into various types of sugar
It also develops other enzymes, such as proteases, that break down the proteins in the grain into forms that can be used by yeast
Malted grain is used to make beer, whisky, flavored drinks such as Horlicks, Ovaltine, and Milo, and some baked goods, such as rich tea biscuits

## Slide 15: BREAKFAST CEREALS
Wholewheat cereal biscuits
Shredded wholegrain pillows
Porridge oats/barley
Corn flakes
Museli

## Slide 16: SNACKS FROM CEREALS
Popcorn
Granula bars
Oats caramel bites
Muffins
Energy bites

## Slide 17: SNACKS FROM CEREALS

## Slide 18: INDUSTRIAL USES OF CEREALS
Human consumption
Animal feed
Biofuel