## Slide 1: Walking Aids
Dr Atif Malik

## Slide 2: Mobility aids
A mobility aid is a device designed to assist walking
It also improve the mobility of people with a mobility impairment.

## Slide 3: Walking aids
Walking aids include
Assistive canes
Walking sticks
Crutches
Walkers / frame
Wheel chair
Elbow crutch
Axillary crutch

## Slide 4: Walking aids

## Slide 5: Walking aids
Walking aids are useful to assist people who have difficulty in walking or people who cannot walk independently.
These devices help to maintain upright ambulation by providing the following function:
Improved stability
Reduced lower-limb loading
Generating movement.

## Slide 6: Crutches
These are used to reduce weight bearing on one or both legs
Also give support where balance is impaired and strength is inadequate.

## Slide 7: Types of crutches
Axilary crutch
Elbow crutch
Forearm/ gutter crutch

## Slide 8: Axillary crutch
They are made of wood with
An axillary pad
A hand piece
A rubber ferrule.
The position of the hand piece and the total length are usually adjustable.

## Slide 9: Axillary crutch
The axillary pad should rest beneath the apex of axilla
Hand grip in slight flexion when weight is not being taken.
When weight is being taken through axillary pad, the elbow will go into extension and weight is transmitted down the arm to hand piece

## Slide 10: Axillary crutch

## Slide 11: Elbow crutches
They are made of
Metal
A plastic forearm band.
Rubber ferrule
They are usually adjustable in length by means of a press clip or metal button

## Slide 12: Elbow crutch
These crutches are suitable for patients with good balance and strong arms.
Weight is transmitted exactly the same way as for axillary crutches.

## Slide 13: Elbow crutch

## Slide 14: Forearm crutches
Also called gutter crutches
They are made of
Metal
With a padded forearm support
Strap
An adjustable hand piece
A rubber ferrule

## Slide 15: Gutter crutch

## Slide 16: Gutter/forearm crutch
These are used for patients with rheumatoid disease for providing support.
They cannot take weight through
Hands
Wrists
Elbows
Deformity
Pain

## Slide 17: Preparation for crutch walking
Arms:Shoulder extensors
Adductors
Elbow extensors
All are must be assessed and strengthened before the patient starts walking.
The hand grip must also be tested to see that the patient has sufficient power and mobility to grasp hand piece.

## Slide 18: Preparation for crutch walking
Legs: the strength and mobility of both legs should be assessed and strengthened
Main attention to the
Hip abductors
Hip extensor
Knee extensors
Plantar flexors

## Slide 19: Preparation for crutch walking
Balance:
Sitting and standing balance must be tested.
Demonstration:
The physiotherapist should demonstrate appropriate crutch walking to the patient.

## Slide 20: Crutch walking
During first time, when the patient is to stand and walk, the physiotherapist should have an assistant for supporting the patient.

## Slide 21: Non-weight bearing
Patient should always stand with a triangular base i.e.
Crutches either in front or behind the weight bearing leg

## Slide 22: Non-weight bearing

## Slide 23: Partial weight bearing
The crutches and the affected leg are taken forward and put down together.
Weight is then taken through the crutches and the affected leg, while the unaffected leg is brought through.

## Slide 24: Partial weight bearing

## Slide 25: Sticks
Sticks may be made up of either
Wood
Metal
Curved
Straight
Metal ores are adjustable while the
wooden ones are non-adjustable.

## Slide 26: Sticks
Uses:
Sticks allow more weight to be taken through the leg than crutches.
One stick may be used on the unaffected side
The stick and affected leg are placed forward together
Taking some of the weight through the stick

## Slide 27: Sticks

## Slide 28: Tripod or quadripod
Metal sticks with three or four prolonged bases
It gives more stable support than stick

## Slide 29: Tripod or quadripod

## Slide 30: Frames/ walker
They are light weight with four feet which can be adjustable in height.
Patient lifts the frame forward then leans on it and takes steps.
The patient should take even steps, keeping the frame forward.
Rotator frames which can be pushed or reciprocal frame
where each side moves independently are useful for ataxic patients.

## Slide 31: Walker

## Slide 32: Walking aids

## Slide 33: Tripods