## Slide 1: Carbon Dioxide
Processing of Carbon Dioxide

## Slide 2: Contents
Carbon Dioxide
Properties
Dry Ice
Sources of CO2
Introduction to Carbon Capture and Storage(CCS)
CO2 Transportation
CO2 Capturing Technologies
CO2 Storing
Advantages
Disadvantages

## Slide 3: Carbon Dioxide
Carbon Dioxide is natural gas
It is present in air at very low level 0.03% by volume
It vital substance to plant kingdom for the process of photosynthesis
Carbon Dioxide can exist in three forms:
Gas
Solid (dry ice)
Liquid (under certain pressure level)
O
O
C

## Slide 6: Properties
Non-toxic, colorless and odorless gas that does not impart any flavor to the beverage
Nonflammable and no fire hazards when handling
Soluble in water and dissolves easily in the beverages
Its solubility can be controlled by regulating the temperature and pressure
In water , it forms a weak acid(carbonic acid)
The carbonic acid can retard the growth of microorganisms
Carbonic acid easily releases Co2 gas to create effervescence

## Slide 7: Dry Ice
Dry ice is the solid form of carbon dioxide
It is used primarily as a cooling agent
Its temperature is lower than water ice
It is useful for preserving frozen foods where mechanical cooling is unavailable

## Slide 8: Sources of CO2
By burning of carbonaceous materials
C + O2 CO2
In the production of H2 by steam reforming of methane or other hydrocarbons, 16% pure Co2 is obtain
CH4 + 2H2O CO2 + 4H2
In manufacture of alcohol (ethanol) by the fermentation process 99.9 % pure CO2 is obtained
C6H12O6 C2H5OH + CO2
In calcinations of CaCo3 at 1000°C ,40% Co2 is obtained
CaCo3 CaO + Co2

## Slide 9
CO2 Capturing & Storing process

## Slide 10: Carbon Capture & Storage Technology
“A Technology that can capture 90% of the Carbon Dioxide Emission and Prevent Co2 from entering the Atmosphere”
The CCS chain consist of three parts
Capturing
Transportation
Storage

## Slide 11: Capturing Carbon Dioxide
Capturing of Co2 by
Pre Combustion Technology
Post Combustion Technology
Oxy Fuel Process

## Slide 12: Pre Combustion Technology
Removing CO2 before combustion
By Gasifying the coal through the reaction with oxygen(O2)
It is possible to obtain a mixture of mostly CO2 & H2
CO2 is captured and H2 is use as fuel

## Slide 13: Post Combustion Technology
Removing CO2 after combustion
Applicable to fossil fuel burning power plants that release fuel gas
Reacting the fuel gas with chemicals that absorb CO2 and then heat the chemicals to release CO2
Fuel Gas “Mixture of Nitrogen , water vapor , 15% CO2

## Slide 14: Oxy Fuel Process
The Fuel is burnt in oxygen(O2) instead of air
The resultant flue gas is condensed through cooling
Resultant is an pure CO2 stream

## Slide 15: Overview of CO2 Capture

## Slide 16: Transport of CO2
CO2 is transported in three states:
Gas
Liquid
Solid
Transportation system used:
Pipeline Transportation system
Marine Transportation system

## Slide 17: Pipeline Transportation system

## Slide 18: Marine Transportation system

## Slide 19: Storage options
Geological storage
Oceanic storage
Mineral storage

## Slide 20: Geological storage
Storing carbon dioxide under earth's surface is called geo-sequestration
Injecting CO2 into:
Underground geological formations
Oil fields
Saline formations

## Slide 22: Oceanic storage
Dissolving CO2 at mid depths
Injecting CO2 at depths exceeding 3km where it would form lakes of liquid CO2
Below 3km where depth
Liquid CO2 will be denser than sea water and will sink to the ocean floor

## Slide 23: Mineral Storage
CO2 is reacted with mineral to form Carbonates

## Slide 24: Purification of CO2
The purification CO2 consist on two methods:
Cryogenic separation
Distillation

## Slide 25: Cryogenic separation
Cryogenic separation method, the liquefaction temperature increases by improving the initial pressure of the mixed gases
The separation ratio could also be maintained at a high level by multi-stage separation and compression

## Slide 26: Distillation
In the distillation subsystem, crude product is distillated under high pressure and near ambient temperature conditions

## Slide 27: MAJOR STORAGE SITES IN THE WORLD
Sleipner, Norwegian North Sea
Altmark, Germany
Weyburn, Canada
In Salah, Algeria
Miranga, Brazil
Hontomin, Spain
Hastings, Texas, USA

## Slide 28: Advantages
Reduces pollution
Reduces changes in atmospheric temperature
Enhanced oil recovery

## Slide 29: Disadvantages
Leakage problems may occur
Costly process
Damage pipelines
Oceanic Acidification

## Slide 30: Conclusion
CCS involves capturing millions of tones of CO2 a year from gas or coal
Valuable tool in the fight against climatic change

## Slide 31: Uses of CO2
Carbon dioxide is a food additive used as a propellant and acidity regulator in the food industry
It is approved for usage in the EU, USA, Australia and New Zealand
Food

## Slide 32: Baking
Leavening agents cause dough to rise by producing carbon dioxide
yeast produces carbon dioxide by fermentation of sugars within the dough, while chemical leaveners such as baking powder and baking soda release carbon dioxide when heated or if exposed to acids

## Slide 33: Beverages Carbonation
Carbon dioxide is used to produce carbonated soft drinks and soda water
Traditionally, the carbonation in beer and sparkling wine came about through natural fermentation, but many manufacturers carbonate these drinks with carbon dioxide recovered from the fermentation process
In the case of bottled and kegged beer, the most common method used is carbonation with recycled carbon dioxide

## Slide 34
Carbonated Beverages

## Slide 35: Wine Making
CO2 is used as a seal gas to prevent oxidation of the wine during maturation
The main advantage of using dry ice over regular water ice is that,
It cools the grapes without adding any additional water that may decrease the sugar concentration in the grape
Therefore also decrease the alcohol concentration in the finished wine.

## Slide 36: Cont...
CO2 is also produced during the fermentation process
It is already captured on-site for reuse for its inert gas properties

## Slide 37: Coffee Decaffeination
Supercritical CO2 is used as the solvent for decaffeinating coffee
It is preferred due to its inert and non-toxic properties.

## Slide 38: Welding & Metal Fabrication
Carbon dioxide is most often mixed with argon as a shielding gas
Used to prevent atmospheric contamination of molten metal in electric arc welding processes

## Slide 39: Fire Extinguisher
Carbon dioxide extinguishes flame
Some fire extinguishers, especially those designed for electrical fires, contain liquid carbon dioxide under pressure

## Slide 40: Food processing, preservation and packaging
CO2 is used for various applications in the food industry
Carbon dioxide is commonly used in MAP and CAP because of its ability to inhibit growth of bacteria that cause spoilage
In packaging applications, CO2 is used in MAP&CAP with products such as cheese, poultry, snacks, produce and red meat etc.
Including cooling while grinding powders such as spices and as an inert atmosphere to prevent food spoilage

## Slide 41: Supercritical CO2 as solvent
Liquid carbon dioxide is a good solvent for many lipophilic organic compounds
It is used to remove caffeine from coffee
Other chemical processing industries as a less toxic alternative to more traditional solvents such as oraganochlorides

## Slide 42: Pulp and paper processing
CO2 is used to reduce pH during pulp washing operations.

## Slide 43: Pharmaceutical
Use of CO2 in the pharmaceutical industry typically includes
Inerting
Chemical synthesis
Supercritical fluid extraction
Product transportation at low temperature
Acidification of wastewater

## Slide 44: Enhanced oil recovery (EOR)
Co2 is injected into depleted oil fields
The CO2 acts as a solvent that reduces the viscosity of the oil, enabling it to flow to the production well
Once production is complete, the CO2 can potentially be permanently stored in the reservoir

## Slide 45: Horticulture
CO2 is provided to greenhouses to maintain optimal Co2 concentration and maximize plant growth rate
Sources include on-site cogeneration schemes as well as off-site industrial sources connected via pipeline networks