## Slide 1: Precooling and its Advantages
Prof. Dr. Sarfraz Hussain

## Slide 2: Pre-cooling
It is the first step in good temperature management. The field heat of a freshly harvested crop(heat the product holds from the sun and ambient temperature) is usually high
It should be removed as quickly as possible before shipping, processing, or storage.
Refrigerated trucks are not designed to cool fresh commodities but only maintain the temperature of pre-cooled

## Slide 3: CONTINUED
The rapid pre-cooling to the product’s lowest safe temperature is most critical for crops with inherently high respiration rates.
These include artichokes, brussels sprouts, cut flowers, green onions, snap beans, asparagus, broccoli, mushrooms, peas, and sweet corn.
Crops with low respiration rates include nuts, apples, grapes, garlic, onions, potatoes (mature), and sweet potatoes

## Slide 4: Methods of Pre-cooling
Pre-cooling can be accomplished by simply blowing cold ambient air over the produce,
Refrigeration is required for ensuring short cooling time that is so critical in preventing the loss of quality.
Cooling rates depend on the type of product, its size, weight, and the surface-to-volume ratio.
A small sized product with a large surface area-to-volume ratio cools at a faster rate.

## Slide 5
Cooling rates are often expressed in several half-cooling times and can be used for comparing and predicting the effectiveness of different cooling methods for a given cooling time interval irrespective of the temperature of the produce or cooling medium used.
Half-time is the time required to reduce the temperature difference between the product and the cooling medium by one half.

## Slide 6: 1. Room cooling
This method involves using cold air as a medium to extract heat from the produce.
Air is cooled by a refrigeration system.
For efficient heat removal, the produce container should be well vented and stacked so that the container surface is in contact with cold air and the storage space is utilized to the maximum extent.
Since the rate of heat removal by still air is slow,

## Slide 7: Continued. . .
it takes longer to cool a produce to a safe transit or storage temperature.
High relative humidity (90%–95%) is maintained in the air to avoid desiccation and weight loss during cooling. The method is not recommended for produce packed in bulk.

## Slide 8: 2. Forced air or pressure cooling
This is a modification of room cooling where cold air is forced through the produce containers and around the produce to speed up cooling.
Fans specially positioned in the room create the pressure differential to circulate air.
Cooling time depends on the speed of the airflow, provided sufficient refrigeration capacity is available for a given duty.
The problems of moisture condensation on the produce, package, and the wall are eliminated due to air movement.

## Slide 9: Continued . . .
Cooling times can be significantly reduced and cooling accomplished in 10–25% less time compared to room cooling.
Forced air cooling is accomplished by using three systems:
A cold wall,
forced air tunnel,
serpentine cooling.

## Slide 10: 3. Package icing
This method of cooling involves keeping a finely crushed, flaked ice, and ice–water mixture in direct contact with the produce for cooling and maintaining low temperatures during short-time storage, transit, and display in superstores.
The latent heat of melting of ice (334 kJ/kg) provides the cooling effect.
The use is limited for products that can tolerate both weight of the ice and water that wets the product and the package.

## Slide 11: Continued. . .
Use of ice slurry is recommended to avoid mechanical damage due to sharp-end ice.
It is commonly used for cooling spinach and broccoli during transport and retail displays.

## Slide 12: Vegetables that can be iced
Asparagus
Beets
Broccoli
Carrots
Cauliflower
Green onions
Leafy greens
Radishes
Spinach
Sweet corn
Watermelon

## Slide 13: These items are damaged by direct contact with ice
Strawberries
Blueberries
Raspberries
Tomatoes
Squash
Green beans
Cucumbers
Garlic
Okra
Bulb onions
Romaine lettuce
Herbs

## Slide 14: 4. Hydro-cooling
Hydro-cooling is a rapid way to cool large batches of product by spraying or flooding the commodity with near-freezing water (~0°C).
Water, being liquid, is a superior heat transfer medium than air due to its large heat capacity.
Near-freezing water cools the product about 15 times faster than air, allowing for greater harvesting and marketing flexibility.

## Slide 15: Continued. . .
There is no desiccation of the product. However, water may be a source of contamination if soil and debris picked up during cooling are not removed before recycling.
Water needs to be appropriately filtered and disinfected. Chlorination is the most commonly used method to control infections.