## Slide 1: Analytical Geochemistry and related techniques
The purposes of the analytical geochemistry are to find the distribution of elements as well as their origin and evolution of the solar system including the Earth, the Moon, other planets.

## Slide 2
We have ﬁve strategies in analytical geochemistry:
(i) major element geochemistry
(ii) trace element geochemistry
(iii) determination of mass fractionation
(iv) age dating
(v) radiogenic isotopes for geochemical tracers

## Slide 3
X-ray detector
Polished sample
Characteristic X-ray
Secondary electron detector
Electron beam
Electron gun
Vacuum pump
Lenses and
apertures
Electron lenses
Schematic diagram of the scanning electron microscope (SEM).

## Slide 7
The electron beam is produced at the top of the column, and the shape of the electron beam is reformed using electron lenses and apertures. Finally, the beam is projected onto the sample. The electron beam is scanned over a small area, and the secondary electrons, scattered electrons, and the characteristic X-rays are detected by electron detectors and an X-ray detector, respectively. A semiconductor detector is used for X-ray detection. This configuration is called the energy dispersive spectrometry(EDS).

## Slide 8
The merits of SEM-EDS are
(i) the spectra for all elements are recorded in one scan, so measurement time is very short
(ii) secondary and backscattering electron images are better than that of an electron probe micro analyzer (EPMA) because the detector positions are designed to collect these electrons
(iii) the price of SEM-EDS is one third to one fourth of that of EPMA.

## Slide 9
Detector
x
–
y
stage
Polished sample
Electron beam
Electron lenses
Characteristic X-ray
Diffracting crystal
Electron gun
Vacuum pump
Schematic diagram of electron probe micro analyzer (EPMA).

## Slide 10
The electron gun, lenses, apertures are almost the same as those of SEM. The difference is in the collection and determination of characteristic X-rays. Characteristic X-rays emitted from the sample are diffracted by the crystals and collected by X-ray detectors. The position and material of the diffracting crystals are changed according to the wavelengths of characteristic X-rays of the target elements. This is called the wave length dispersive spectrometry (WDS). Five sets of diffracting crystals are maximally placed, and 10 elements can be determined in two scans.