## Slide 1: Lecture Series Online (2020) Hydro-Geography MSC 4th + BS 8th Lecture# 2: Date: 17-03-2020 (Taswar Abbas)
Flood
Causes and Factors
Effects and its Impacts

## Slide 2
Causes of Floods
Rains
River overflow
Strong winds in coastal areas

## Slide 3
              Factors
Upslope factors:
Down slope factors
Coincidence
1. Upslope factors:
The amount, location, and timing of water reaching in a drainage channel from natural precipitation and controlled or uncontrolled reservoir releases determine the flow at downstream locations. Some precipitation evaporates, some slowly percolates through soil, some may be temporarily sequestered as snow or ice, and some may produce rapid runoff from surfaces including rock, pavement, roofs, and saturated or frozen ground. The fraction of incident precipitation promptly reaching a drainage channel has been observed from nil for light rain on dry level ground to as high as 170 percent for warm rain on accumulated snow.
Most precipitation records are based on a measured depth of water received within a fixed time interval. Frequency of a precipitation threshold of interest may be determined from the number of measurements exceeding that threshold value within the total time period for which observations are available.

## Slide 4
Individual data points are converted to intensity by dividing each measured depth by the period of time between observations. This intensity will be less than the actual peak intensity if the duration of the rainfall event was less than the fixed time interval for which measurements are reported.
Convective precipitation events (thunderstorms) tend to produce shorter duration storm events than orographic precipitation. Duration, intensity, and frequency of rainfall events are important to flood prediction. Short duration precipitation is more significant to flooding within small drainage basins.
The most important upslope factor in determining flood magnitude is the land area of the watershed upstream of the area of interest. Rainfall intensity is the second most important factor for watersheds of less than approximately 30 square miles or 80 square kilometers. The main channel slope is the second most important factor for larger watersheds.
Channel slope and rainfall intensity become the third most important factors for small and large watersheds, respectively.

## Slide 5
2. Down Slope Factors
Water flowing downhill ultimately encounters downstream conditions slowing movement. The final limitation in coastal flooding lands is often the ocean or some coastal flooding bars which form natural lakes. In flooding low lands, elevation changes such as tidal fluctuations are significant determinants of coastal and estuarine flooding. Less predictable events like tsunamis and storm surges may also cause elevation changes in large bodies of water. Elevation of flowing water is controlled by the geometry of the flow channel and, especially, by depth of channel, speed of flow and amount of sediments in it. Flow channel restrictions like bridges and canyons tend to control water elevation above the restriction. The actual control point for any given reach of the drainage may change with changing water elevation, so a closer point may control for lower water levels until a more distant point controls at higher water levels.
Effective flood channel geometry may be changed by growth of vegetation, accumulation of ice or debris, or construction of bridges, buildings, or levees within the flood channel.

## Slide 6
3. Coincidence
Extreme flood events often result from coincidence such as unusually intense, warm rainfall melting heavy snow pack, producing channel obstructions from floating ice, and releasing small impoundments like beaver dams. Coincident events may cause extensive flooding to be more frequent than anticipated from simplistic statistical prediction models considering only precipitation runoff flowing within unobstructed drainage channels. Debris modification of channel geometry is common when heavy flows move uprooted woody vegetation and flood-damaged structures and vehicles, including boats and railway equipment. Recent field measurements during the 2010–11 Queensland floods showed that any criterion solely based upon the flow velocity, water depth or specific momentum cannot account for the hazards caused by velocity and water depth fluctuations. These considerations ignore further the risks associated with large debris entrained by the flow motion.

## Slide 7
            Effects
Primary effects
The primary effects of flooding include loss of life and damage to buildings and other structures, including bridges, sewerage systems, roadways, and canals.
Floods also frequently damage power transmission and sometimes power generation, which then has knock-on effects caused by the loss of power. This includes loss of drinking water treatment and water supply, which may result in loss of drinking water or severe water contamination. It may also cause the loss of sewage disposal facilities. Lack of clean water combined with human sewage in the flood waters raises the risk of waterborne diseases, which can include typhoid, cryptosporidium, cholera and many other diseases depending upon the location of the flood.
Damage to roads and transport infrastructure may make it difficult to mobilize aid to those affected or to provide emergency health treatment.

## Slide 8
2. Secondary and long-term effects
Economic hardship due to a temporary decline in tourism, rebuilding costs, or food shortages leading to price increases is a common after-effect of severe flooding. The impact on those affected may cause psychological damage to those affected, in particular where deaths, serious injuries and loss of property occur.
Urban flooding can cause chronically wet houses, leading to the growth of indoor mold and resulting in adverse health effects, particularly respiratory symptoms. Urban flooding also has significant economic implications for affected neighborhoods. In the United States, industry experts estimate that wet basements can lower property values by 10–25 percent and are cited among the top reasons for not purchasing a home. According to the U.S. Federal Emergency Management Agency (FEMA), almost 40 percent of small businesses never reopen their doors following a flooding disaster. In the United States, insurance is available against flood damage to both homes and businesses.

## Slide 9
            Impact Of Floods
Environmental impact
Wildlife and Livestock Health and Well-being
Riverbank and Sedimentation
Dispersal Of Nutrients And Pollution
Replenishment Of Surface And Groundwater
Local Landscape And Habitat

## Slide 10
              Environmental Impact
It effects the :
the health and wellbeing of wildlife and livestock
riverbank erosion and sedimentation
the dispersal of nutrients and pollutants
surface and groundwater supplies
and local landscapes and habitats

## Slide 11
Wildlife and Livestock Health and Well-being
livestock unable to relocate to higher ground in time were washed away by flood waters or forced to stand in polluted water until rescued.
Flood reduce the level of biodiversity, habitat potential and food present in the ecosystem, creating long-term impacts for surviving wildlife.

## Slide 12
Wildlife and Livestock Health and Well-being
livestock unable to relocate to higher ground in time were washed away by flood waters or forced to stand in polluted water until rescued.
Flood reduce the level of biodiversity, habitat potential and food present in the ecosystem, creating long-term impacts for surviving wildlife.

## Slide 13
      Riverbank and Sedimentation
Riverbank erosion is caused by high and fast moving water that exceeds riverbanks.
Flood waters can carry large amounts of sediment and leave deposits behind once flood waters recede.
Dispersal Of Nutrients And Pollution
•Flood water can contain debris, pollutants and nutrients.
•Pollutants in flood water, such as bacteria and pesticides, can be carried far distances. •Sedimentation and turbidity can result in the growth of algae and phytoplankton blooms that jeopardize water quality.

## Slide 14
      Riverbank and Sedimentation
Riverbank erosion is caused by high and fast moving water that exceeds riverbanks.
Flood waters can carry large amounts of sediment and leave deposits behind once flood waters recede.
Dispersal Of Nutrients And Pollution
•Flood water can contain debris, pollutants and nutrients.
•Pollutants in flood water, such as bacteria and pesticides, can be carried far distances. •Sedimentation and turbidity can result in the growth of algae and phytoplankton blooms that jeopardize water quality.

## Slide 15
Replenishment Of Surface And Groundwater
•One of the positive direct benefits of flooding is the replenishment of surface water and groundwater supplies.
•The replenishment of supplies can benefit soil, resulting in healthy crops and pastures.
Local Landscape And Habitat
•In urban areas, flooding can be extremely damaging and costly, as it can negatively impact infrastructure, homes and businesses. In the natural environment.
•Flooding has a more positive impact on the natural environment as flood water provides nourishment to the landscape.
THANK YOU.