## Slide 1: Controlled Atmospheric Storage
Prof. Dr. Sarfraz Hussain
FST 508

## Slide 2: Contents
What is CAS
Technical aspects
Advantages
Disadvantages
Conclusion
Reference

## Slide 3: CAS
It is storage of horticultural commodities under controlled o2 and co2 in the surrounding at its best suited temperature
O2 5% co2 1% for fruit and vegetables preservation
In general the o2 levels are reduced and co2 levels are raised for fruit preservation
Temperature differ for every fruit and vegetable

## Slide 4: Continued . .
Gas composition depends upon
Amount of product
Respiration Rate
Exchange rate between storage room and surroundings, storage room.

## Slide 5: Difference b/w CA and MA Storage
CA Storage
High degree of control over gas concentration
Longer storage life
More expensive technology
Atmosphere is modified by gas adding
Specific temperature should be maintained
MA Storage
Low degree
Less storage life
Less expensive
It is created by either actively(removing or adding gas) or passively (produce generated)
May or may be maintained

## Slide 6: Technical aspects
Exchange of gasses takes places
By ventilation or leakage
Diffusion through Permeable membrane
Air flow channels
Atmospehric composition remains constant for several weeks without any changes and it is insensitive to changes in barometric pressure

## Slide 7: Continued . . .
And cyclic fluctuations in the temperature in the storage room
In sufficient air tight rooms exchange can be achieved by fiber filled channels of varying cross sectional area
connecting the room with the vessel containing CO2

## Slide 9: Advantages
Retards the senescence and further deterioration of the fruits
Quality retains of fruit quality
Shelf life increases
Ripening is delayed as the ethylene scrubbed from the storage air
The shelf life of banana is four to six weeks at ambient temperature under CA conditions

## Slide 10: Continued.. .
Control over insects, pathogens and some physiological disorders
Little or no chemical preservatives are required
Aesthetic appeal increases

## Slide 11: Disadvantages
It is quite expensive
Temperature control is required
Gas compositions are different for every product
Special equipment and operator trainings are required
Once any leakage occurs the benefits are lost.

## Slide 12: Conclusion
Controlled or modified storage and packaging should be used as a supplement and not as a substitute so on first hand the maintenance of proper temperature and humidity is important.

## Slide 13: References
Thompson, A.K. 1988. Controlled Atmosphere Storage of Fruits and Vegetables, CAB International, UK.
Gormely, T.R., 1985, Chilled Foods, the state of the art, Elsevier App. Sci., London, New York.