## Slide 1: Heat Treatments
Prof. Dr. Sarfraz Hussain
FST 508

## Slide 2: Heat Treatments
The method of heating fruit to kill insect eggs and larvae as a quarantine treatment before fresh market shipment with diping in water and air saturated with water vapor (humidified by injection of steam) at temperatures of 40–50°C for 20 minutes. Vapor heat was developed specifically for insect control

## Slide 3: Hot Water Dipping
Hot water dipping (HWD) is the simplest heat treatment. There are three basic HWD systems
Batch system
Continuous system
Drainage system

## Slide 4
Application of HWT at 50°C for 20 min reduced crown rot severity caused by Colletotrichum musae in banana fruits by 50% after 7 days and by 33% after 14 days
Longer exposure caused fruit injuries such as scalding and shriveling, and failure to soften
40 to 50 °C for 20 minutes

## Slide 5: Batch system
In the first of these, the fresh produce is dipped into the hot water immersion container, where it remains at the recommended temperature 40 to 50 °C for a pre- determined length of time (20 minutes) before being taken out

## Slide 6: Advantages
This is very simple method with initial low cost
Simple heating source and a thermometer is required
Manually controlled
Easy process
No specific technical staff is required
Disadvantages
Only feasible to treat small batches
It is ineffective to treat bulk quantities
It is time consuming
Water soaked appearance
Some of the natural wax is removed

## Slide 7: Continuous system
In this system, the freshly harvested produce, contained in a basket, is carried on a conveyor belt, which takes it slowly through the hot water container from one end to the other

## Slide 8: Drainage system
In the drainage system, the freshly harvested produce is moved along a stainless-steel roller conveyor onto which hot water is spraed from above and drained away.
The belt/conveyor speed is set to ensure that the fruits are submerged or wetted for the required length of time
All three systems are equipped with a pump and water circulation system and temperature sensors to ensure uniform water temperatures throughout the treatment process

## Slide 9: Advantages of drainage
Huge quantities are treated
Less time is consumed
It also helps to clean the surface of fruit and reduce m.o
We can also use disinfectants like hypochlorites
water is drained away and prevent contamination
This method ensure wash away concept

## Slide 10: Vapor heat treatment
It is a method of heating fruit with air saturated with water vapor (humidified by injection of steam) at temperatures of 40–50°C to kill insect eggs and larvae as a quarantine treatment before fresh market shipment. Vapor heat was developed specifically for insect control

## Slide 11: Advantages
It is highly technical procedure in which a boiler installation is essential
It requires high initial investment
Quality control system is required
Huge quantities of fruits can be treated continously
Also require specific staff
Less time consumption is involved due to high penetration power of steam vapours
Less damage and losses to fruit is observed
No water penetrates in the fruit is observed with vapor treatment
No water soaked water appearence

## Slide 12: Disadvantages
High cost maintenance
Technical staff is required
Higher initial investments
Any fluctuation in temperature may damage the fruit
Frequent maintenance is required