## Slide 1
Chapter 3
Thin film deposition techniques
Thin film deposition is a process in which we coat very thin layer of any required material on a substrate to form functional devices e.g,
In the data storage industry, to deposit magnetic thin films to make Hard Disk Drives (HDD’s)
In the semiconductor industry to deposit electronic materials e.g, semiconductor (Silicon etc) thin films to make Solar Cells.
In the aerospace industry to form thermal and chemical barrier coatings to protect surfaces against corrosive environments

## Slide 2
In optics to impart the desired reflective and transmissive properties to a substrate
And elsewhere in industry to modify surfaces to have a variety of desired properties.

## Slide 3
The deposition process can be broadly classified into :
Physical Vapor Deposition (PVD)
Chemical Vapor Deposition (CVD)
In PVD process material goes from a condensed (solid or liquid) phase to vapor phase and then back to thin film condensed phase.
This process can be carried out at lower deposition temperatures and without corrosive products, It may produce ultra pure thin films but deposition rates are typically lower.
At least extreme primary vacuum is usually required
Classification of thin film deposition process

## Slide 4
Schematic diagram of Physical Vapor Deposition (PVD)process

## Slide 5
In CVD process substrate is exposed to one or more volatile precursors, which react and/ or decompose on the pre-heated substrate surface to produce the desired thin film deposit.
In CVD, the film growth takes place at high temperatures, leading to the formation of corrosive gaseous products, and it may leave impurities in the film.
Schematic diagram of Chemical Vapor Deposition (CVD)process

## Slide 6
If thin film grows with same crystallogrphic orientation as that of substrate, that type of growth is called epitaxial growth and process is called epitaxy e.g
FCC(111) orientation thin film grown on FCC(111) orientation substrate. Or
FCC(100) orientation thin film grown on FCC(100) orientation substrate etc.
Epitaxial thin film growth

## Slide 8
The growth of epitaxial thin films during the initial stages is determined by the balance of the different surface free energies of deposited material and substrate atoms and follows one of the three well-known growth modes:
Frank-van der Merwe mode (Layer by layer growth)
Stranski-Krastanov mode (Layer plus island growth)
Volmer-Weber mode (Island growth)
Epitaxial thin film growth modes

## Slide 9
Schematic representation of three epitaxial growth modes

## Slide 10
Frank-van der Merwe mode
This growth mode is characterized by a layer by-layer deposition. Each monolayer start to grow after the completion of previous layer
The interaction between the atoms of the deposited material and the substrate is stronger than the mutual interaction of deposited material atoms.
This mode is favourable for materials with same lattice parameters or small lattice mismatch with the substrate.

## Slide 11
Stranski-Krastanov mode
This growth mode corresponds to the nucleation of 3D islands after a layer by layer growth of one or several monolayers.
However, at lower temperatures in non equilibrium conditions this is not the case. In this case some roughness so called “mounds" is created which can be overcome by tuning the temperature.
Volmer-Weber mode
This growth process corresponds to the formation of three dimensional (3D) islands growth.
The interaction between the atoms of deposited material and the
substrate is weaker than the mutual interaction of the deposited
material atoms.