## Slide 1: CAMERA OPERATIONS AND PICTURE COMPOSITION

## Slide 2: Working the Camcorder and EFP Camera
Some basic camera “don’ts”
There are some basic Don’ts on camera use and that should be obeyed
Don't leave camcorder unattended in a car in order to avoid the equipment suffering from excessive heat and to prevent theft
Don't leave camcorder left in wet or moist condition as the wet will cause wet tape and ruined drive motor in the VTR
Don't point the lens at the sun for long time since the magnifying lens (at the viewfinder) will collect the sun rays and melt the equipment
Don't leave camcorder batteries in hot place and avoid dropping the batteries as the batteries are sensitive to heat and shock
Don’t forget to put the camera lens cover and close the aperture to C (cap) position upon using it.

## Slide 3: Before the Shoot
Before starting, check all the equipment and make sure
connectors and cables are available
Make sure tripod, camera plate and the camera are in
balance
Check if the external microphone and camera microphone
work properly
Verify whether the portable camera lighting equipment is
working properly by turning on the light

## Slide 4: During the Shoot
There are some basic steps that will show how the handheld camcorder and ENG/ EFP camera are operated
a) Handheld camcorder operating techniques
Keep the camera in steady position in order to obtain steady pictures
Zoom out the camera when moving the camera because when the camera is in wide-angle position and great depth of field. It is very possible that the obtained image will be in focus
When taking the moving pictures, get in front of them and walk backward with zoom lens in wide-angle position
When pointing the camera sideways (to pan the camera) move your whole body instead of just moving your arms

## Slide 5
b) ENG/ EFP camera or camcorder operating techniques
Carry the camera on the right shoulder and put your right hand through the support strap on the zoom lens while your left hand operates the manual focus ring (or reverse the procedure if you are left handed)
Check the audio level before and during recording
If the automated white balance is absent from the camera, do the white balance before shooting or each time you encounter new lighting condition such as the switch after taking outside pictures under the sun to taking pictures inside the house
Put the camera into auto-iris mode when the camera is in normal condition (when the camera is free from having to reveal picture in extreme details)
Calibrate the zoom lens routinely in order to get good and in-focus pictures
To achieve continuity during postproduction editing, utilize the camera microphone when videotaping, or record in AGC (automatic gain control) when videotaping in quiet surrounding

## Slide 6: After the Shoot
After shooting, take care of all the equipment
Take the full videocassettes out of VTR, replace with the new one, and
label all cassettes
Put all switches into off mode after shooting or put it in standby
position if the camera is heading for next assignment
Cap the camera by closing the iris and snap on the lens cover
Tidy the microphone cable by tying it with string or shoelace
Put everything into boxes or bags and recharge all batteries upon
shooting
If camcorder get wet, dried out first before putting the camera back
into the case since moist may cause serious problems to ENG/ EFP
equipment
Check all portable lights before the next assignment.

## Slide 7: Working with the Studio Camera
The significant difference between operating ENG/ EFP camera and the studio camera is that studio camera is always mounted on camera support

## Slide 8: Before the Show
Put your headset, check the intercom system and make sure (at least) that you can hear the director, the technical director (TD) and the video operator
Check the camera position on its mounting equipment: unlock the pan-and-tilt mechanism on the camera mounting head and adjust the horizontal and vertical drag
Check the camera balance on mounting head: unlock the pedestal and check whether it is correctly counterweighted since a properly balanced camera can be put in any positions
Check the camera cable availability and prevent the cables from any interferences

## Slide 9
Check whether the camera can be uncapped from the camera control unit and whether the lens cap can be removed
Check if the zoom lens can work smoothly, or whether the zoom is dirty (if it is dirty blow/ clean it with a rubber bulb and a can of compressed air)
Check whether the focus control can be moved easily and smoothly
Calibrate (preset) the zoom lens
Check the teleprompter
Always lock the camera
Cap the camera if it will be unattended for a while.

## Slide 10: During the Show
Put on the headset and check the intercom connection with the director, technical director, and video operator
Position the camera (calibrate the zoom) and make sure the camera can stay focus over the entire zoom range
Set the camera focus on its sharpest position. We can use the object itself as the standard (for example the hair detail or the line of dress the object is wearing)
Set the lens at its wide-angle position (zoom out position) or approximately midpoint from the object. Avoid setting it into extreme wide-angle position
Make sure whether the camera pedestal is properly set
Determine the approximate reach of camera cable in order to avoid the annoying situation caused by the messy cable during the shooting session or ask the floor person to help you with the cable

## Slide 11
Pay high attention to other camera and other equipment (the floor monitor, scenery, properties, floor lights, rug, etc.)
Keep an eye on viewfinder
During rehearsal, coordinate with the floor manager or the director if the unusual production problems exist
Mark the critical camera positions on the studio floor with masking tape
Listen carefully to the instructions from the director to all camera operator in order to coordinate the shoots among camera and to avoid duplication of shots
Avoid unnecessary conversation over the intercom

## Slide 12: After the Show
Wait for the all clear signal before locking the camera
Ask the video engineer if it is allowed to cap the lens with the lens cap
Lock the camera mounting head and the pedestal and push the camera to a safe place in the studio. If it is not possible, set the parking brake for the camera instead of putting it in the middle of the studio
Twist the cable as neatly as possible