## Slide 1: Lighting for Television

## Slide 2
Some important definitions related to television lighting are:
BARN DOORS: Metal flaps attached to the front of a lighting instrument; used to control where the light falls on a scene.
DIFFUSER: Some type of a translucent material (wire mesh, frosted plastic, or spun-glass sheet) that diffuses and reduces the light intensity.
FLOOD LIGHT: Also known as soft light; the scattered, diffused, shadow less illumination that in nature comes from a cloudy overcast sky, and is reflected from rough surfaces of all kinds.
GELS: Colour gels (filters) can be placed over lights to enhance the colour of the light.

## Slide 3
INCIDENT LIGHT: Also known as direct lighting; what’s measured with a hand held light meter- that is, the amount of light falling on a subject. When measuring incident lighting, the light meter must be positioned next to the subject, pointed at the light sources.
LIGHTING PLOT: A plan that shows where each light will be placed on the set.
REFLECTED LIGHT: Measured with a handheld light meter or a camera’s built in meter; the light bouncing off a subject. In this situation, the meter is aimed directly at a subject.
SPOTLIGHTS: Spotlights are a directional or hard illumination that produces sharp shadows.

## Slide 4
THREE-POINT LIGHTING: Also known as photographic lighting and triangle lighting; use of two spotlights(key light and back light) and a flood light(fill) to illuminate the subject.
ZEBRA: Some video cameras include a zebra indicator in the view finder. The zebra allows camera operators to evaluate the exposure of the image in the viewfinder by showing all over-exposed segments of a scene with stripes.

## Slide 5: Goals of Lighting
Lighting in television is much more than just making things visible. It has to satisfy a number of objectives:
The lighting must be bright enough to enable all the television cameras to produce pictures of the highest quality. This is usually referred to as base lighting.
Lighting should convey to the viewer the time, mood, and atmosphere of the story.
Lighting must provide a consistent look, as chosen by the director. That means it must look consistent from each camera angle.
The lighting must fit in with the other components of the studio or location: scenery, camera placement, mic placement, and so on. Badly positioned lights can prevent the talent from reading the teleprompter, cause flares in a camera lens, result in shadows, spoil a skillfully designed setting, and degrade makeup.

## Slide 6
Good lighting creates a three dimensional illusion in a flat image. It provides an impression of solidity and depth in subjects and surroundings.
Lighting should lower the contrast ratio between the light and dark areas. By adding more light to the dark areas or dimming the extremely light areas, it is possible to get more detail in both areas.
Successful lighting guides the audience’s interests. It directs their attention toward important features, because the viewer’s eyes are generally attracted to the brightest area of the screen.
Lighting can create compositional opportunities for the camera.
Lighting is used to increase or reduce the picture’s depth of field.

## Slide 7: Why is lighting necessary?
Technical Reasons
The camera needs a certain amount of light reflected from the scene to be able to produce a good tonal range in the image. If there is too little light, the lens aperture has to be opened up to compensate, and the available depth of field is considerably reduced. When there is too much light, the images become overexposed , unless the lens is stopped down(the depth ma v now be too great) or a neutral densit v filter is used to reduce the light.
In the studio, excess light wastes power, causes ventilation problems, and is unpleasant to work in. Light levels need to be related, wherever possible, to the preferred working f-stop.

## Slide 8
The television camera can handle and reproduce only relatively limited tonal contrasts. If lighting is contrasty, details in the lightest and darkest tones will be lost.
On location, the existing lighting may not be suitable. From
the camera position, it may prove to be:
too bright: causing performers to squint their eyes.
too dim: insufficient for well exposed shots.
too flat: diffused light in which subjects lack form or definition.
too contrasty: lighter tones burned out (pure white) and shadows too black.
Under these conditions we need to augment or replace the natural lighting.

## Slide 9
2. Artistic Reason
Lighting plays a major part in how we interpret what we see. Even when structure and outline give us leading clues , the play of light and shade strongly influences our judgment of size, shape, distance, surface texture and contours.
Lighting is strongly associated with mood. Through carefully chosen light direction and contrast, you can change a scene’s entire atmosphere. lt can portray fun, fantasy, mystery, or dramatic tension. Lighting can enhance a setting and create pictorial beauty, or it can deliberately create a harsh, unattractive setting.

## Slide 10
You can use light selectively to emphasize certain aspects of the scene while subduing others, or avoiding or reducing distracting features. You can exaggerate form, and draw attention to texture or suppress it . Through shadow formations, lighting can suggest structures that do not exist, or hide what is there.

## Slide 11: The Nature of Light
Light can be washed across a scene, or used to pick out and emphasize certain features. To exercise this control over light lets look at the practical basics of illumination:
Light intensity: The strength of light that we require on the subject and the surroundings will determine how powerful the lamps need to be, relative to the area they have to cover.
Colour temperature: The colour quality of the light. Light and camera performance should be matched to avoid poor colour quality
Light dispersion: Some light sources produce hard light, which casts strong shadows; others create soft light, which is diffused and has few shadows.
Light direction: The direction of the light affects the way light and shade fall on a subject. It determines which features are highlighted, and which fall into shadow.

## Slide 12: Light Intensity
The amount of light needed to illuminate a set or location and the action within it is partly a technical decision and partly an artistic one, e.g. you may use one strong key light to cover both the action and the background, or a series of restricted lamps, each lighting a carefully chosen area.
In a set or location, light intensity depends mostly on the nature of the surroundings and the mood the director wants to create. To reveal detail in the walls of a dark-paneled room will require much more light than would be needed with light toned walls.
Lighting intensity is also influenced by surface finish; whether walls are smooth or rough textured, and whether they are plain or strongly contoured. The contrast range of set dressings used can also affect the amount of light needed to illuminate a situation effectively.
Lighting quality cannot be judged by the watts of the lights.

## Slide 13
The most helpful way to review the lighting is on an actual monitor, on which we can assess its artistic effect and judge its technical qualities.
When lighting under unfamiliar conditions, it is advisable to make careful measurements of light levels. There are two primary ways of measuring the lighting in a scene:
Incident light measurement helps to assess the relative intensities of lighting from various directions. When measuring incident lighting, the light meter must be positioned next to the subject, pointed at the light sources. It is measuring the amount of light that is falling on the subject, from the subject’s perspective.
Reflected light measurement provides a general indication of the amount of reflected light reaching the camera. Reflected light measurements average the amount of light reflected from the scene, arriving at the camera’s lens. The meter is aimed directly at the subject. Television cameras use reflected light metering.

## Slide 14: The Colour Quality of Light
We accept a very wide range of quite different light qualities as representing “white” light. If we analyze “white” light, we find that it is really a mixture of a range of colours. The spectrum is red, orange, yellow, green, blue, indigo, and violet light in similar proportions.
In many forms of illumination, some parts of the spectrum are much more prominent than others, and the result is far from true white. e.g. Light from candles or dimmed tungsten lamps actually has a warm yellowish-red colour quality; or a low colour temperature. Daylight can vary considerably, from cold, bluish sky light to the warm quality of light around sunset.
Our brains compensate and accept all these sources of
illumination as white light. Television cameras do not self-
compensate. If the lighting has bluish or reddish features, the
images will show this as pronounced colour cast.

## Slide 15
There are two ways to correct the colour when shooting:
Adjust the camera to compensate for the colour variations of
the prevailing light, by using a suitable colour correcting filter
(in the filter wheel) and/or by adjusting the white balance.
Adjust the colour temperature of the light to suit the camera’s colour balance. If you are using tungsten lights when shooting in daylight to illuminate shadows, blue filter material can be used to raise their colour temperature. Conversely ,if daylight is illuminating a room in which you are using quartz or tungsten lamps, a large sheet of amber orange filter can be stretched over the window to reduce the effective colour temperature of the daylight to match the interior lighting.
Cameras are usually balanced for the dominant light source in
the scene.

## Slide 16: Light Dispersion
FLOOD LIGHT: It is also known as soft light. It is scattered, diffused, shadow less illumination that in nature comes from a cloudy overcast sky, and is reflected from rough surfaces of all kinds (walls, sand, snow).
Soft lights are usually used to illuminate shadows without creating additional shadows. However, soft light does have practical disadvantages. Really diffused light can be difficult to control, because it spreads around and is not easy to restrict.
Badly used soft light can produce flat unmodelled illumination. Texture and form can be difficult to see in the picture. If used as an overall base light, it can reduce the impression of depth, over-light the walls of settings, destroy atmosphere, and produce flat, uninteresting pictures.

## Slide 17
SPOTLIGHTS: This is a directional or hard illumination that produces sharp shadows. This type of light comes from any concentrated light source, such as the sun or a spotlight.
Spotlights produce well defined shadows and are used to create well defined modeling, least pronounced shadows(e.g. Tree-branch shadows), articulate light to specific areas, produce harsh shading or an abrupt brightness fall-off , project light over some distance at a reasonably constant intensity. The light from focused spotlights does not “fall off” quickly with distance.
Spotlights are generally used as key lights, as backlights, as background /set lighting, and for effects (sunlight, broad decorative patterns). The light spread of the spotlight’s beam is adjustable and can be focused. A couple of types of spotlights include:

## Slide 18
Effects/pattern projectors: These spotlights, can project patterns on the set or scene to simulate windows, branches, and so on.
Follow spots: Used for isolating static subjects or following moving performers (singers, skaters, dancers) in a confined pool of light. These large spotlights are carefully balanced for continuous accurate handling and are usually mounted on a stand.
However, spotlights do have practical disadvantages:
The shadows from a spotlight may prove to be unattractive, inappropriate, or distracting.
Spotlights can over emphasize texture and surface modelling.
High contrast can produce harsh, unsubtle tones.
Multiple shadows arise when the subject is lit by more than one hard light source.

## Slide 19
For effective lighting treatment you need a suitable blend of spotlights and soft diffused lights. The spotlight reveals the subject’s contours and textures, and the soft light reduces undue contrast or harshness and makes shadow detail visible.

## Slide 20: Main Lighting Sources
Key Light: As a principle source of illumination, the major function of the key light is to reveal the basic shape of the subject. To achieve this the key light must produce some shadows. Because during the day we see the principle light source-the sun- coming from above, the key light is normally placed above and to the left or right side of the object, from the camera’s point of view.

## Slide 21
Back light: Adding illumination from behind helps separate the subject from the background. Besides providing spatial definition, the backlight adds sparkle and professional polish.
Try to position the backlight as directly behind the subject (opposite the camera) as possible; there is no inherent value in placing it somewhat to one side or the other unless it is in the camera’s view. A more critical problem is controlling the vertical angle at which the back light strikes the object. If it is positioned directly above the person (talent or presenter), or somewhere in that neighbourhood, the back light becomes an undesirable top light: instead or revealing the subject’s contour to make him/her stand out from the background and giving the hair sparkle, the light simply brightens the top of his/her head, causing dense shadows below the eyes and chin. On the other hand, if the backlight is positioned too low, it shines into the camera.

## Slide 22
Fill Light: Despite the use of back light on the performer , the difference between the light and shadow sides is still extreme, and the light side of the face still changes abruptly to a dense shadow. This change is called falloff. Falloff refers to the speed (degree) to which a light picture portion turns into shadow area. If the change is sudden, it is fast falloff. To slow down the falloff, that is to make the shadow less prominent and more transparent, you need some fill light.
The fill light is placed on the opposite side of the camera from the key light. A highly diffused floodlight or reflected light is generally used as a fill. The more fill light you use, the slower the falloff becomes. When the intensity of the fill light approaches or even matches that of the key light, the shadows, and with them the falloff, are virtually eliminated. This gives the subject a flat look-shadows no longer help define shape and texture.

## Slide 23: THREE POINT LIGHTING OR TRIANGLE LIGHTING
With the three main light sources(key, fill and back) you have
established the basic photographic lighting principle, also called triangle lighting.
However you must fine tune this lighting arrangement. Look at the lighted object or use the studio monitor to see whether the scene or presenter/host needs further adjustment for optimal lighting. Are there shadows still? Are there shadows that distort rather than reveal the face of the presenter? How is the light balance? Does the fill light wash out the necessary shadows, or are the shadows still too dense? Is the backlight too strong for the key/fill combination?

## Slide 24: Background or Set Light
To illuminate the background(walls or cyclorama) of the set or portions of the set that are not a direct part of the principle performance area, you use the background light, or the set light. To keep the shadows of the background on the same side as those of the person or object in front of it, the background light must strike the background from the same direction as the key light.
If the key light is placed on the camera right, causing the shadows of the subject to fall on the camera left side, then the background light should be placed on the camera right to make the shadows on the camera left to correspond with those of the foreground.
If you place the background light on the opposite side from the key, the viewer may assume that there are two separate light sources illuminating the scene.

## Slide 25
Side Light: Usually placed directly to the side of the subject, the side light can function as a key or fill light. When used as a key, it produces fast fall off, leaving the face in dense shadow. When used as a fill light, it lightens up the whole shadow side of the face. When you place the side lights on opposite sides of the person, the sides of the face are bright, with the front of the face remaining shadowed.
The side light becomes a major light source if the camera’s shooting arc is exceptionally wide. If, for instance, the camera moves around the subject from a 6 o’clock to an 8 o’clock position, the side light takes on a function of the key light and provides essential modeling (lighting for a three dimension effect).
For extra brilliant lighting, you can support the key light with side fill light. The fill light gives the key side of the subject basic illumination, with the key light providing the necessary sparkle and accent.

## Slide 26
Kicker Light: It is generally a sharply focused Fresnel spot. The kicker light strikes the subject from behind and on the opposite side of the camera from the key light (the fill light side). Its main purpose is to highlight the subject’s contour at a place where the key light fall off is the densest and where the dense shadow of the subject opposite the key lighted side tends to merge with dark background.
The function of the kicker is similar to that of the backlight except that the kicker “rims” the subject not at the top-back but at the lower side back. It usually strikes the subject from below eye level. Kicker lights are especially useful for creating the illusion of moonlight.

## Slide 27: Lighting Scenarios
These include:
High and low lighting
Flat lighting
Continuous action lighting
Large area lighting
High contrast lighting
Cameo lighting
Silhouette lighting
Chroma-key area lighting

## Slide 28
High and Low Key Lighting
A light background, a generous amount of light (high base-light IeveIs), and slow fall off usually constitute a high-key scene with an upbeat, happy mood. Situation comedies and game shows are much more brightly lighted(higher base light level and less contrast) than are mystery and police dramas (lower base light level and more contrast).
Selective, fast-fall off lighting with distinct shadows and
normally a dark background

## Slide 29
2. Flat Lighting
Flat lighting means you light for optimal visibility minimal shadows. Most flat lighting setups use floodlights (soft lights or fluorescent) for front lighting and background lighting and more focused instruments (Fresnel spots or small broads) for backlights. This setup is the favourite lighting technique for more or less permanently installed news sets and interview areas. The basic lighting triangle is preserved. In effect you have three key lights, or if you wish three fill lights, evenly illuminating the front area. The back lights add the sparkle and make the flatness of the lighting setup less noticeable. Additional background lights illuminate the set.
The major disadvantage of flat lighting is that it looks like what it is: flat.

## Slide 30
3. Continuous Action Lighting
When watching dramas or soap operas on television, notice that many of them have fast fall-off, low key lighting, which means prominent shadows and relatively dark backgrounds. In such multi-camera productions, the cameras look at a scene from different points of view, and people and cameras are always on the move.
In such situations, flat lighting can be used but then the lighting would not contribute to the mood of the scene or how viewers’ feel about the persons acting in it.
Fortunately, the basic lighting triangle of key, back and fill lights can be multiplied and overlapped for each set or performance area for continuous action lighting.
To compensate for the movement of the performers, you should illuminate all adjacent performance areas so that the basic triangle-lighted areas overlap.

## Slide 31
If you don’t have enough instruments to apply multiple-triangle lighting for several performance areas when lighting for continuous action, you must place the instruments so that each can serve two or more functions. In reverse angle shooting, for instance, the key light for one performer may become the back light for the other and vice versa. This technique is generally called cross—keying.
Application of lighting instruments for multiple functions requires exact positioning of set pieces such as tables and chairs, clearly defined performance areas, and blocking (movements of performers).

## Slide 32
4. Large Area Lighting
For large area lighting, such as for an audience or large choir, the basic photographic principle still holds: Partially overlap one triangle on another until entire area is adequately covered

## Slide 33
5. High Contrast Lighting
This is the opposite of flat lighting and it mirrors motion picture lighting techniques. Because of the increased tolerance of latest video cameras to low light levels and higher contrast lighting, many television plays make extensive use of fast-fall off lighting. Notice that in some series, such as crime or medical shows, do not use only extremely fast fall-off lighting (harsh shadows) but also colour distortion to intensify the scenes. Fast fall-off creates dramatic scenes and can be used to portray a certain mood. Dramatic lighting requires not only skill but also takes a lot of production time.

## Slide 34
6. Cameo Lighting
Certain television shows, especially those of a dramatic nature, are staged in the middle of an empty studio against an unlighted background. This technique, where the performers are highlighted against a plain dark background, is commonly known as cameo lighting. Cameo lighting concentrates on the talent and not the environment.
All cameo lighting is highly directional and is achieved most effectively using spotlights with barn doors. In small studios, the background areas are carefully shielded from any kind of distracting spill light with black, light absorbing draperies.

## Slide 35
7. Silhouette Lighting
Lighting for silhouette effect is the opposite of cameo lighting. In silhouette lighting you light the background but leave the figures in front unlighted. This way you see only the contour of objects and people but not there volume and texture. To achieve silhouette lighting, use highly diffused light (usually soft lights) to evenly illuminate the background. You can use silhouette lighting to conceal the identity of a person appearing on camera.

## Slide 36
8. Chroma-key Lighting
The chroma-key set area normally consists of a plain blue or green backdrop. It is used to provide backgrounds that are electronically generated, replacing the blue or green areas during the key-a process called chroma-keying.
A popular use of the chroma key is a weather report. Although the weatherman seems to be standing in front of a large weather map, he/she is in fact standing in front of an empty, evenly lighted blue or green backdrop. When the blue or green areas are electronically replaced by the weather map during the key, the weather caster must look into a monitor to see the map.
The most important aspect of lighting the chroma-key set area is even background illumination, which means that the blue or green backdrop must be lighted with highly diffused instruments, such as soft lights or floodlight banks.