## Slide 1: Technology Management Tools

## Slide 3: Life Cycle Theory
Abstract Entity (inputs and outputs are cognitive and mostly virtual)
The product is conceived by identified need & opportunity
Needs are translated into concept and then designs
Physical Entity (inputs and outputs are material)
Quantities of physical material are transformed to make the product
The product delivers value to the user
When value is less than cost the product is disposed
concept
need
design
production
use
disposal
Development Cycle abstract entity
Applied Cycle physical entity
Driving Force – Markets & Economies
Event Progression
Life Cycle of Whole Entity
Consider technology that enables reuse or repurposing
The irreversible nature of time!

## Slide 4: Life Cycle Theory
Platform Technologies
  Leveraging investment in R&D for extended product lifecycles
  Standardisation and mass production
  Facilitates “plug and play” modular architectures
  More sophisticated modular systems enable mass customisation
pure research
innovation
development
applied research
business
15 – 30 years
platform domain
2 – 5 years
incremental domain
1 – 2 years
breakthrough domain
10 + years

## Slide 5: Life Cycle, Cash Flow & Platform Technology
Extending an existing product design extends the revenue period
Investment in design and development is carried forward
An added bonus period of profit is realizable since cost is already recovered
TIME
SALES
introduction
growth
maturity
decline
new product platform new product
next product
overall profit
profit curve
break even, sooner

## Slide 6: Technology S-Curve
Richard N. Foster – determined a way of predicting discontinuity associated with disruptive technologies
Advancement of a new technology may be slow in the beginning whilst capability and competence builds
As knowledge and experience develop the technology reaches a breakthrough point that qualifies it as an recognised enabler of new greater benefits
The technology goes through rapid advances as it matures and creates new markets
At late stages, minor incremental changes have limited impact on generating revenue
Cumulative measure of
Adoption and Advancement
Time and Effort
Pioneering efforts in engineering and development until breakthrough is achieved
Technology hits it’s effectiveness limits and declines in revenue generation
for the specific application
New curve may have different profile of advancement
Representing a different technology with a more advanced approach to achieving the same or similar benefits
Discontinuity
Introduction of New Technologies
Technology
A
e.g. propeller aircraft
Technology B
e.g. jet aircraft

## Slide 7: Disruptive Technology
Helps create new markets by displacing existing technology with new functions, features, efficiencies and cost structure (valued – benefits).
Businesses that are locked into a value network are vulnerable to disruptive technology.
Due to the investment barrier associated with a new technology survival often means focus shifts to competing on a cost reduction basis and options become very limited leading to the commodity corner.
Incumbent
cassette tape
ICE powered cars fixed wire phone photographic film paperback books
Disruptor
 compact disc
 electric powered cars
 mobile phone, VOIP
 CMOS, CCD, digital imaging
 internet, ebooks
Need
Incumbent
Disruptor
Quality
Time
Clayton M. Christensen Model

## Slide 9: Roadmapping Process
The V - Model
The development funnel - screening / qualifying
Based on the V-model commonly used in systems engineering
Corporate strategy determines the context of the V model based on capabilities and risk/return
Requirements/strategies are identified and broken down to sub-set levels
Implementation solutions should be developed and iterated via “the development funnel”
The development funnel applies a stage gate process to screen and qualify the good from the bad
Past
Future
Product
Technology
Product
Implementation
Market
Requirements (strategy)
Market

## Slide 10: Roadmapping Process
Workshop Markets
 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Product |  |  |  |  |  |  |  |  |  | 
Segment Product |  |  |  |  |  |  |  |  |  | 
T Marketgy echnolo |  |  |  |  |  |  |  |  |  | 
Environment |  |  |  |  |  |  |  |  |  | 
Social |  |  |  |  |  |  |  |  |  | 
Political |  |  |  |  |  |  |  |  |  | 
Economic |  |  |  |  |  |  |  |  |  | 
Competition |  |  |  |  |  |  |  |  |  | 
Diversification |  |  |  |  |  |  |  |  |  | 
Sequence of workshops
Regular workshop and review processes
Roadmaps are built up and maintained as live documents
Consolidated Roadmaps
Workshop Business Strategy
Workshop Products
record
record
Review via decision criteria
Review via decision criteria
Track progress via
Program Stage Gates
Workshop Technologies
Review via decision criteria
record
25-May-16

## Slide 11: Defining a Project
Aim & Objectives
Expected Outcomes
Strategy & Scope (time +budget +resources → expected outcomes)
Work Breakdown Structure (e.g. Pert Chart)
RASIC Chart (Responsible, Approvals, Support, Inform, Consult)
Milestones, Deliverables, Critical Path and Timing (Gantt Chart)
Managing Resources
Budget – track cost and measure Earned Value
Monitoring – respond as needed
Reporting

## Slide 12: The Stage Gate Process
Preceding each stage is a point or gate review which serves as a Go/Kill and decision point.
Gate reviews are where average projects are discarded out so that resources can be allocated to the best projects.
  Ideally, troubled projects are brought to review before they are in crisis
  Problems are analyzed and corrective actions are issued
  Being too hasty in killing a project for purely financial reasons can wipe out potentially profitable business opportunities
  Recovery versus write off of a bad investment or overspend requires a judgment on whether a saleable product is achievable. i.e. it may be better to accept a break even or minor loss with ROI than get nothing from the investment.
Quality of execution, business rationale, quality of action plan
deliverables
criteria
outputs

## Slide 13: Design Reviews versus Gate Reviews
Design/Engineering reviews assess the technical progress
Understanding requirements
Determining alternative solutions
Understanding the compromises
Determining the optimal solution
Details of how the optimal solution is to be executed
Details of any changes required to rectify an identified problem (ECR)
Details of the embodiment of the optimal solution include design release information (ERN)
Details of the sensitivities / technical risk presented by the design solution
Proof that the design is what was expected / intended - verification
Proof that the design meets the
customer, legal and market requirements – validation
Outputs and deliverables of design reviews are summarized
in gate reviews
Gate reviews focus more on the business metrics
Is the money spent creating value
Is the program meeting milestone and timing commitments
What are the risk priorities
Is the spend rate on track
Is the program going to be profitable
What are the appropriate next actions

## Slide 14: Risk Management
A risk is characterised by an event or condition that, if occurs, will have a negative impact, cause harm or a loss.
Risk is generally quantified in terms of likelihood of occurrence and the consequences of the negative event.
Risk = Probability X Consequence
Risk is inherent in all systems that are subject to the chaotic conditions of cause and effect.
Risk is an integral part of life and evolution. Even if you’re completely isolated from the world you yourself are a system of interconnecting subsystems, functions and processes… any of which could behave unexpectedly.

## Slide 15: Risk Management
The complete consideration of risk takes into account:
Likelihood (l)
Outcome (o)
Utility or significance (u)
Cause scenarios (c)
Scope or extent of exposure (p)
Hazard or Threat
Exposure: population, property, environment
Vulnerability
At Risk
Risk ≡ {(li,oi,ui,ci,pi),…, (ln,on,un,cn,pn)}

## Slide 16: Reliability Engineering
Infant mortality
Useful life
Wear out
Bathtub Curve
Infant mortality period:
characterised by an initially high failure rate which decreases rapidly
failures are due primarily to poor manufacturing techniques and quality control
Useful life period:
  characterised by a nearly level failure rate
  failures are random and are due primarily to inadequate design
Wear out period:
characterised by an increasing failure rate
failures are due to natural aging, sometimes poor maintenance
Failure Rate
time

## Slide 17: Simple Break Even Analysis
Recap… simple break even analysis is intended to find the volume of saleable units that are needed to achieve to recovery of an investment required to make the units in-house as compared to purchasing (outsourced).
Selling Price (P) … determined by market supply and demand
Quantity (Q) is the volume of units sold
Fixed Cost (FC) is generally associated with the capital cost or investment in development and production capacity such as manufacturing infrastructure/assets
Variable Cost (VC) is the cost associated with each unit produced, usually consists of the
cost of labour, materials and consumed resources
Total Cost (TC) = FC + VC
Total Revenue (TR) is the income from sales (P x Q )
Break Even Point (BEP) is the point where revenue matches the total cost… beyond which a profit will be realised
Because there is no profit ($0) at the break-even point, TR − TC = 0, and then P × Q − ( FC + VC × Q ) = 0. Therefore, Q = FC / ( P − VC )
However, it may be more useful to know the quantity necessary to generate a desired level of profit (Z).
TR − TC = Z
P × Q − ( FC + VC × Q ) = Z
Then … Q = ( FC + Z ) ÷ ( P − VC )
VC
TC
TR
FC
Q
$
BEP
Loss
Profit

## Slide 18: Decision Trees
How to…
  List options (include all possible action alternatives!)
  List uncertain events (mutually exclusive and collectively exhaustive)
  Construct a decision tree along a time line
Evaluate endpoints (outcomes for each end branch)
Assess event probabilities
“Expect-out and Fold Back” = Backwards Induction
Do sensitivity analysis on variables
Consider what the result means in context of the bigger picture decision making?
… are you backing the right horse?
decision nodes
event nodes
(list of choices)
(list of events)

## Slide 19: Decision Trees - Example
A high technology business is in the midst of developing a diversification strategy to broaden it’s market share and build greater scope in the product portfolio. A decision must be made on whether to make or buy the product of their newly developed technology. The choices and probabilistic outcomes have been mapped as described in the decision tree below… Which is the best option?
0.4
$ 6,020,800
0.3
1
0.2
0.1
$ 10,700,000
$ 7,400,000
$ 1,104,000
-$ 7,000,000
0.5
$ 7,490,000
0.2
$ 7,490,000
1
0.2
0.1
-
$
Outsource
In-house
Do nothing
Exceed target volume
Achieve target volume
Less than target volume
Expected Return
Expected Return
Expected Return
$ 13,800,000 | * 0.5 = | 6,900,000
$ 8,400,000 | * 0.2 = | 1,680,000
$ 300,000 | * 0.2 = | 60,000
Program failure
Exceed target volume
Achieve target volume
Less than target volume
Program failure
* 0.4 =
4,280,000
* 0.3 =
2,220,000
* 0.2 =
220,800
* 0.1 =
- 700,000
6,020,800
-$ 11,500,000 * 0.1 = - 1,150,000
7,490,000

## Slide 20: Decision Trees – your turn…
0.4
$ | 2,675,000
$ | 1,850,000
$ | 276,000
-$ | 1,750,000
$ | 2,450,000
$ | 1,950,000
$ | 75,000
-$ | 2,875,000
$ | -
0.3
0.1
0.5
0.1
0.1
Outsource
In-house
Do nothing
Exceed target volume
Achieve target volume
Less than target volume
Expected Return
Expected Return
Expected Return
Program failure
Exceed target volume
Achieve target volume
Less than target volume
Program failure
$ 1,505,200
$ 1,530,000
$ 1,530,000
0.2
0.3
25-May-16