## Slide 1: William Stallings Data and Computer Communications 9th Edition
Chapter 2
Protocols and Architecture

## Slide 2: Need For Protocol Architecture
E.g. File transfer
  Source must activate comms. Path or inform network of destination
  Source must check destination is prepared to receive
  File transfer application on source must check destination file management system will accept and store file for his user
  In case of incompatible file formats, we may require file format translation
Task broken into subtasks
Implemented separately in layers in stack
Functions needed in both systems
Peer layers communicate

## Slide 3: Protocol
A protocol is a set of rules that governs the communications between computers on a network. In order for two computers to talk to each other, they must be speaking the same language.

## Slide 4: Key Elements of a Protocol
Syntax
  Data formats
  Signal levels
Semantics
  Control information
  Error handling
Timing
  Speed matching
  Sequencing

## Slide 5: Protocol Architecture
Task of communication broken up into modules
For example file transfer could use three modules
  File transfer application
  Communication service module
  Network access module
Nature of exchange between systems is independent of the nature of the network that connects them.

## Slide 6: Simplified File Transfer Architecture

## Slide 7: A Three Layer Model
Network Access Layer
Transport Layer
Application Layer

## Slide 8: Network Access Layer
Exchange of data between the computer and the network
Sending computer provides address of destination
May invoke levels of service
Dependent on type of network used (LAN, packet switched etc.)

## Slide 9: Transport Layer
Reliable data exchange
Independent of network being used
Independent of application

## Slide 10: Application Layer
Support for different user applications
e.g. e-mail, file transfer

## Slide 11: Protocol Architectures and Networks

## Slide 12: Addressing Requirements
Two levels of addressing required
Each computer needs unique network address
Each application on a (multi-tasking) computer needs a unique address within the computer
  The service access point or SAP
  The port on TCP/IP stacks

## Slide 13: Protocol Data Units (PDU)
At each layer, protocols are used to communicate
Control information is added to user data at each layer
Transport layer may fragment user data
Each fragment has a transport header
  Destination SAP
  Sequence number
  Error detection code
This gives a transport protocol data unit

## Slide 14: Protocol Data Units

## Slide 15: Network PDU
Adds network header
  network address for destination computer
  Facilities requests

## Slide 16: Operation of a Protocol Architecture

## Slide 17: OSI
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers

## Slide 18: OSI - The Model
A layer model
Each layer performs a subset of the required communication functions
Each layer relies on the next lower layer to perform more primitive functions
Each layer provides services to the next higher layer
Changes in one layer should not require changes in other layers

## Slide 19: The OSI Environment
Notes: In communication technology, trailer or footer refers to supplemental data placed at the end of a block of data being stored or transmitted, which may contain information for the handling of the data block, or just mark its end.

## Slide 20: OSI Layers (1)
Physical
  Physical interface between devices
  Hub operates at the physical layer
Data Link
  Means of activating, maintaining and deactivating a reliable link
  Error detection and control
  Higher layers may assume error free transmission
  Switch operates at the data link layer

## Slide 21: OSI Layers (2)
Network
  Transport of information
  Higher layers do not need to know about underlying technology
  Not needed on direct links
  Routers operate at the network layer
  Important Protocols at this layer: IP
Transport
  Exchange of data between end systems
  Error free
  In sequence
  No losses
  No duplicates
  Quality of service
  Important Protocols at this layer: TCP, UDP

## Slide 22: OSI Layers (3)
Session
  Control of dialogues between applications
  Dialogue discipline
  Grouping
  Recovery
Presentation
  Data formats and coding
  Data compression
  Encryption
Application
  Means for applications to access OSI environment

## Slide 23: Use of a Relay

## Slide 24: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
Used by the global Internet
No official model but a working one.
  Application layer
  Host to host or transport layer
  Internet layer
  Network access layer
  Physical layer

## Slide 25: Physical Layer
Physical interface between data transmission device (e.g. computer) and transmission medium or network
Characteristics of transmission medium
Signal levels
Data rates
etc.

## Slide 26: Network Access Layer
Exchange of data between end system and network
Destination address provision
Invoking services like priority

## Slide 27: Internet Layer (IP)
Systems may be attached to different networks
Routing functions across multiple networks
Implemented in end systems and routers

## Slide 28: Transport Layer (TCP)
Reliable delivery of data
Ordering of delivery

## Slide 29: Application Layer
Support for user applications
e.g. http, SMTP

## Slide 30: OSI v TCP/IP

## Slide 31: TCP/IP Concepts

## Slide 32: Addressing level
Level in architecture at which entity is named
Unique address for each end system (computer) and router
Network level address
  IP or internet address (TCP/IP)
  Network service access point or NSAP (OSI)
Process within the system
  Port number (TCP/IP)
  Service access point or SAP (OSI)

## Slide 33: Trace of Simple Operation
Process associated with port 1 in host A sends message to port 2 in host B
Process at A hands down message to TCP to send to port 2
TCP hands down to IP to send to host B
IP hands down to network layer (e.g. Ethernet) to send to router J
Generates a set of encapsulated PDUs

## Slide 34: PDUs in TCP/IP

## Slide 35: UDP(User Datagram Protocol)
Transport-level protocol
Does not guarantee delivery
Connectionless
Optional use of the checksum

## Slide 36: TCP Header
Notes: TCP segments include a header. Stallings DCC8e Figure 2.3a shows the header format for TCP, which is a minimum of 20 octets, or 160 bits. The Source Port and Destination Port fields identify the applications at the source and destination systems that are using this connection. The Sequence Number, Acknowledgment Number, and Window fields provide flow control and error control. The checksum is a 16-bit frame check sequence used to detect errors in the TCP segment. Chapter 20 provides more details.

## Slide 37: UDP Header
Notes: Because it is connectionless, UDP has very little to do. just adding a port addressing capability to IP. This is best seen by examining the UDP header, shown in Stallings DCC8e Figure 2.3b. The UDP header also includes a checksum to verify that no error occurs in the data; the use of the checksum is optional.

## Slide 38: IP Header
Notes: For decades, the keystone of the TCP/IP protocol architecture has been IP. Stallings DCC8e Figure 2.4a shows the IP header format, which is a minimum of 20 octets, or 160 bits. The header, together with the segment from the transport layer, forms an IP-level PDU referred to as an IP datagram or an IP packet. The header includes 32-bit source and destination addresses. The Header Checksum field is used to detect errors in the header to avoid misdelivery. The Protocol field indicates which higher-layer protocol is using IP. The ID, Flags, and Fragment Offset fields are used in the fragmentation and reassembly process. Chapter 18 provides more detail.

## Slide 39: Example Header Information
Destination port
Sequence number
Checksum

## Slide 40: Some Protocols in TCP/IP Suite

## Slide 41: End of chapter 2
Quiz of chapter 2 due