## Slide 1
Lab Safety Measures and Waste Chemical Disposal: A Key Step towards Safe, Healthy and Productive Workplace Environment

## Slide 2: Safe, and Healthy Workplace Environment
Better Workplace Environment-High Yield and Productivity
For a Cleaner, Human-friendly and Safer Workplace Environment, we should ensure that our students, faculty and staff meet and follow the regulations related to handling of:
Hazardous materials
Laboratory chemicals
Waste chemicals disposal
ISO-9000, ISO 14000 series
A Shared Responsibility;
Supplier/Producers
Employer
Employee

## Slide 3: Ill-Controlled Handling of Chemicals/Toxins-A Threat!
Health problems
Environment pollution
Worker safety

## Slide 4: Health Issues
Exposure to harmful/toxic materials can cause or contribute to many serious health effects such as:
    Irritation of the skin (rashes)
    Burns
    Sensitization
    Heart, liver, kidney and pulmonary ailments
    Cancer
    Reproductive disorders

## Slide 5: Environment Pollution
Air pollution- volatile solvents
Contaminate under ground water reservoir
Affect aquatic life
Global warming
Contaminated food and drinking water by POPs
Soil contamination due to heavy metal, herbicides, pesticides etc.
Soil becomes infertile and unsuitable for plants
Radioactive contamination

## Slide 6: Worker Safety
Fire Hazards
Explosions
Electric Shock
Cuts

## Slide 7: What are Chemical Hazards????
A chemical hazard arises from contact with harmful or potentially harmful chemicals
Chemical hazards may be described under three broad headings –
Flammability
Flammable substances are those that readily catch fire and burn in air.
Reactivity
Reactive chemical hazards invariably involve the release of energy (heat) in relatively high quantities or at a rapid rate.
Health
Contact with many chemicals can result in adverse health effects.
Possible route of contact
Skin and eye contact
Inhalation
Ingestion
injection

## Slide 8: Classifications of Chemicals
Prohibited – May not be advertised, sold or imported
Restricted – Must meet Consumer Chemicals and Containers regulations (e.g. Bleach)
Controlled – Products regulated by some legislation/specifications

## Slide 9: Controlled Products –(Six Classes ) Characteristics, Hazards and Precautions

## Slide 10
Class A: Compressed Gas
Class B: Flammable and Combustible Material
Class C: Oxidizing Material

## Slide 11: Class D
Division 1:
Materials Causing Immediate and Serious Toxic Effects
Division 2:
Materials Causing Other Toxic Effects
Division 3:
Biohazardous Infectious Materials

## Slide 12
Class E: Corrosive Material
Class F: Dangerously Reactive Material

## Slide 13: Class A: Compressed Gas
Characteristics:
Gas inside cylinder is under pressure
Hazards:
The cylinder may explode if heated or dropped.
hazard from both the force of explosion and the release of its contents.
Sudden release of high pressure gas streams may puncture skin and cause fatal embolism.
E.g. Propane, oxygen, acetylene

## Slide 14: Class A: Compressed Gas
Precautions
Transport and handle with care
Make sure cylinders are properly secured
Store away from sources of heat or fire
Use proper regulator

## Slide 15: Class B: Flammable & Combustible Material
    Six divisions:
    Division 1: Flammable Gas
    Division 2: Flammable Liquid
    Division 3: Combustible Liquid
    Division 4: Flammable Solid
    Division 5: Flammable Aerosol
    Division 6: Reactive Flammable Material

## Slide 16: Class B: Flammable and Combustible Material
Characteristics:
May burn or explode when exposed to heat, sparks or flames
Flammables: burns readily at room temperature (flash point < 37.8oC)
Combustible: burns when heated (flash point > 37.8oC)

## Slide 17: Class B: Flammable and Combustible Material
Hazards:
may ignite spontaneously
may be a material which will release flammable products if allowed to degrade or when exposed to water
Precautions:
Store away from Class C (oxidizing materials)
Store away from sources of heat, sparks and flame
Do not smoke near these materials may ignite spontaneously

## Slide 18: Class B: Flammable and Combustible Material
Flammable Gas: Hydrogen, Butane
Flammable Liquid: Gasoline
Combustible Liquid: Diesel Fuel, Organic solvents
Flammable Solid: White Phosphorus, Magnesium
Flammable Aerosol: flammable propellants such as propane, butane and dimethyl ether
Reactive Flammable Material: aluminum alkyls, metallic sodium and lithium aluminum hydride

## Slide 19: Class C: Oxidizing Material
Characteristics:
Can cause other materials to burn or explode by providing oxygen to support combustion
Hazards:
May burn skin and eyes on contact
Increase fire and explosion hazard
May cause combustibles to explode or react violently
E.g. Hydrogen peroxide, bleach, nitric acid and ozone

## Slide 20: Class C: Oxidizing Material
Precautions
Store away from Class B (flammable and combustible) materials
Store away from sources of heat and ignition
Wear the recommended protective equipment and clothing

## Slide 21: Class D, Division 1 Materials Causing Immediate and Serious Toxic Effects
Subdivision A: Very Toxic Material
Subdivision B: Toxic Material
Characteristics:
Poisons potentially fatal materials which cause immediate and severe harm
Hazards:
May cause immediate death or serious injury if inhaled, swallowed, or absorbed through the skin.
Very small quantities may be harmful
E.g.: Arsenic, hydrogen cyanide, chlorine gas.

## Slide 22: Class D, Division 1 Materials Causing Immediate and Serious Toxic Effects
Precautions:
Avoid inhaling gas or vapors
Avoid skin and eye contact
Wear the recommended protective equipment and clothing
Do not eat, drink or smoke near these materials
Wash hands after handling

## Slide 23: Class D, Division 2 Materials Causing Other Toxic Effects
  Subdivision A: Very toxic material
  Subdivision B: Toxic material
Characteristics:
Materials which have harmful effects after repeated exposures or over long periods of time
Hazards:
May cause death or permanent injury following repeated or long-term exposure
May irritate eyes, skin and breathing passages: may lead to chronic lung problems and skin sensitivity
May cause liver or kidney damage, cancer, birth defects or sterility

## Slide 24: Class D, Division 2 Materials Causing Other Toxic Effects
Precautions
Avoid inhaling gas or vapors
Avoid skin and eye contact
Wear the recommended protective equipment and clothing
Do not eat, drink or smoke near these materials
Wash hands after handling
E.g.: Asbestos, silica, fiberglass, coal dust.

## Slide 25: Class D, Division 3 Bio hazardous Infectious Material
Characteristics:
Infectious agents or a biological toxin causing a serious disease or death
  Includes viruses, yeasts, moulds, bacteria and parasites which affect humans
  Includes fluids containing toxic products
  Includes cellular components
Hazards:
May cause serious disease resulting in illness or death.
E.g.: E. coli, salmonella, molds, bacteria, viruses, parasites, body fluids.

## Slide 26: Class D, Division 3 Bio hazardous Infectious Material
Precautions:
Wear the recommended protective equipment and clothing
Work with these materials only in designated areas
Disinfect area after handling
Wash hands after handling

## Slide 27: Class E: Corrosive Material
Characteristics:
Materials that will erode metals or destroy tissues
Hazards:
Will burn eyes and skin on contact
May cause blindness
Will burn tissues of respiratory tract if inhaled.
E.g.: battery acid, hydrochloric acid, bleach, ammonia

## Slide 28: Class E: Corrosive Material
Precautions:
Store acids and bases in separate areas
Avoid inhaling these materials
Avoid contact with skin and eyes
Wear the recommended protective equipment and clothing

## Slide 29: Class F: Dangerously Reactive Material
Characteristics:
Materials with may undergo unexpected reactions under certain conditions
Hazards:
May be chemically unstable
May explode if exposed to shock or heat
May react with water to release a toxic or flammable gas.
May vigorously polymerize
May burn unexpectedly
E.g.: Calcium carbide, hydrazine and benzoyl peroxide, metalic sodium

## Slide 30: Class F: Dangerously Reactive Material
Precautions
Follow manufacturer's recommendations for storage (i.e. store away from heat ; avoid shock and friction)
Wear the recommended protective equipment and clothing

## Slide 31: Laboratory Waste Disposal
Improper handling and disposal of hazardous chemical waste can causes severe environmental and health problems.
Proper disposal of laboratory chemical waste is a key factor to generating safer and healthier environment.
Use of Waste management practices

## Slide 32: Common Errors in Waste Handling
Improper labeling of waste
Improper segregation of waste
Improper storage of waste
Failure to cap waste bottles
Accumulation of excessive watse

## Slide 33: Segregation of chemical waste
Followings can be grouped based upon reactivity!
Inorganic acids and acid salts
Nitrogenated bases, caustics and acid-reactive compounds
Neutral organic solids
Flammable liquids, Halogenated solvents and organic acids
Oxidizers
Pesticides
Water and air reactive materials

## Slide 34: Never Store the Followings Types of Wastes Together
Acids and bases
Organics and acids
Cyanide, sulfide or arsenic compounds and acids
Alkiali or alkali earth metals, alkyllithiums etc. and aqueous waste
Powdered or reactive metals and combustible materials
Mercury or silver and ammonium containing compounds

## Slide 35: Laboratory Hazards & First Aid
1-Cuts
Caused by glassware, metal or other materials
Use sterilize bandage
2-Burns
Cool burnt with cold water/ice, seek medical help
3-Electric shock
Switch off the source of electric power
Call the doctor immediately
4-Chemical Injuries
Rinse with running tap water
Acid with saturated solution of sodium bicarbonate
Alkaline with 2% acetic acid solution
Shift the person into open air when a person inhaled poisonous vapors
5-Fire Explosions
Close the oxygen/gas supply supply , cover the person with fire blanket, use fire extinguishes, Do not create rush, try to leave the lab carefully

## Slide 36: Laboratory management practices
Do not cause panic in case of any mishap (unwanted chemical reaction, injury or equipment damage). Call supervisor!
Use protective clothes/gloves
No smoking, eating or drinking in lab
Work carefully with scientific attitude
Follow safety instructions
Do not leave the lab with out permission
Clean and organized work place
Do not put yourself in danger
Call the supervisor upon unwanted chemical reaction
Use fume hood for volatile and flammable solvents
Use electric heater for flammable substances
Wash infected area of body with fresh water
Mouth pipetting is strictly prohibited
Do not leave any experiment unattended
Carefully work with gas cylinders
Wash your hand before leaving the lab

## Slide 37
THANK YOU FOR YOUR ATTENTION!