## Slide 1: ESTIMATION Engr. Muhammad Owais
1
8/24/2016
Estimation-Engr. Shehroze Ali

## Slide 2: ESTIMATION
“Estimation is the scientific way of working out the approximate cost of an engineering project before execution of the work”
It is totally different from calculation of the exact cost after completion of the project.
Estimation requires a thorough Knowledge of the construction procedures and cost of materials & labour in addition to the skill , experience, foresight and good judgment.
8/24/2016
Estimation-Engr. Shehroze Ali
2

## Slide 3:  An estimate of the cost of a construction job is the probable cost of that job as computed from plans and specifications.
 For a good estimate the, actual cost of the proposed work after completion should not differ by more then 5 to 10 % from its approximate cost estimate, provided there are no unusual, unforeseen circumstances.
8/24/2016
Estimation-Engr. Shehroze Ali
3

## Slide 4: NEED FOR ESTIMATE
It help to work out the approximate cost of the project in order to decide its feasibility with respect to the cost and to ensure the financial resources, if the proposal is approved.
Requirements of controlled materials, such as cement and steel can be estimated for making applications to the controlling authorities.
It is used for framing the tenders for the works and to check contractor’s work during and after the its execution for the purpose of making payments to the contractor.
From quantities of different items of work calculated in detailed estimation, resources are allocated to different activities of the project and ultimately their durations and whole planning and scheduling of the project is carried out.
8/24/2016
Estimation-Engr. Shehroze Ali
4

## Slide 5: SITE CONDITIONS AFFECTING THE OVERALL COST
Each type of work requires a different method of construction. Construction may be of an ordinary house or office and it may also be of a Dam, Tunnel, Multistory building, Airport, Bridge, or a Road, already in operation. Each of these works requires totally different construction techniques, type of machinery, and formwork.
Quality of labour and labour output varies in different localities.
Weather conditions greatly affect the output and, hence, the overall cost.
8/24/2016
Estimation-Engr. Shehroze Ali
5

## Slide 6: 4. Ground conditions vary and change the method of construction. For example, excavation may be dry, wet, hard, soft, shallow or deep requiring different efforts.
The work may be in open ground such as fields or it may be in congested areas such as near or on the public roads, necessitating extensive watching, lightening, and controlling efforts, etc.
The source of availability of a sufficient supply of materials of good quality is also a factor.
The availability of construction machinery also affects the method of construction.
Access to the site must be reasonable. If the access is poor, temporary roads may be constructed.
8/24/2016
Estimation-Engr. Shehroze Ali
6

## Slide 7: Terminologies
Contingencies – Indicates incidental expenses of miscellaneous character which cannot be classified under any distinct item. (3% to 5% of the estimated cost is provided to allow for contingencies)
Work-charged Establishment – Work-charged employees are temporary staff whose services are terminated at the expiry of sanctioned period but usually one month notice is given. (1.5% to 2% of the estimated cost is added).
Tools and Plants – Normally contractor has to arrange tools and plants. (1% to 1.5% of estimated cost is provided).
 Centage charges or Departmental charges – Also known as Supervision charges for works. To meet the expenses of establishment, designing, planning, supervision etc. (10% to 15% of the estimated cost). When engineering department takes up work of other department.
8/24/2016 Estimation-Engr. Shehroze Ali
7

## Slide 8:  Sub-Head items of work – Works like earthwork, concrete work, brick work etc. Under each sub head there are different items of work.
Sub-Work – Large project may consist of small buildings. Detailed estimate of each sub-work is prepared separately.
Schedule of Rates – It is a list of rate of various items of works maintained by engineering department under the name “Schedule of Rates Book”. “Road Metal Rate Book” is also maintained by PWD.
Administrative Sanction/ Approval – It is the formal acceptance by the department concerned of the proposal. After the approval, design, estimates etc. are prepared and thereafter execution of work.
8/24/2016
Estimation-Engr. Shehroze Ali
8

## Slide 9:  Expenditure Sanction – It represents allotment of money to meet the expenditure. It is usually accorded by Finance Department.
Technical Sanction – It is the sanction of the detailed estimate, design calculation, quantities of work etc. Technical sanction is accorded by engineering department and execution of work is carried out thereafter.
Quantity Survey – It means estimating of quantities of different items of works.
Plinth Area – It is the built up covered area of a building measured at floor level of any storey by taking external dimensions of the building at the floor level.
8/24/2016
Estimation-Engr. Shehroze Ali
9

## Slide 10:  Floor Area – It is obtained after deducting area of walls from the plinth area of building. It should include:
Door and other openings
Intermediate pillars and supports
Circulation Area – It is the floor area of verandahs, passages, corridors, balconies, staircases, lift etc. which are used for movements of persons using the building. It is further classified into Horizontal and Vertical.
Carpet Area – It is the useful area of the building. It is determined after deducting :
  Circulation Area
  Sanitary Accommodations
  Kitchen, Pantry, Stores
  For office building approximate 60% to 75% of plinth area
  For residential buildings approximate 50% to 65% of plinth area
8/24/2016 Estimation-Engr. Shehroze Ali
10

## Slide 11: Plan showing orientation of building, boundaries of land, position of roads, drains, sewer line, water pipelines and adjoining plots of lands. North direction is also shown on one corner of site plan).
 Site Plan –
Layout Plan –
  Plan showing proposed buildings, structures etc. showing their locations, size and orientations.
  Roads, drains, pipe lines , electric lines, parks etc are shown.
  The boundary, main approach roads and adjoining areas are also indicated.
Index Plan –
  Plan is usually drawn for Roads, Irrigation, Water supply etc.
  It shows alignment with position of culverts, main outline of whole work to give idea of the project
  For big project it is drawn with much small scale and is known as key plan
8/24/2016 Estimation-Engr. Shehroze Ali
11

## Slide 12: Types of Estimates
Preliminary/Appx./Abstract/Rough Cost Estimate
Plinth Area Estimate
Cube Rate or Cubical Content Estimate
Appx. Quantity Method Estimate
Detailed Estimate or Item Rate Estimate
Revised Estimate
Supplementary Estimate
Supplementary and Revised Estimate
Annual Repair or Maintenance Estimate (A.R or A.M Estimate)
8/24/2016
Estimation-Engr. Shehroze Ali
12

## Slide 13: PRELIMINARY ESTIMATE
Preliminary Estimate is prepared by various ways for different structures as mentioned below :
Buildings
  Per Unit Basis – Per student for schools and hostels, per class room for schools, per bed for hospitals, per seat for cinema and theatre halls, per tenement for residential buildings.
  Plinth area basis
  Cubic content basis
  Appx. Quantity method
Roads and Highways – Per km basis depending upon nature of road, width and thickness of metalling.
Irrigation Channels
  Per km basis
  Per hectare basis (Area of land commanded)
8/24/2016 Estimation-Engr. Shehroze Ali
13

## Slide 14: PRELIMINARY ESTIMATE (Ctd.)
Bridges and Culverts – Per running meter of span depending upon type of structure, type and depth of foundation.
Sewerage and Water Supply Project
  Per head of population served
  Per hectare basis (Area covered)
Over Head water Tank – Per liter or per gallon of tank depending upon type of structure and height of tank.
8/24/2016
Estimation-Engr. Shehroze Ali
14

## Slide 15: PLINTH AREA ESTIMATE
P.A. is approximate estimate
Plinth area should be calculated for covered area by taking external dimensions of the building at the floor level
Courtyard and other open area should not be included.
For multi storeyed building Plinth Area for each storey is determined separately.
Approximate total plinth area may be calculated by adding 30 to 40% of the already calculated area for walls, circulation and waste etc.
 Plinth area rate is known from cost of similar building in the locality.
8/24/2016 Estimation-Engr. Shehroze Ali
15

## Slide 16: CUBE RATE ESTIMATE
Cube rate estimate is again approximate estimate
Cubical content of the building is determined by multiplying length, breadth and height of the building.
External length and breadth at the floor level are calculated for the purpose
Height should be taken from the floor level to the top of roof.
For multi storeyed building height is taken from floor level of one
storey to top of next higher floor.
Cube rate estimate is more accurate as compared to the plinth area estimate.
8/24/2016 Estimation-Engr. Shehroze Ali
16

## Slide 17: APPROXIMATE QUANTITY METHOD ESTIMATE
Structure divided into two parts –
  Foundation including plinth
  Superstructure
Total length of walls is found out.
To find running meter rate of foundation, appx. quantities of various items are calculated per running meter
Similarly for superstructure appx. Quantities of brickwork, roof, flooring etc is calculated per running meter.
8/24/2016
Estimation-Engr. Shehroze Ali
17

## Slide 18: DETAIL ESTIMATE
It is the accurate estimate prepared by working out quantities of each
items of work.
It is prepared in two stages –
  Details of measurements and calculation of quantities.
  Abstract of estimated cost – 3% to 5% of estimated cost is added to cover miscellaneous expenditure
Detailed estimate is prepared work-wise and it consists of-
  Report
  General Specifications
  Detailed specifications
  Drawings
  Calculation and designs
  Analysis of rates
Detailed estimate is prepared for technical sanction, for arranging contract and for execution of project.
8/24/2016 Estimation-Engr. Shehroze Ali 18

## Slide 19: REVISED ESTIMATE
Revised estimate is prepared when original sanctioned estimate is likely to exceed more than 5%.
When expenditure on work is likely to exceed amount of
administrative sanction by more than 10%
When there are material deviation from original proposal even though cost may be met from sanctioned cost.
It is accompanied by comparative statement showing variations in each item of works and reason for the same.
8/24/2016
Estimation-Engr. Shehroze Ali
19

## Slide 20: SUPPLEMENTARY ESTIMATE
It is the fresh detailed estimate of the additional works in addition to the original estimate.
It is required when further development is required during the progress of work.
Abstract should show the amount of original estimate and total amount including supplementary amount.
8/24/2016
Estimation-Engr. Shehroze Ali
20

## Slide 21: SUPPLEMENTARY AND REVISED ESTIMATE
When a work is partially abandoned and estimated cost of remaining work is less than 95% of original sanctioned estimate.
When there are material deviations and changes in the design
If at any time before or during the execution of work, it is found that original estimate is excessive then divisional officer may sanction a revised estimate of reduced amount.
8/24/2016
Estimation-Engr. Shehroze Ali
21

## Slide 22: ANNUAL REPAIR OR MAINTENANCE ESTIMATE (A.R / A.M ESTIMATE)
It is prepared to maintain structure or work in proper order and safe condition
For buildings like white washing, painting, minor repairs etc.
For road works A.R. estimate provides for patch repairing, repairs of bridges and culverts etc.
8/24/2016
Estimation-Engr. Shehroze Ali
22

## Slide 23
Any Questions?