## Slide 1: CCNA (Exam Code: 640-801)
Todd Lammle
Data and Computer Communications
IP Addressing

## Slide 2: IP Address
A unique identifier assigned to each machine on an IP network
Designates the specific location of a device on a network
A software address

## Slide 3: IP Address MAC Address
Allows a host on one network to communicate with a host on other network
3rd layer address
Software address
Geographical
Hierarchical
IPv4, IPv6
Used for finding hosts on a local network
2nd layer address
Hardware address
Non-geographical
Flat

## Slide 4: Terminologies
Network Address
  Uniquely identifies each network
  Each machine on the same network shares that network address as part of its IP address
  E.g. in 172.16.30.56, 172.16 is the network address
Node / Host Address
  Uniquely identifies each machine on a network
  Each machine on the same network has a unique host address
  E.g. in 172.16.30.56, 30.56 is the host address

## Slide 5: Terminologies
Broadcast Address
  A broadcast address is a logical address at which all devices connected to a multiple-access communication network are enabled to receive datagrams. A message sent to a broadcast address is typically received by all network-attached hosts, rather than by a specific host.

## Slide 6: Classes of IPV4 Addresses
Class A:
  Format
    Network.Host.Host.Host
  Range:
      0000 0000 – 0111 1111
      0 -127
  Number of networks
    27 = 128 (0 -127)
  Number of hosts
    224 -2 = 16,777,216 – 2 = 16,777,214 (All 0’s and all 1’s reserved)
  Valid Host ID’s:
    Network Address: 10.0.0.0
    Broadcast Address: 10.255.255.255
    Valid Hosts: 10.0.0.1 – 10.255.255.254

## Slide 7: Classes of IP Addresses
Class B:
  Format
    Network.Network.Host.Host
  Range:
    10xx xxxx
    From:
      1000 0000 – 1011 1111
      128 -191
  Number of networks
    214 = 16,384
  Number of hosts
    216 -2 = 65536 – 2 = 65534 (All 0’s and all 1’s reserved)
  Valid Host ID’s:
    Network Address: 172.16.0.0
    Broadcast Address:172.16.255.255
    Valid Hosts: 172.16.0.1 – 172.16.255.254

## Slide 8: Classes of IP Addresses
Class C:
  Format
    Network.Network.Network.Host
  Range:
    110x xxxx
    From:
      1100 0000 – 1101 1111
      192 - 223
  Number of networks
    221 = 2,097,152
  Number of hosts
    28 -2 = 256 – 2 = 254 (All 0’s and all 1’s reserved)
  Valid Host ID’s:
    Network Address: 192.168.100.0
    Broadcast Address: 192.168.100.255
    Valid Hosts: 192.168.100.1 – 192.168.100.254

## Slide 9: Classes of IP Addresses
Class D:
  Range
    224 – 239
  Purpose
    Multicast
Class E:
  Range
    240 – 255
  Purpose
    Scientific

## Slide 10: Static and Dynamic IP Address
Static IP Address:
If your IP address at home is static, it means that it will remain the same every time you connect...from home.
Dynamic IP Address:
An IP address that can be changed at any time. This is true but, the fact is, even if you have a dynamic IP address it's possible that it won't change for months on end.
You couldn't set up a reliable server with a changeable IP address. But most of us don't care about that.

## Slide 11: Public and Private IP Address
Public IP Address:
A public IP address is the address that is assigned to a computing device to allow direct access over the Internet. A public IP address is globally unique, and can only be assigned to an unique device.
Private IP Address:
A private IP address is a non-Internet facing IP address on an internal network. Private IP addresses are provided by network devices, such as routers, using network address translation (NAT).

## Slide 12: Public and Private IP Address

## Slide 13: Private IP Addresses
Used on a private work
Not routable through the internet
Advantages:
  Security
  Saves address space
Network Address Translation (NAT)
  Takes a private IP address and converts it for use on the Internet
Reserved Private Addresses
  Class A: 10.0.0.0 - 10.255.255.255
  Class B: 172.16.0.0 – 172.31.255.255
  Class C: 192.168.0.0 – 192.168.255.255

## Slide 14: Broadcast Address
Unicast
  Sent to a single destination host
Layer 2 broadcasts
  Sent to all nodes on a LAN
Broadcast (layer 3)
  Sent to all nodes on the network

## Slide 15: Broadcast Address

## Slide 16: Multicast Address
  Packets sent from a single host and transmitted to many devices on different networks

## Slide 17: Flavors of NAT
Static NAT
  Allows one-to-one mapping between local and global address
  Internal host may be server or network device
Dynamic NAT
  Maps an unregistered IP address to a registered IP address from out of a pool of IP registered addresses
Overloading
  Most popular type
  Maps multiple unregistered addresses to a single registered IP address (many-to-one)

## Slide 18: Flavors of NAT

## Slide 19
Subnetting Network portion increases and bits are borrowed from host. This concept belongs to classless IP addressing
Super-netting IF you increase the host portion by borrowing bits from network then this concept is called supernetting.

## Slide 20: Subnet Mask
Allows the machine to distinguish the network portion and host portion of the IP address.
Subnet Masks of Classes:
  Class A: 255.0.0.0
  Class B: 255.255.0.0
  Class C: 255.255.255.0

## Slide 21: Subnetting: Example 1C:
Subnet the following IP: 192.168.10.0/26
  Network address: 192.168.10.0
  Subnet Mask: 255.255.255.192
No. of subnets
  22 = 4 = 4 subnets
No. of hosts
  26-2 = 62 hosts
Valid subnets
  256-192 = 64, 192.168.10.0/ 64/ 128/ 192
Broadcast address?
Valid subnets?

## Slide 22: Subnetting: Example 1C cont …
Subnets 0 64 128 192
1st host 1 65 129 193
Last host 62 126 190 254
Broadcast 63 127 191 255

## Slide 23: Subnetting: Example 1B:
Subnet the following IP: 172.16.0.0/18
  Network address: 172.16.0.0
  Subnet Mask: 255.255.192.0
No. of subnets
  22 = 4 = 4 subnets
No. of hosts
  214-2 = 16382 hosts
Valid subnets
  256-192 = 64.0, 128.0, 192.0
Broadcast address?
Valid subnets?

## Slide 24: Subnetting: Example 1B cont …
Subnets 0.0 64.0 128.0 192.0
1st host 0.1 64.1 128.1 192.1
Last host 63.254 127.254 191.254 255.254
Broadcast 63.255 127.255 191.255 255.255

## Slide 25: Subnetting: Example 1A:
Subnet the following IP: 10.0.0.0/16
  Network address: 10.0.0.0
  Subnet Mask: 255.255.0.0
No. of subnets
  28 = 256 subnets
No. of hosts
  216-2 = 65534 hosts
Valid subnets
  256-255 = 1.0.0, 10.1.0.0/ 2.0.0/ 3.0.0, etc. up to 255.0.0
Broadcast address?
Valid subnets?

## Slide 26: Subnetting: Example 1A cont …
First two subnets:
  Subnets 10.0.0.0 10.1.0.0 …
  1st host 10.0.0.1 10.1.0.1 …
  Last host 10.0.255.254 10.1.255.254 …
  Broadcast 10.0.255.255 10.1.255.255 …
Last two subnets:
  Subnets 10.254.0.0 10.255.0.0
  1st host 10.254.0.1 10.255.0.1
  Last host 10.254.255.254 10.255.255.254
  Broadcast 10.254.255.255 10.255.255.255

## Slide 27: REVIEW