## Slide 1: Number System

## Slide 2: CONTENTS
Number System
Representation of Numbers of Different Radix
Conversion of Numbers from one Radix to Another Radix
Complement of Number
Binary Arithmetic

## Slide 3: What is Number System ?
A system for representing number of certain type.
Example:
–There are several systems for representing the
–counting numbers.
– These include the usual base “10” or decimal system : 1,2,3
,…..10,11,12,..99,100,…

## Slide 4: Common Number System
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 5: Counting
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 6: Counting
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 7: Conversion Among Bases
Hexadecimal
Decimal
Octal
Binary

## Slide 8: Binary to Octal
Group into 3's starting at least significant symbol (if the number of bits is not evenly divisible by 3, then add 0's at the most significant end)
write 1 octal digit for each group e.g.: (1010101)2 to ( )8
001 | 010 | 101
1 | 2 | 5
Answer = 1258

## Slide 9: Octal to Binary
Answer = (010101111)2
For each of the Octal digit write its binary equivalent e.g.: (257)8 to ( )2
2 5 7
010
101
111

## Slide 10: Binary to Hexadecimal
Group into 4's starting at least significant symbol (if the number of bits is not evenly divisible by 4, then add 0's at the most significant end)
write 1 hex digit for each group. e.g.: (1010111011)2 to ( )16
10 1011 1011
B
2 B
Answer = (2BB)16

## Slide 11: Hexadecimal to Binary
For each of the Hex digit write its binary equivalent (use 4 bits to represent).
e.g.: (25A0)16 to ( )2
2 5 A 0
0010
0101 1010
0000
Answer = (0010010110100000)2

## Slide 12: Octal to Hexadecimal
Steps:
  Convert octal number to its binary equivalent
  Convert binary number to its hexadecimal equivalent e.g.: (635.27)8 to ( )16
6 3 5 . 2 7
110 011 101 . 010 111
000
00
1 | 9 | D | . | 5 | C

## Slide 13: Hexadecimal to Octal
Steps:
  Convert hexadecimal number to its binary equivalent
  Convert binary number to its octal equivalent e.g.:
A | 3 | B . 7
1010 | 0011 | 1011 . 0111
00
5 | 0 | 7 | 3 | . | 3 | 4

## Slide 14: Any Base to Decimal
Converting from any base to decimal is done by multiplying each digit by its weight and summing.
e.g.:
Binary to Decimal
1011.112 = (1x23 ) + (0x22 ) + (1x21 ) + (1x20) + (1x2-1) + (1x2-2)
= 8 + 0 + 2 + 1 + 0.5 + 0.25
= 11.7510

## Slide 15: Decimal to Any Base
Steps:
Convert integer part
( Successive Division Method )
Convert fractional part
( Successive Multiplication Method )

## Slide 16
Steps in Successive Division Method
Divide the integer part of decimal number by desired base number, store quotient (Q) and remainder (R)
Consider quotient as a new decimal number and repeat step1 until quotient becomes 0
List the remainders in the reverse order
Steps in Successive Multiplication Method
Multiply the fractional part of decimal number by desired base number
Record the integer part of product as carry and fractional part as new fractional part
Repeat steps 1 and 2 until fractional part of product becomes 0 or until you have many digits as necessary for your application
Read carries downwards to get desired base number

## Slide 17: e.g.: (125)10 to ( )2
Answer : (1111101)2

## Slide 18: 1’s Complement
The 1’s complement of a binary number is the number that results when we change all 1’s to zeros and the zeros to ones.
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
NOT OPEARATION |  |  |  |  |  |  | 
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1

## Slide 19: 2’s Complement
The 2’s complement the binary number that results when add 1 to the 1’s complement. It’s given as,
2’s complement = 1’s complement + 1
Example: Express 35 in 8-bit 2’s complement form. Solution:
35 in 8-bit form is 00100011
0 0 1 0 0 0 1 1
1 1 0 1 1 1 0 0
+ 1
1 1 0 1 1 1 0 1

## Slide 20: 9’s Complement
The nines' complement of a decimal digit is the number that must be added to it to produce 9. The complement of 3 is 6, the complement of 7 is 2.
Example: Obtain 9’s complement of 7493 Solution:
9 9 9 9
- 7 4 9 3
2 5 0 6
9’s complement

## Slide 21: 10’s Complement
The 10’s complement of the given number is obtained by adding 1 to the 9’s complement. It is given as,
10’s complement = 9’s complement + 1
Example: Obtain 10’s complement of 7493 Solution:
9 9 9 9 |  | 2 5 0 6
- 7 4 9 3 | + | 1
2 5 0 6
2 5 0 7
10’s complement

## Slide 22: Binary Addition
consists of four possible elementary
The addition operations:
Sr no. | Operations
0. | 0+0=0
1. | 0+1=1
2. | 1+0=1
3. | 1+1=10 (0 with carry of 1)
In the last case, sum is of two digits: Higher Significant bit is called Carry and lower significant bit is called Sum.

## Slide 23: Binary Addition
e.g.:
1
+ 0
1
1
0
1
0
0
1 0
0
1 0
Carry

## Slide 24: Binary Subtraction
The subtraction consists of four possible elementary operations:
In case of second operation the minuend bit is smaller than the subtrahend bit, hence 1 is borrowed.
Sr no. | Operations
0. | 0-0=0
1. | 0-1=1(borrow 1)
2. | 1-0=1
3. | 1-1=0

## Slide 25: Binary Subtraction
e.g.:
-
1
0
1
0
1
1

## Slide 26: Binary Multiplication
Rules for Binary Multiplication are:
Sr no. | Operations
0. | 0*0=0
1. | 0*1=0
2. | 1*0=0
3. | 1*1=1
*
e.g.: Multiply 110 by 10
1 1
1
0
0
0 0 0
+ 1 1 0 0
1 1 0 0

## Slide 27: Binary Division
Rules for Binary Division are:
Sr no. | Operations
0. | 0/0=0
1. | 1/0=0
2. | 0/1=0
3. | 1/1=1
e.g.:
Divide 110 by 10
1 1
1 0 1 1 0
1 0
0 1 0
1 0
0 0

## Slide 28: REFERENCES
“Digital Electronics” By A.P.Godse and Dr.D.A.Godse
“Digital Electronics” By A.Anandkumar