## Slide 1: Computer Networks – A Systems Approach
Fourth Edition
Larrie Peterson and Bruce Davie
Internetworking

## Slide 2: Internetworking
What is internetwork
  An arbitrary collection of networks interconnected to provide some sort of host-host to packet delivery service

## Slide 3: A Simple Internetwork

## Slide 4: A Simple Internetwork

## Slide 5: IP Service Model
Packet Delivery Model
  Connectionless model for data delivery
  Best-effort delivery (unreliable service)
    packets are lost
    packets are delivered out of order
    duplicate copies of a packet are delivered
    packets can be delayed for a long time
  if something goes wrong and the packet gets lost, corrupted, misdelivered, or in any way fails to reach its intended destination, the network does nothing

## Slide 6: Packet Format
  Version (4): currently 4
  Hlen (4): number of 32-bit words in header
  TOS (8): type of service (not widely used)
  Length (16): number of bytes in this datagram
  Ident (16): used by fragmentation
  Flags/Offset (16): used by fragmentation
  TTL (8): number of hops this datagram has traveled
  Protocol (8): demux key (TCP=6, UDP=17)
  Checksum (16): of the header only
  DestAddr & SrcAddr (32)

## Slide 7: Fragmentation and Reassembly
Each network technology tends to have its own idea of how large a packet can be
  Ethernet can accept packets up to 1500 bytes long
  FDDI packets may be 4500 bytes long
  ATM (asynchronous transfer mode) has a fixed MTU of 48 bytes
  PPP (point-to-point protocol) has a negotiated MTU that is usually between 500 and 2000 bytes.

## Slide 8: Fragmentation and Reassembly
Two choices for the IP service model:
  Make sure that all IP datagrams are small enough to fit inside one packet on any network technology
  Provide a means by which packets can be fragmented and reassembled when they are too big to go over a given network technology

## Slide 9: Fragmentation and Reassembly
Maximum Transmission Unit (MTU)
  The largest IP datagram that it can carry in a frame
Reasonable Choice of MTU
  MTU of the network to which the host is directly attached

## Slide 10: Fragmentation Related Fields
Length
  Length of IP fragment
Identification
  To match up with other fragments
Flags
  Don’t fragment flag(0)
  More fragments flag(1)
Fragment offset
  Where this fragment lies in entire IP datagram
  Measured in 8 octet units (13 bit field)

## Slide 11: Fragmentation and Reassembly

## Slide 12: Fragmentation and Reassembly

## Slide 13: Fragmentation and Reassembly
Suppose a TCP message that contains 2048 bytes of data and 20 bytes of TCP header is passed to IP for delivery across two networks of the Internet (i.e., from the source host to a router to the destination host). The first network uses 14-byte headers and has an MTU of 1024 bytes; the second uses 8-byte headers with an MTU of 512 bytes. Each network’s MTU gives the size of the largest IP datagram that can be carried in a link-layer frame. Give the sizes and offsets of the sequence of fragments delivered to the network layer at the destination host. Assume all IP headers are 20 bytes.

## Slide 14: Fragmentation and Reassembly

## Slide 15: Routing
Forwarding versus Routing
  Forwarding
    to select an output port based on destination address and routing table
  Routing
    process by which routing table is built
  Forwarding table VS Routing table
  Forwarding table
    Used when a packet is being forwarded and so must contain enough information to accomplish the forwarding function
    A row in the forwarding table contains the mapping from a network number to an outgoing interface and some MAC information, such as Ethernet Address of the next hop
  Routing table
    Built by the routing algorithm as a precursor to build the forwarding table
    Generally contains mapping from network numbers to next hops

## Slide 16: Routing Table / Forwarding Table

## Slide 17: Routing Protocols
Dynamic Routing
Intradomain
(IGP)
Interdomain
(EGP)
Link State
Distance Vector
RIP
IGRP
OSPF
BGP
Routing
Static Routing
Hybrid
EIGRP

## Slide 18: Network as a Graph
The basic problem of routing is to find the lowest-cost path between any two nodes
Where the cost of a path equals the sum of the costs of all the edges that make up the path

## Slide 19: Network as a Graph
For a simple network, we can calculate all shortest paths and load them into some nonvolatile storage on each node.
Such a static approach has several shortcomings
  It does not deal with node or link failures
  It does not consider the addition of new nodes or links
  It implies that edge costs cannot change
What is the solution?
  Need a distributed and dynamic protocol
  Two main classes of protocols
    Distance Vector
    Link State

## Slide 20: Distance Vector
Also known as Bellman-Ford Algorithm
Each node constructs a one dimensional array (a vector) containing the “distances” (costs) to all other nodes and distributes that vector to its immediate neighbors
Starting assumption is that each node knows the cost of the link to each of its directly connected neighbors

## Slide 21: Distance Vector
Initial distances stored at each node (global view)

## Slide 22: Distance Vector
Initial routing table at node A

## Slide 23: Distance Vector
Final routing table at node A

## Slide 24: Distance Vector
Final distances stored at each node (global view)

## Slide 25: Distance Vector
Convergence
  The process of getting consistent routing information to all the nodes
Two different circumstances under which a given node decides to send a routing update to its neighbors
  Periodic Update
    each node automatically sends an update message after some time
    serves to let the other nodes know that this node is still running
    frequency of these periodic updates varies from protocol to protocol
  Triggered Update
    node receives an update from one of its neighbors that causes it to change one of the routes in its routing table

## Slide 26: Distance Vector
When a node detects a link failure
  F detects that link to G has failed
  F sets distance to G to infinity and sends update to A
  A sets distance to G to infinity since it uses F to reach G
  A receives periodic update from C with 2-hop path to G
  A sets distance to G to 3 and sends update to F
  F decides it can reach G in 4 hops via A

## Slide 27: Distance Vector
Slightly different circumstances can prevent the network from stabilizing
  Suppose the link from A to E goes down
  In the next round of updates, A advertises a distance of infinity to E, but B and C advertise a distance of 2 to E

## Slide 28: Distance Vector
  Depending on the exact timing of events, the following might happen
    Node B, upon hearing that E can be reached in 2 hops from C, concludes that it can reach E in 3 hops and advertises this to A
    Node A concludes that it can reach E in 4 hops and advertises this to C
    Node C concludes that it can
    reach E in 5 hops; and so on.
    This cycle stops only when the
    distances reach some number
    that is large enough to be considered
    infinite
      Count-to-Infinity Problem

## Slide 29: Count-to-infinity Problem
Use some relatively small number as an approximation of infinity
  For example, the maximum number of hops to get across a certain network is never going to be more than 16
Split horizon
  When a node sends a routing update to its neighbors, it does not send those routes it learned from each neighbor back to that neighbor
  For example, if B has the route (E, 2, A) in its table, then it knows it must have learned this route from A, and so whenever B sends a routing update to A, it does not include the route (E, 2) in that update

## Slide 30: Count-to-infinity Problem
Split horizon with poison reverse
  B actually sends that back route to A, but it puts negative information in the route to ensure that A will not eventually use B to get to E
  For example, B sends the route (E, ∞) to A