## Slide 1: Supercritical Fluid Extraction(SCFE) and Supercritical Fluid Chromatography (SCFC)
Part 1: SCFE
Part11: SCFC

## Slide 2: PART I : SCFE

## Slide 3: What are Supercritical Fluids?
A supercritical fluid is the phase of a material at critical temperature and critical pressure of the material
At temperature and pressure above critical point (CP), a single homogenous fluid is formed, which is known as SCF. SCF is heavy like liquid but has penetration power like gas.
A supercritical fluid is a material that can be either liquid or gas used in state above critical temperature or critical
pressure where gases or liquid can co exist
SCF properties are in between a gas and a liquid. They have dual nature!
Supercritical fluid have a viscosity close to gases a density close liquids and a high diffusivity

## Slide 4: Phase diagram
The motion of the molecules are quite similar to gas molecules. On the other hand, a supercritical fluid behaves like a liquid because its density property is near liquid and, thus, a supercritical fluid shows a similarity to the dissolving effect of a liquid

## Slide 5: SC-CO2: A Good Choice as SCF
Supercritical CO2 is most
commonly used solvent
because of its :-
1. Low critical parameters (31.1 º C
,73.8 bar)
2. Low cost
3. Non- toxic/GRAS nature
Their has to use of SCF- grade
CO2 because it is free from
water, hydrocarbons and
halocarbons. ( As cryogenic
CO2 grade is not pure)
Apart from CO2 other super
critical fluids can be seen in table

## Slide 6: SCFE : A green Extraction Technique
SCFE can be used to extract bioactive ingredients or analytes from various plants and natural products
An Eco-friendly technique- uses SC –CO2 as extraction media
Optimization of temperature and pressure of the fluid can solubilize the material of interest and offers selective extras
Modifier can be added (1-10%) to tune polarity of SC –CO2 for various applications

## Slide 7
Why Use of MODIFIERS?
Modifiers- These are highly polar solvents which are added in small volumes exert significant changes in the properties. Of SCF
Supercritical CO2 because of its low polarity is less effective in extracting more polar compounds
To overcome this problem, modifiers ( also called co-solvents) are added
Common modifier are methanol and ethanol which can be typically added with contribution of 1-10%; this addition of modifier increases the polarity of supercritical C02

## Slide 8: Advantages of SCFE over CSE
Selectively Controllable
Eco-friendly
Inexpensive
Less costly to dispose safely than organic solvents.
Contaminant free
Oxidative and thermal degradation of active compounds is much less likely in SFE than in conventional solvent extraction(CSE) and steam

## Slide 9
Sustainable process with higher efficacy and extraction yield
Safer
Avoids thermal degradation of natural compounds
Offer food grade products/extracts
Fast and non-pathogenic extraction
Versatile applications due to control on pressure and adding the modifiers

## Slide 10: Schematic Diagram of SCFE

## Slide 12: PARTS OF SFE
SOLVENT PUMP- Solvent pump or CO2 pump delivers the fluid throughout
the system.
EXTRACTION CELL OR COLUMN- It is made up of stainless steel to
withstand high pressure with compression and fitting. Generally size of
extraction cell ranges from 50-100 mL .The extraction cell is usually in an
oven to control the temperature because any fluctuation in the temperature
results in the change in SFE density and solvating property.
FRACTINATION CELLS/SEPARATOR- Also know as separators, they can be one or more
separators in which extracts are collected and the solvent is depressurized.
VALVES- Helps in controlling process pressure, pumps flow rate, the chiller,
the boiler and temperature in every section .
Refrigerated system – It is along with the trapping vessel designed to
trap the most volatile compounds.
Recycling system- Recycle the SCF which have been employed.

## Slide 13: Working!
The sample is placed in an extraction vessel and pressurized with SCF CO2 to dissolve the sample.
After extraction the extract is transferred to the fraction chamber and depressurized due to which CO2 loses its solvating power causing entire material to precipitate.
Now the CO2 gets recycled . Precipitated material is extracted with addition of small amount of solvents.

## Slide 14: Applications
SFE can be used in industries for the extraction of various products of commercial importance, especially from plant materials such as Coffee, Hpos, Tea and Spices etc.
Extraction of antioxidants/ antimicrobial agents from medicinal plants
Extraction of Flavanoids - Quercetin from Onion skins, Epicatechin from sea coat of sweet Thai tamarind, ginkgolides from ginkgo leaves
Extraction of essential oils from plant materials/spices and herbs

## Slide 15
Extraction of High-value vegetable oils such as flax seed and hemp seed oil
Purification and denacotation
Extraction of pesticides fro food and different agricultural crops`

## Slide 16
Part II- SCFC

## Slide 17: Introduction
Most important feature of SCFC is that a SCF is used as a mobile phase instead of a liquid or gas for the purposes of chemical separations
Supercritical fluid chromatography is accepted as a column chromatography methods along with gas
chromatography (GC) and high-performance
liquid chromatography (HPLC).
Due to the properties of supercritical fluids, SFC combines each of the advantages of both GC and HPLC in one method

## Slide 18
Supercritical fluids combine the benefits of liquids and gases, SFC bring the advantages and can be use din HPLC and GC together.
SFC can be more advantageous than HPLC and GC when compounds which decompose at high temperatures with GC and do not have functional groups to be detected by HPLC detection systems are analyzed.

## Slide 19
In SFC Sample is carried through a separating column by an SFC fluid where mixture is separated in stationary phase in the column.
As the compounds leave columns there identities and quantities are determined by detector.
• SFC TEMPERATURE : For every substance there is a
temperature above which it can no longer exist as a liquid no matter how much pressure is applied.
• SFC PRESSURE : For every substance there is a pressure
above which it can no longer exist as a liquid no matter how high temperature is raised.

## Slide 20: Principle
Principles of SCFC are similar to those of High Performance Liquid Chromatography (HPLC), however SFC typically utilizes carbon dioxide as the mobile phase
Supercritical phase represents a state in which liquid and gas properties converge, supercritical fluid chromatography is sometimes called "convergence chromatography

## Slide 21
Instrumentation
SFC has a similar instrumental setup to an HPLC instrument. They use similar stationary phases with similar column types. However, there are some differences.
Temperature is critical for supercritical fluids, so there should be a heat control tool in the system similar to that of GC. Also, there should be a pressure control mechanism, a restrictor, because pressure is another essential parameter in order for supercritical fluid materials to be kept at the required level.
A microprocessor mechanism is placed in the instrument for SFC. This unit collects data for pressure, oven temperature, and detector performance to control the related pieces of the instrument.

## Slide 22: Instrumental Parts
Mobile Phase System/mobile Phase
Pumps
Injectors
Oven
Column
Detector
Restrictor

## Slide 24
Pumps:
Flow controlling is the vital function of pumping systems.
Reciprocating pumps allow easier mixing of mobile phase or introduction of modifier fluids.
Syringe pumps provide consistent pressure for neat mobile
phase.

## Slide 25
Oven: A thermostated column oven is required for precise temperature control of the mobile phase. Conventional GC or LC ovens are generally used.
Back – Pressure Device or Restrictor
This device is used to maintain required pressure in the column by pressure adjustable diaphragm /controlled nozzle, so as to maintain same column outlet pressure irrespective of mobile phase pump flow rate.
Pressure restriction is placed either at the end of the column or after detector.

## Slide 26
Injectors:
Purposes of this device is to inject the sample. There are different sample injector that can be employed.
For Packed SFC a conventional HPLC injection system can be used, However, for a capillary column SFC, very small volume to be injected must be quickly injected into column.
Following pneumatically driven sample injection options can be used for capillary column such as LOOP INJECTORS, INLINE INJECTION and INCOLOUMN INJECTION

## Slide 27
Loop Injector
In Line Injector
In column injector

## Slide 28
Columns:
Once the sample is injected into supercritical stream, it is carried into the analytical column that contains a highly viscous liquid (stationary phase)
There are two types of analytical columns used in SCFC :
Packed columns are packed with small deactivated particles so which the stationary phases adheres the columns are conventionally stainless steel
B) Capillary columns/ open tubular columns: are of narrow internal diameter made of fused silica with the stationary phase bonded to the wall of the column

## Slide 29
SFC columns are similar to HPLC columns in terms of coating materials.
Open-tubular columns and packed columns are the two most common types used in SFC.
Open-tubular ones are preferred and they have similarities to HPLC fused-silica columns. This type of column contains an internal coating of a cross-linked siloxane material as a stationary phase.

## Slide 30
Stationary Phases:
•These are same as those used for GC & LC with slight modifications.
Silica / Alumina
• Useful for nonpolar compounds.
• Lead to irreversible adsorption of some polar solutes.
• Need organic modifiers to elute analytes
Non polar stationary phase:
• POLYSILOXANE – Stable, Flexible, Si-O bond leads to
good diffusion.
• POLYMETHYL SILOXANES – Increase efficiency in
separating closed related analytes.

## Slide 31
Mobile Phase System:
• Some of the features such as cost, compatibility with detector,
detectors and other properties e.g., nontoxic
nature, nonflammable, low critical values etc. are considered during selection of mobile phase.
Carbondioxide (CO2): is the best choice which meets most of above properties. It is safe to use /nontoxic , nonflammable , noncorrosive, and inert. The main disadvantage of using CO2 is its less polar nature so polar or ionic compounds are difficult to be eluted. This can be overcome by adding a small portion of a modifier .
Use of Modifier:
A small portion of a modifier (co-solvent, mostly a polar organic solvent completely miscible with CO2 such as alchols, cyclic ethers) is added to improve solvating ability of supercritical fluid and sometimes it enhances selectivity of separation efficiency by blocking some of the highly active sites on the stationary phase.

## Slide 32
Other SFC solvents
• Nitrous oxide :- Similar in solvating and
separation efficiency to CO2 but it is expensive and not safe
• Alkanes- Less safe and not detector compatible as CO2- better solvent characteristics for nonpolar solutes.
• Halocarbons , xenon etc. - Specialty applications only
More polar solvents for highly polar and high molecular weight compounds.

## Slide 33
Detectors
These are devices which detect signal and provide response in the form of peak. A range of detectors are available:
Choice depends upon:
Mobile phase composition
Column type
Flow rate
Ability to withstand high pressure of SFC.
SCFC system is compatible with both HPLC and GC detectors.
Flame ionization Process (FID)
Liquid phase detectors like RID, Ultra violet – Visible
Spectrophotometric detector and Light Scattering
detectors have been employed for SFC.

## Slide 34: Advantages and Disadvantages of SCFC
Advantages:
Favorable combination of process steps
Capability of both HPLC and GC
Improved resolution
Lower operating temperatures.
High resolution at lower temperature.
Easier regeneration of supercritical solvent
Improved product properties
Lower product cost
Low Viscosity of SCF
Very high volatility compared to dissolved substance
Provide rapid separation without use of organic solvents.
Uses environmentally conscious technology.
High diffusion coefficient/power
Enhance solubility of polar analyte
Reduce retention volume.
Eliminate strong interaction between adsorptive site and polar site
Will modify polarity of diluent
CO2 – Ideal to satisfy all properties
Safe to use
Nontoxic
Non flammable
Non corrosive
Detector compatible.

## Slide 35
Disadvantages:
Relatively higher capital cost of equipment
Elevated pressures is involved and unusual operating conditions
• Complicated phase separation behavior
Expensive technology
Cleaning time consuming
• Very polar or ionic not able to be eluted.
Can overcome by adding small portion of scanned fluid called
modifier fluid (Alcohols, cyclic ethers, acetonitrile, chloroform).

## Slide 36
Applications of SCFC
PESTICIDES pesticide residues in different foods and crops
NATURAL PRODUCTS :
• Analysis of natural products such a s vegetable oils, essential oils, carotenoids, alkaloids and other bioactive compounds
LIPIDS :
phospholipids after conversion to diacylglycerol derivatives, fatty acids, methyl esters, biosynthetic poly unsaturated fatty acids (PUFA), non saponifiable lipids, cholesterol and its esters :
SURFACTANTS:
Separation of the oligomers in sample of nonionic surfactant triton X 100
DRUGS:
Separation of various drugs such as sedatives, analgesics, narcotics, stimulants, antidepressants , phenothiazines, antipsychotic, beta blockers etc. In SFC conditions are mild and no volatilization is required, therefore it is a good choice than any existing method.
•

## Slide 37
Thank You