## Slide 1
Presented to: Dr. Imtiaz Hussain
Topic: Transmission of electron microscope

## Slide 2
WORKING
APPLICATION
SUMMARY
INTRODUCTION
PRINCIPLE
INSTRUMENT
CONTENTS

## Slide 3: Transmission Electron
INTRODUCTION
In 1931, while conducting research for his masters at the technical college of Berlin, Ernst Ruska and Max Knoll designed first TEM.
This is much like a slide projector but the basic difference is light microscope uses Beam of Light whereas TEM uses Beam of electron.
TEM is a microscopy technique in which a beam
of electrons is transmitted through an ultra thin
specimen, interacting with the specimen as it passes through.

## Slide 4
What is a Transmission Electron Microscope
(TEM)?
Electrons pass through a (very thin) sample (i.e. are transmitted) to form an image.
Simplistically, In its operation a TEM can be thought of as analogous to a slide projector:-

## Slide 5: Principle
TEM operates on the same basic principles as the light microscope but uses electrons instead of light. Since, light microscope is limited by the wavelength of light. TEMs use electrons as a “light source” and their much lower wavelength makes it possible to get a resolution a 1000 times better than with a light microscope

## Slide 7: INSTRUMENT
INSTRUMENT

## Slide 8: Main components of a TEM
The TEM can be broken down into a few main components, these are:-
The Gun – which produces electrons.
The condenser system – which forms the probe.
The sample – sample preparation is important, and time consuming.
Image formation – use of image plane or back focal plane.
Intermediate lens- transmitting and magnifying the first enlarged
diffraction or image pattern to projector lens. Projection of the image (magnification), viewing and recording.

## Slide 10: WORKING
In a TEM the electron beam is focused on the sample using the condenser lens system.
This produces an image which is focused by the objective lens to a point .
This image is then magnified by a series of projector lenses to vary the size of the image on a fluorescent screen.
Changing the current of an electromagnetic lens alters its focal length altering magnification

## Slide 11: Applications of TEM On industrial basis:
A Transmission Electron Microscope is ideal for a number of different fields such as life sciences, nanotechnology, medical, biological and material research, forensic analysis, gemology and metallurgy as well as industry and education.
TEMs can be used in semiconductor analysis and production and the manufacturing of computer and silicon chips.

## Slide 12
Technology companies use TEMs to identify flaws, fractures and damages to micro sized objects; this data can help fix problems and/or help to make a more durable, efficient product.

## Slide 13: For education purpose:
Colleges and universities can utilize TEMs for research and studies.
Although electron microscopes require specialized training, students can assist professors and learn TEM techniques. Students will have the opportunity to observe a nano sized world in incredible depth and detail

## Slide 14: SUMMARY
Advantages of TEM
A Transmission Electron Microscope is an impressive instrument with a number of advantages such as:
TEMs offer the most powerful magnification, potentially over one million times or more
TEMs have a wide range of applications and can be utilized in a variety of different scientific, educational and industrial fields

## Slide 15
TEMs provide information on element and compound structure
Images are high quality and detailed

## Slide 16
Disadvantages of TEM
TEMs are large and very expensive
Laborious sample preparation
Operation and analysis requires special training
Samples are limited to those that are electron transparent, able to tolerate the vacuum chamber and small enough to fit in the chamber
TEMs require special housing and maintenance
Images are black and white.

## Slide 17: Thank you!