## Slide 1: Structural Engineering Lec#3
Engr. Muhammad Mubashir Ajmal
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 2
Text Book
“Structural Analysis” by R.C. Hibbeler
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 3: List of Content
Bridge Engineering
Department of Civil Engineering, University of Sargodha, Sargodha
Structural Engineering

## Slide 4: Introduction
Bridges are defined as structures which provide a connection or passage over a gap without blocking the opening or passageway beneath.
They can be over streams, canals, rivers, creeks and valleys or roads and railways passing beneath.
Bridges are now being provided across ocean bodies and for linking a number of islands as in Japan.
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 5: Introduction
Department of Civil Engineering, University of Sargodha, Sargodha
World’s longest sea crossing: Hong Kong-Zhuhai bridge having spans 55 Km

## Slide 6: Introduction
The bridge crossing carrying a road or railway over another road or railway is called a grade separator or fly over.
The bridge structure can be for passage/carriage of persons, cattle, vehicles, water or other material carried across in pipes or conveyors.
When they are used for carriage of water, they are called aqueducts
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 7: Introduction
Department of Civil Engineering, University of Sargodha, Sargodha
Magdeburg Water Bridge, the World’s Longest Navigable Aqueduct (918 m)

## Slide 8: Components of Bridge
Superstructure:
This includes slab, girder, truss etc.
This is also called as decking.
This bears the load passing over it and transmits the forces caused by the same to the substructure
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 9: Components of Bridge
Bearings:
The bearings transmit the load received from the decking on to the substrurcture and are provided for distribution of the load evenly over the substructure material.
These also allow for longitudinal movement of girders due to longitudinal forces of moving loads and temperature variation
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 10: Components of Bridge
Substructure:
Piers and Abutments:
  These are vertical structures supporting deck/bearing provided for transmitting the load down to the bed/earth through foundation.
  Abutment, in addition retain earth behind.
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 11: Components of Bridge
Substructure:
Wing walls and Returns:
  These are provided as extension of the abutments to retain the earth of approach bank which otherwise has a natural angle of repose
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 12: Components of Bridge
Substructure:
Foundation:
  This is provided to transmit the load from the piers or abutments and wings or returns to the strata
  This is to be provided sufficiently deep so that it is not affected by the scour cased by the flow in the river
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 13: Components of Bridge
Department of Civil Engineering, University of Sargodha, Sargodha
Components of a bridge

## Slide 14: Classification of Bridges
There are many ways of classification of bridges and the different considerations on which they can be classified are:
  Material of construction
  Form of superstructure
  Types of span
  Position of roadway or railway w.r.t. main girder
  Headway requirement
  Permanent or temporary nature
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 15: Classification of Bridges
Materials for Construction:
Timber
Iron and steel
  Pin-jointed
  Rivetted
  Bolted
  welded
Concrete
  Reinforced concrete
  Prestressed concrete
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 16: Classification of Bridges
Form of Superstructure:
Arches (steel arches up to 500m and concrete arches up to 300 m)
Slabs (up to 9 m)
Girders (10 to 60 m)
Trusses (30 to 375m simply supported)
Suspension (500 to 2000 m)
Cable-stayed bridges (300 to 600 m)
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 17: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Arch Bridge

## Slide 18: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Arch Bridge

## Slide 19: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Slab Bridge

## Slide 20: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Slab Bridge

## Slide 21: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Girder Bridge

## Slide 22: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Girder Bridge

## Slide 23: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Truss Bridge

## Slide 24: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Truss Bridge

## Slide 25: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Suspension Bridge

## Slide 26: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Suspension Bridge

## Slide 27: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Cable-Strayed Bridge

## Slide 28: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Cable-Strayed Bridge

## Slide 29: Classification of Bridges
Classification by Types of Span:
Small Span (up to 15m)
Medium Span (up to 50m)
Large Span (up to 150m)
Extra Large Span (over 150m)
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 30: Classification of Bridges
Position of Roadway/Railway w.r.t. Main Girders:
Main structure below the deck line
Main structure above the deck line
Main structure coincides with the deck line
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 31: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Main structure below the deck line

## Slide 32: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Main structure above the deck line

## Slide 33: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Main structure coincides the deck line

## Slide 34: Classification of Bridges
Clearance Requirement Consideration:
Normally bridges have to be provided in such a way that they are clear of the high flood level
Where there is navigation, the bottom of the superstructure has to be kept sufficiently high to permit the boats and ships to pass under
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 35: Classification of Bridges
Causeway:
  It may be found that in some cases the high flood in the stream is occasional and the normal flow is very little or the bed is dry most of the time
  In such cases, causeways are provided which are nothing but a paved road formed between retaining walls on either sides.
Submersible Bridge:
  A submersible bridge is a type of movable bridge that lowers the bridge deck below the water level to permit waterborne traffic to use the waterway.
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 36: Classification of Bridges
Department of Civil Engineering, University of Sargodha, Sargodha
Submersible Bridge

## Slide 37: Classification of Bridges
High Level Bridges:
  These are provided in such a way that they can pass the design flood discharge with sufficient head room.
  There may be cases where ships may have to pass through them requiring very high clearance
Department of Civil Engineering, University of Sargodha, Sargodha

## Slide 38
Department of Civil Engineering, University of Sargodha, Sargodha