## Slide 1: Reclamation and management of saline soils

## Slide 2: Reclamation of Saline soil
Removal of excess salt by good quality irrigation water: Ponding and intermittent ponding is more efficient in leaching of salts. For the success of leaching water table must be sufficiently low
Drainage of the soluble salts at surface and subsurface region Surface drainage is for draining of excess run off Subsurface drainage for lowering the water table
Proper water mangement of cropping system are important for crop production

## Slide 3: Salt Balance
The salt balance compares the movement of dissolved salts into and out of an area over a specified period of time. While flushing care must be taken so that the salt balance becomes always positive. In this background a term is used which is known as Leaching Requirement (LR).
“The ratio of the amount of drainage water, percolating from the root zone of an irrigated field, and the amount of water entering the root zone as irrigation and rainfall.”

## Slide 4
20
15
10
5
0
Jan
Feb
March
April
May
June
July
Aug
Sept
Oct
Nov
Dec
Soil salinity (ECe, dS/m)
Variation in soil salinity in different months of the year

## Slide 5
Integrated management practices for the reclamation of salt-affected soils.

## Slide 6
Soil Management:
Maintenance of satisfactory fertility levels, pH and structure of soils to encourage growth of high yielding crops
Maximization of soil surface cover, e.g. use of multiple crop species
Mulching exposed ground to help retain soil moisture and reduce erosion
Crop selection, e.g. use of deep-rooted plants to maximise water extraction
Using crop rotation, minimum tillage, minimum fallow periods
Management strategies for combating SALINIZATION

## Slide 7
Water Management:
Efficient irrigation of crops: soil moisture monitoring and accurate determination of water requirements
Choice of appropriate drainage according to the situation:\
  Surface drainage systems to collect and control water entering and/or leaving the irrigation site
  Subsurface drainage systems to control a shallow water table below the crop root zone
  Biodrainage the use of vegetation to control water fluxes in the landscape through evapo-transpiration
Adequate disposal of drainage water to avoid contamination of receiving waters and the environment

## Slide 8
Removal of soluble salts from the root zone
Scraping: Removing the salts that have accumulated on the soil surface by mechanical means
Flushing: Washing away the surface accumulated salts by flushing water over the surface is sometimes used to desalinize soils having surface salt crusts.

## Slide 9
Leaching:
This is by far the most effective procedure for removing salts from the root zone of soils.
Leaching is most often accomplished by ponding fresh water on the soil surface and allowing it to infiltrate.
Leaching is effective when the salty drainage water is discharged through subsurface drains that carry the leached salts out of the area under reclamation.
Leaching may reduce salinity levels in the absence of artificial drains when there is sufficient natural drainage, i.e. the ponded water drains without raising the water table.
Leaching should preferably be done when the soil moisture content is low and the groundwater table is deep.
Leaching is best accomplished during the summer months because this is the time when the water table is deepest and the soil is dry. This is also the only time when large quantities of fresh water can be diverted for reclamation purposes.

## Slide 10: Various management practices based on reducing the salt zone for seed germination and seedling establishment
Early seedling establishment and tillering phase: The most sensitive stages to salinity
Any management practice that could provide an environment of reduced salt concentration during these stages would mitigate the salinity effects
Promotion of plant density

## Slide 11
1: Scraping and removal of surface soil:
Due to continuous evaporation the salt concentration is the highest in the surface soil. The top soil can be scraped and transported out of the field.
2: Pre-sowing irrigation with good quality water:
Where available, irrigation with good quality water prior to sowing helps leach salts from the top soil. This helps in promoting better seed germination and seedling establishment.
Techniques

## Slide 12
3. Appropriate use of ridges or beds for planting:
The impact of salinity may be minimized by appropriately placing the seeds (or plants) on ridges
Where exactly the seeds should be planted on the ridge or bed will depend on the irrigation design
If the crop planted on ridges would be irrigated via furrows on both sides of the ridge, it is better to place plants on the ridge shoulders rather than the ridge top because water evaporation will concentrate more salts on the ridge top or center of the bed
If the crop is irrigated via alternate furrows, then it is better to plant only on one shoulder of the ridge closer to the furrow that will have water

## Slide 13: Sloping beds may be slightly better on highly saline soils because seed can be planted on the slope below the zone of salt accumulation.
Microtopography of ridge and furrow systems designed to avoid salinity damage to crops: (a) paired crop rows on broadly sloping ridges
(b) single crop rows on asymmetric ridges

## Slide 14: Certain modifications of the furrow irrigation method including planting in single/double rows or on sloping beds, are helpful in getting better stands under saline conditions. With double beds, most of the salts accumulate in the centre of the bed leaving the edges relatively free of salts.
The pattern of salt built up depends on bed shape and irrigation method. Seeds sprout only when they are placed so as to avoid excessive salt build up around them

## Slide 15
Pattern of salt build-up as a function of seed placement, bed shape and irrigation water quality.

## Slide 16
In addition to the management practices mentioned above, the following approaches may help reduce salinity impacts
  Mulching:
Mulching with crop residue, such as straw reduces evaporation from the soil surface
This in turn reduces the upward movement of salts
Reduced evaporation also reduces the need to irrigate. Consequently fewer salts accumulate
  Deep Tillage:
Accumulation of salts closer to the surface is a typical feature of saline soils
Deep tillage would mix the salts present in the surface zone into a much larger volume of soil and hence reduce its concentration and impact
Many soils have an impervious hard pan which hinders in the salt leaching process.
Under such circumstances “chiseling” would improve water infiltration and hence downward movement of salts.
General management practices to reduce the impact of soil salinity on crop performance

## Slide 17
Incorporation of Organic matter
Incorporating crop residues or green-manure crops improves soil tilth, structure, and improves water infiltration
Provides safeguard against adverse effects of salinity
In order for this to be effective, regular additions of organic matter (crop residue, manure, sludge, compost) must be made.

## Slide 18: Conservative farming practices to control soil salinity
Reducing summer fallow
Using conservative tillage
Adding organic matter to the soil
Planting salt-tolerant crops (eg., rapeseed and cabbage)

## Slide 19: Irrigation reduces salinity
Sweet water (SW)
Soil saturated with sweet water
No upward movement of brackish water
Reduce effect of degradation due to land shaping
Upward movement of SW

## Slide 20: Proposed land shaping technologies
e) Land shaping for growing vegetables round the year (high to medium land)
Bitter gourd (kharif)
Beans (kharif)

## Slide 21: Tolerance of some crops to saline conditions. Salinity expressed as EC.
Brady, N.C., 2002, The Nature and Properties of Soils, New Jersey, USA, Prentice Hall.