## Slide 1: Subnetting

## Slide 2: Subnetting Basics
There are lots of reasons in favor of subnetting, including the following benefits:
  Reduced network traffic
  Optimized network performance
  Simplified management
  Facilitated spanning of large geographical distances

## Slide 3: How to Create Subnets
To create sub networks, you take bits from the host portion of the IP address and reserve them to define the subnet address

## Slide 4: Steps to create subnets
Determine the number of required network IDs:
  One for each LAN subnet
  One for each wide area network connection
Determine the number of required host IDs per subnet:
  One for each TCP/IP host
  One for each router interface
Based on the above requirements, create the following:
  One subnet mask for your entire network
  A unique subnet ID for each physical segment
  A range of host IDs for each subnet

## Slide 5: Subnet Mask
Subnet mask is 32-bit number that masks an IP address
Subnet mask separates the IP address into the network and host address
Subnet mask is made by setting network bits to all 1’s and setting all host bits to all 0’s
Two addresses are reserved “0” address assigned to network address and “255” is assigned to broadcast address

## Slide 6: Subnetting Class C IP addresses
In class-C only 8-bits are available for defining the hosts
How many subnets does the chosen subnet mask produce?
How many valid hosts per subnet are available?
What are the valid subnets?
What’s the broadcast address of each subnet?
What are the valid hosts in each subnet?

## Slide 7: Subnetting Class C IP addresses
2X x is the number of masked bits or the 1’s
2. For example 11000000
  The no. of 1’s gives us 22 subnets, there are 4 subnets
3. How many hosts per subnet
  2y – 2= no. of hosts per subnet
  y is the no. of unmasked bits or 0’s
4. 11000000, 26 – 2, in this there are 62 hosts per subnet
5. Valid subnet ? Block size = 256 – subnet mask
6. For example 256 – 192 = 64, the block size of a 192 mask is always 64

## Slide 8: Subnetting of Class-C

## Slide 9: Subnetting of Class-C

## Slide 10: Subnetting of Class-B IP addresses

## Slide 11: Example # 02

## Slide 12: Example 03

## Slide 13: Example 04

## Slide 14: Example 05

## Slide 15: Example 06