## Slide 2: Routing Protocol
(Static and Dynamic)

## Slide 3: What is Routing?
Define route.
Selection of the best path.

## Slide 4: Types of Routing
Static Routing.
Dynamic Routing.

## Slide 5: Static Routing
Is the process in which the system network administrator would manually configure network routers with all the information necessary for successful packet forwarding

## Slide 6: Recursive Static routing
With a recursive static route the next hop IP address is specified.
Example: #ip route( Network Address) (Subnet Mask ) (ip address)

## Slide 7: 2. Directly connected static route
With a directly connected static route ,the exit interface parameter is specified
Example: #Ip route (network address) (subnet mask) (exit interface)

## Slide 8: 2. Dynamic Routing
Selection of best path through any protocol and fill the routing table

## Slide 9: Routing Table
A routing table contains the information necessary to forward a packet along the best path toward its destination.

## Slide 10
Destination: The IP address of the packet's final destination
Next hop: The IP address to which the packet is forwarded
Interface: The outgoing network interface the device should use when forwarding the packet to the next hop or final destination
Metric: Assigns a cost to each available route so that the most cost-effective path can be chosen
A basic routing table includes the following information

## Slide 11
Routing Protocol
IGP
EGP

## Slide 12: Routing Protocol’s

## Slide 13: Distance vector
In distance vector routing each nods share its routing table with its immediate neighbor periodically and when there is a change

## Slide 14: Difference b/w RIP and OSPF
Algorithm Distance Vector Bellman Ford.
Routing updates are broadcast.
Its broadcast address is 255.255.255.255
Its AD value are120
Repeat routing updates every 30 second. It is UDP base (transport)
Rip is design for a small AS Its include 15 hope count.
It is design for class full network
Rip v2 support both class full and classless
RIP is an IGP(Interior Gateway Protocol)
Algorithm link state Dijkstra Algorithm.
It is multicast protocol.
Its multicast address is 224.0.0.5.
Its AD value is110
Repeats routing updates every 10 second it is UDP base (transport)
is design for large size topology.
Its support class full and classless routing.
RIP is an IGP(Interior Gateway Protocol)