## Slide 1
Culture Facilities

## Slide 2: NEED OF LOW CAST LAB.
Low cost options should lower the cost of production
micro-
without compromising the quality of the propagation and plants.
Micro propagation technique is too much costly.
Potential increasing interest in agricultural crop
production increased.
Low-cost tissue-culture technology will stay a high priority in agriculture, horticulture, forestry, and floriculture of many developing countries for the production of suitably priced high quality planting material.

## Slide 3
GENERAL REQUIREMENT
FOR SET UP
A LOW COST LABORATIRY

## Slide 5: LOCATION
The location shall confirm to the land use plan of the area.
The building should be located away from sources of contamination such as soil mixing area, storage etc.
The site shall be accessible to service roads, water supply and electric lines.
The site shall be well drained.

## Slide 6: STRUCTURAL REQUIREMENT
The roof structure should be treated timber or steel with anti-rust
paint. Roof vents, when provided, shall be properly screened.
Ceilings shall be at least 2.4 m from the finished floor line and painted with latex paint and should be prevent from dust.
The wall shall be concreted, smooth finished and properly painted
with anti-fungal- epoxic-paints and slope shall be at 450c
All windows shall be properly installed with 16-mesh screen and at least 1 m from the finish floor line.
Main door ways shall be at least 1.5 m wide and moisture and rust- resistant material..
Floor shall be concreted, smooth, non-skid, slope 2% -4% towards
the drain.

## Slide 7: THE BASIC FACILITIES OF LABORATORES
For Keeping
One Room With Computer With Locker Apron
Working Place
Layout Of Plant Tissue Culture -
Washing Room
Sterilization Room
Media Preparation Room
Inoculation Room
Incubation Room.
Skilled Labour

## Slide 8: WASHING ROOM
The glassware washing area shall be located near the
sterilization and media preparation areas.
Washing sink(45cm x 60cm) can be fitted in one side of Room and should be acidic and alkali resistant.
Room also provided with Bucket, detergent , mug and also Plastic tray to kept washed Media bottles and sterilized media.
Room provided with water line and electricity line.

## Slide 9: STERILIZATION ROOM
The room should have One autoclave(vertical or
horizontal) or cooker with well ventilated exhaust fan.
Also having tools for support while placing the media bottles in autoclave or cooker for sterilization.
The bottles should sterilized At 1210C at 15 lb. for 1 hrs.
It contains wrapping paper to wrap and the rubber to tight the inoculating dishes for sterilization.

## Slide 10: MEDIA PREPARATION ROOM
The area shall be provided with working tables which should be up to 1.2 m wide and the height should be 850 mm - 900 mm.
Table top shall be covered with materials which are easily cleaned and which will stand disinfectant solution.
Water source and glassware storage area shall be provided.
Room contains double distilled water unit , pH meter, buffer solution, electronic balance , cooling freeze, measuring cylinder, magnetic stirrer, pipette, hot plate, media bottle.
Room should contains the stock A,B,C,D, E and F solution with required chemicals such as sucrose, adenine sulphate , innositol , agar-agar( solidifying agent) etc.

## Slide 11: INOCULATION ROOM
The floor of room covered with tiles to facilitate proper
cleaning.
Room contains the laminar air flow cabinet with installation of a HEPA (high efficiency particulate air) filter for filtered air supply.
It also requires sodium hypochlorite, mercuric chloride and 70% alcohol for surface sterilization .
It requires forceps , scalpel, sterile bottles, sterile dishes, spirit lamp , cotton and hand care etc.

## Slide 12: INCUBATION ROOM
The width of the racks should be 405 mm to 1 m. The distance between each layer of the racks should be not less then 455 mm.
Photoperiod racks with culture bottles shall be provided. we mostly operate light intensity with a standard day length of 16 hours and 8 hour dark regime.
Temperature is maintained at a standard 25 + 2 o C with 1.5 ton window A.C. to creating the controlled environment condition.
Light intensity required about 200 lux to 1600 lux for
growth of culture.

## Slide 13: INSTRUMENT ROOM
Bottle washing machine and autoclave.
Freezer and Rotary shaker.
Multipurpose Magic stove.
Weighing balance, thermometer .
Magnetic stirrer and Digital pH meter.
Laminar air flow with U.V. tube .
Racks-photoperiodic culture Glass bed steriliser .
Air conditioner with Stabiliser and Micro air oven etc.

## Slide 14: Glassware and Other requirement
Glass bottle, Petridis, burette, funnel.
Beakers and pipettes.
conical flask with screw cap.
Graduated measuring cylinder
Spatula, scalpel and forceps
Wrapping paper and bucket, gloves etc.

## Slide 15: OTHER FACILITIES
Hand washing facilities
Fire extinguishing system
Waste disposal area should be provided