## Slide 1
Cell culture contamination

## Slide 2: Introduction
No cell culture problem is as universal as that of culture loss due to contamination.
Contamination problems can be divided into 3 classes:
1.Minor annoyances:
when up to several plates or flasks are occasionally to contamination

## Slide 3
2.Serious problems:
when contamination frequency increases or entire experiments or cell culture are lost
3.Major catastrophes:
contaminants are discovered that call into doubt of past or current work

## Slide 4
Some consequences of contamination
Loss of time, money and effort.
Adverse effects on the cultures.
Inaccurate experimental results.
Personal embarrassment.
Loss of valuable products.

## Slide 5
What are the major cell culture contaminants?
What are the source of biological contaminants?
How can cell culture contamination be controlled?

## Slide 6
What are the major cell culture contaminants?
A cell culture contaminant can be defined as some elements in the culture system that’s undesirable because of its possible adverse effects on either the system or its use.
Can be divided into:
Chemical contamination.
Biological contamination.

## Slide 7
1-Chemical contamination
Media: from reagent and water
Sera: uncontrolled lot to lot variation in hormone and growth factors
Water
Endotoxins: from water, sera and some culture additives
Storage vessels
Fluorescent lights
Incubators

## Slide 8
Source
Deposits on glassware, pipettes, instruments etc., left by disinfection or detergents
Metal ions, endotoxins, and other components of media, sera, and water
Plasticizers in plastic tubing and storage bottle
Free radicals generated in media by the photo-activation of tryptophan, riboflavin or HEPES exposed to fluorescent light.

## Slide 9
Residues from germicides used to disinfect incubators, equipments and labs
Impurities in gases used in CO2 incubators

## Slide 10
2-Biological contamination
Bacterial, mould, and yeast.
Viruses.
Protozoa.
Mycoplasmas.
Cross-contamination by other cell culture.

## Slide 11
Source
Contact with non-sterile supplies, media or solution.
Particulate or aerosol fallout during manipulation, transportation, or incubation.
Swimming, crawling, or growing into culture vessels.
Accidents and mistakes.

## Slide 12
Bacteria , molds and yeast
Found virtually everywhere and are able to quickly colonize and flourish in environment provided by cell culture.
In the absence of antibiotic, microbes can be detected in a culture within a few days, either by direct microscopic examination or by its effects on culture (pH shifts, turbidity and cell destruction)
When antibiotic are routinely used, resistant organisms may develop low level infection that are very difficult to detect by direct visual observation.

## Slide 13
Viruses
Due to their small size, viruses are the most difficult cell culture contaminants to detect in culture .
Their small size also make them difficult to remove from media, solution, and other solution of biological origin.
A major concern of using virally infected cultures is not their effect on the cultures, but potential health hazards they pose for laboratory personnel.
Caution should always be used when working with tissues or cells from human or other primates to avoid possible transmission of viral infection (HIV, HBV, EBV, etc.).

## Slide 14
Protozoa
Both parasitic and free living amoeba occasionally identified as cell culture contaminants.
They can cause chronic eosinphilic pneumonia (CPE) resembling viral damage and completely destroy a culture within 10 days
Because of their slow growth and morphological similarities to cultured cells, amoeba are difficult to detect in culture.
Fortunately, this type of contaminants are rare, but it is important to be alert to the possibility of their occurrence.

## Slide 15
Mycoplasma
1st detected in cell culture by Robinson and coworkers in 1956. When they attempt to study the effects of PPLO on Hela cells
At least 11 to 15% of cell cultures are currently infected by mycoplasmas
Mycoplasmas are not benign culture contaminants but have the ability to alter culture cell function, growth, metabolism, morphology , virus propagation and yield, and cause chromosomal aberrations and damage, and CPE including plaque formation

## Slide 16
What gives mycoplasma the ability to infect so many cultures?
3 basic characters:
1-smallest self replicating organism known.
2-lack cell wall.
3-fastidious growth requirement
characters allow growth to very high densities in cell culture without any visible signs of contamination.

## Slide 17
Also, small size make them like viruses, very difficult to remove from sera by membrane filtration
In addition, fastidious growth requirements (provided by cell culture) make them very difficult to grow and detect using standard microbiological cultivation methods.
The ability to alter every cell function parameter make them the most serious, widespread, and devastating culture contaminants.
Mycoplasmas have been described as “crabgrass "of cell culture

## Slide 18
How can cell culture contamination be controlled?
Use good aseptic techniques
Reduce accidents
Keep the laboratory clean
Routinely monitor for contamination
Use frozen cell repository strategically
Use antibiotics sparingly if at all

## Slide 19
Dealing with cell culture contamination
1- Use the microscope to examine all tissue culture flasks for any contamination (tiny dots of bacteria or stings of hyphen from fungi / mould)
2- Remove all infected flasks into an appropriate laboratory where no tissue culture occurs
3- Half fill the contaminated flask with 10% sodium hypochlorite. Leave for 2 hours before rinsing down the sink
4- With copious amounts of water, wipe the outside of all non-infected flasks with 2.5% sodium hypochlorite and 70% isopropanol

## Slide 20
. 5- Clean the CO2 incubator thoroughly, including the water tray, with 2.5% sodium hypochlorite. The sodium hypochlorite should be left to soak for a maximum of 5 minutes and rinsed off with water for irrigation and
6- absorbent tissue (to prevent sodium hypochlorite corroding the metal of the cabinet). Spray incubator with 70% isopropanol and wipe with dry tissues to remove any residual sodium hypochlorite and water.
7- Refill the water tray with 1 liter of water for irrigation and a suitable concentration of mild detergent / fungicide commercially available for water trays and incubators. Return the tray to incubator.

## Slide 21
8- Discard all culture medium prepared at the same time as the culture medium used in the infected flasks
9 - Wipe out the cabinet used with 2.5% sodium hypochlorite
The sodium hypochlorite should be left to soak for a maximum of 5 minutes and rinsed off with water for irrigation
absorbent tissue (to prevent sodium hypochlorite corroding the metal of the cabinet)
Spray the cabinet with 70 isopropanol and wipe with dry tissues to remove any residual sodium hypochlorite and water

## Slide 22
10- Put all gowns to laundry when cleaning has been completed. Use freshly laundered gowns when cleaning precautions are complete

## Slide 23
Persistent contamination
We recommend the following must be performed in addition to the points described in the above section if contamination occurs frequently (more than once in a week)
1- Discard all cell culture flasks
2- Discard all aliquots of penicillin /streptomycin, glutamine and fetal bovine serum and any open bottles of water for irrigation.

## Slide 24
3- Decontaminate the Class I / II cabinet by formaldehyde fumigation if possible
4- Decontaminate incubator by using the usual laboratory cabinet cleaning procedure including disinfectants

## Slide 25
Thank You