## Slide 1: Equipment required for cell
culture
 Laminar Air Flow Hood
 Co2 Incubator
 Centrifuge
 Refrigerator
 Cryo-storage container
 liquid nitrogen container
 Haemocytometer
 Water bath
 Flow cytometry
 Inverted Microscope
 Dissecting microscope
 Glass wares and plastic wares

## Slide 2: Biosafety cabinet
 The basic purpose of Biosafety Cabinet is to provide protection to the culture from any organism such as fungi, virus, bacteria under aseptic conditions and also protect the operator form the risk of infection.
 The purpose of this cabinet is to protect the product by use of HEPA filters (High Efficiency Particulate Air).
 The level of contamination depends on the use of biosafety cabinet.
HEPA filters is 90%.
is 95%.
BSC 1= Should have a biosafety cabinet, Efficiency of
BSC 2= Closed Biosafety cabinet, Efficiency of HEPA filters
BSC 3= Closed Biosafety cabinet, High density, Radioactive
sterilization, Efficiency of HEPA filters is 99.5%.

## Slide 3: Co2 Incubator
 Incubator is a temporary chamber which provides suitable
temperature, density, moisture and pH for better growth and
development of animal cells.
 They maintain sterility of the chamber by using HEPA filters.
 They maintain a constant temperature by using a silicon gasket on the inner door.
 Humidity is created which prevents desiccation of the
media and maintain osmolarity.
 pH is also maintained in the media.

## Slide 4: Cooling centrifuge
 Centrifuge is an instrument used to separate the particles from a solution according to their size, shape, density, viscosity of the medium and the rotor speed by using the principle of centrifugal force.
 Cooling centrifuge is used to prepare
the cell for cryo-preservation.

## Slide 5: Refrigerator
 Cell culture laboratories needs a domestic refrigerator (preferably one without an auto defrost freezer)
 It stores the reagent, media and cells at 2-8 degree
centigrade used for small laboratories.
 For large laboratories a cold room is restricted for the storage of cells.

## Slide 6: Cryo-storage container
 Cell lines in continues culture are likely suffer form genetic instability as their passage number increases therefore it is essential to prepare working stocks of the cells and preserve them in cryogenic storage.

## Slide 7: Liquid nitrogen container
 Liquid nitrogen container provide a long term storage with low liquid nitrogen evaporation.
 There are two main types of liquid nitrogen storage
system
vapour phase- this system minimizes the risk of explosion with cryo-storage tubes.
liquid phase- This system usually have longer static holding time.

## Slide 8: Haemocytometer
 It is an instrument used to estimate the cell number
and viability.
 It has two parts
Neubauer’s slide- it has counting scales on each quadrant. The depth of the scales is 0.1mm.
Coverslip – it is used to keep the liquid sample in a perfect shape into a flat layer of even thickness.

## Slide 9: Water bath
 A water bath is a device that maintains water at a constant temperature.
 It is used for thawing of the cells directly taken out from the freezing media or from liquid nitrogen to prevent the cell form any mechanical damage due to fluctuation of temperature.
 The temperature of water bath is 5-100 degree
centigrade.

## Slide 10: Flow cytometry
 Flow cytometry is a laser based technique to analyse the characteristics of the cells .
 This is mainly used for the analysis of the expression of the cell surface and intracellular molecules.
 It is used to characterize different cells from a heterogenous mixture.

## Slide 11: Inverted microscope
 The inverted microscope is designed with the light source and the condenser lens above the specimen.
 The objective and turret of the microscope is on the
bottom.
 The objective focus the light to produce a real image.
 It is to observe any contamination in the cell culture.

## Slide 12: Dissecting microscope
 The dissecting microscope is also know as stereo microscope.
 It has a long working distance between 25 and 150mm.
 It has low magnification ability and one can manipulate the
specimen even performing a small dissection under the
microscope.
 Light specimens can also be observed under this microscope.

## Slide 13: Glassware's and plastic wares
 Beaker
 Pipette
 Measuring cylinder
 Horizontal and vertical flask
1. T25
2. T75
3. T100
 Petri plate
 Microscopic slides
 Coverslips
 Cell culture plates.