## Slide 1
A REVIEW ON ENERGY FROM BIOMASS
(NON CONVENTIONAL ENERGY SOURCES)

## Slide 2: Importance of non-conventional sources of energy:
The non-conventional sources of energy are abundant in nature
These are renewable resources. The non-conventional sources of energy can be renewed with minimum effort and money.
Non-conventional sources of energy are pollution-free and eco-friendly

## Slide 3: Bio-Energy
Bioenergy is renewable energy made available from materials derived from biological sources.
Biomass is any organic material, may include wood, wood waste, straw, manure, sugar cane and many other byproducts from a variety of agricultural processes.

## Slide 4: Biomass
Biomass is organic matter produced by plants – terrestrial and
aquatic – and their derivatives. It includes
1. Forest crops and residues
2. Crops specially grown in ‘energy farms’ for their energy content
3. Animal manure

## Slide 5: Ag wastes and other biomass
Waste Biomass
  Crop and forestry residues, animal manure, food processing waste, yard waste, municipal and C&D solid wastes, sewage, industrial waste
New Biomass: (Terrestrial & Aquatic)
  Solar energy and CO2 converted via photosynthesis to organic compounds
  Conventionally harvested for food, feed, fiber, & construction materials

## Slide 6: Agricultural and Forestry Wastes
Crop residues
Animal manures
Food / feed processing residues
Logging residues (harvesting and clearing)
Wood processing mill residues
Paper & pulping waste slurries

## Slide 7: Municipal garbage & other landfilled wastes
Municipal Solid Waste
  Landfill gas-to-energy
Pre- and post-consumer residues
Urban wood residues
  Construction & Demolition wastes
  Tree trimmings
  Yard waste
  Packaging
  Discarded furniture

## Slide 8: Biomass Energy
Biomass continues to account for an estimated 1/3rd of primary energy use, while in the poorest counties up to 90% of all energy is supplied by biomass
Biomass energy, or bio energy is the conversion of biomass (organic material originating from plants, trees, and crops and essentially the collection and storage of the sun’s energy through photosynthesis) into useful forms of energy such as heat, electricity, and liquid fuels

## Slide 9: Biomass to Bioenergy
Biomass: renewable energy sources coming from biological material such as plants, animals, microorganisms and municipal wastes
Notes: Does Oil consider Biomass? No, cause it is not reneable.

## Slide 10: Bioenergy Types
Biofuels
  Liquids
    Methanol, Ethanol, Butanol, Biodiesel
  Gases
    Methane, Hydrogen
Bioheat
  Wood burning
Bioelectricity
  Combustion in Boiler to Turbine
  Microbial Fuel Cells (MFCs)

## Slide 11: Conversion Processes
Biological conversion
  Fermentation (methanol, ethanol, butanol)
  Anaerobic digestion (methane)
  Anaerobic respiration (bio-battery)
Chemical conversion
  Transesterification (biodiesel)
Thermal conversion
  Combustion
  Gasification
  Pyrolysis
Notes: Ethanol fermentation, a form of anaerobic respiration used primarily by yeasts when oxygen is not present in sufficient quantity for normal cellular respiration
transesterification is the process of exchanging the alkoxy group of an ester compound by another alcohol. These reactions are often catalyzed by the addition of an acid or base. Transesterification: alcohol + ester → different alcohol + different ester
Gasification is a process that converts carbonaceous materials, such as coal, petroleum, or biomass, into carbon monoxide and hydrogen by reacting the raw material at high temperatures with a controlled amount of oxygen.
Fast pyrolysis is a process in which organic materials are rapidly heated to 450 - 600 oC in absence of air. Under these conditions, organic vapours, pyrolysis gases and charcoal are produced. The vapours are condensed to bio-oil. Typically, 70-75 wt.% of the feedstock is converted into oil

## Slide 12: Biomass-to-Bioenergy Routes
Wet biomass
(organic waste, manure)
Solid biomass
(wood, straw)
Sugar and starch plants
(sugar-cane, cereals)
Oil crops and algae
(sunflower, soybean)
Biomass
Ethanol
Butanol
Methyl ester
(biodiesel)
Pyrolytic oil
Biogas
H2, CH4
Fuel gas
Sugar
Pure Oil
Conversion processes
Electricity
Heat
Electrical devices
Heating
Liquid biofuels
Transport
Biofuels and Bioenergy
Application
Anaerobic
fermentation
Gasification
Combustion
Pyrolysis
Hydrolysis
Hydrolysis
Extraction
Crushing
Refining
fermentation
Transesterification
Photosynthesis
6CO2 + 6H2O C6H12O6 + 6O2
co2
Notes: This is basically an Overview of the our class topics ….
Everything starts from “Photosynthesis”, which is the process by which plants, some bacteria, and some protistans use the energy from sunlight to produce sugar. Photosynthesis is the process of converting light energy to chemical energy and storing it in the bonds of sugar. This process occurs in plants and some algae (Kingdom Protista).

## Slide 14: Typical composition of biogas
Matter | %
Methane, CH4 | 50-75
Carbon dioxide, CO2 | 25-50
Nitrogen, N2 | 0-10
Hydrogen, H2 | 0-1
Hydrogen sulfide, H2S | 0-3
Oxygen, O2 | 0-

## Slide 15: Stack
MUNICIPAL SOLID WASTE (MSW) TO ENERGY INCINERATION PLANT
SHREDDER
AIR CLASSIFIER
Dry duly treated biomass
HRSG
BOILER
FURNACE
Heat Recovery Steam Generator HRSG
Removal of pollutants
Superheated output
Boiler Feed water
Cooling Tower
Pre-heated Feed water
Refuse derived fuel
Aux fuel
Metal Glass
Recycled
Thermal Output
Electrical
Output
Ash to landfill
Condenser Pre-heated
air

## Slide 16: Main Advantages of Biomass Energy
Indigenous source
Economic development opportunities in rural areas
The pollutant emissions from combustion of biomass are usually lower than those from fossil fuels
Commercial use of biomass
Improve fertility of soil

## Slide 17: Environmental Advantages
Renewable resource
Reduces landfills
Protects clean water supplies
Reduces acid rain and smog
Reduces greenhouse gases
  Carbon dioxide
  Methane

## Slide 18: Disadvantages of Biomass Energy
It is dispersed and land intensive as a source
It is often of low energy density
It is labour intensive and the cost of collecting large quantities for commercial application is significant

## Slide 19: Fuel Properties of Biogas
Calorific Value
60% Methane : 22.350 to 24.22 MJ/m3. Without CO2 : 33.525 to 35.390 MJ/m3. Octane rating without CO2 : 130 Octane rating with CO2 : 110
Ignition temperature : 6500 C Air to methane ratio for complete
Combustion (by volume) : 10 to 1
Explosive limits to air (by volume) : 5 to 15

## Slide 20: Applications

## Slide 21: Biofuel Applications: Liquids
Ethanol and Butanol: can be used in gasoline engines either at low blends (up to 10%), in high blends in Flexible Fuel Vehicles or in pure form in adapted engines
Biodiesel: can be used, both blended with fossil diesel and in pure form. Its acceptance by car manufacturers is growing
Notes: Biodiesel Use in blends below 5% does not require any modification of the engine. Some minor modifications might be necessary when using biodiesel at 100%.
Biogas from anaerobic digestion is mainly used on site for cogeneration applications. The solid and liquid residues from the process are often used as fertilisers on farm land.

## Slide 22: Why Butanol?
More similar to gasoline than ethanol
Butanol can:
  Be transported via existing pipelines (ethanol cannot)
  Fuel engines designed for use with gasoline without modification (ethanol cannot)
Produced from biomass (biobutanol) as well as petroleum (petrobutanol)
Toxicity issues (no worse than gasoline)

## Slide 23: Biodiesel Production
Biodiesel, glycerin
Fuel Grade
Biodiesel
Fertilizer K3PO3
water
Catalyst Mixing
Methanol
Neutralization
Acid (phosphoric)
Biodiesel,
impurities
Methanol Recovery
Crude Glycerine
Recovered
methanol
Wash water
Phase Separation
gravity or centrifuge
Purification
(washing)
Catalyst NaOH
Crude Biodiesel (methyl ester)
Crude glycerin
Excess methanol
Catalyst KOH
Raw Oil
Transesterification Reaction

## Slide 24: Biofuel Applications: Gases
Hydrogen: can be used in fuel cells for generating electricity
Methane: can be combusted directly or converted to ethanol
Notes: Biodiesel Use in blends below 5% does not require any modification of the engine. Some minor modifications might be necessary when using biodiesel at 100%.
Biogas from anaerobic digestion is mainly used on site for cogeneration applications. The solid and liquid residues from the process are often used as fertilisers on farm land.

## Slide 25: Bioheat Applications
Small-scale heating systems for households typically use firewood or pellets
Medium-scale users typically burn wood chips in grate boilers
Large-scale boilers are able to burn a larger variety of fuels, including wood waste and refuse-derived fuel
Biomass Boiler
Notes:   Heat can also be produced on a medium or large scale through cogeneration which provides heat for industrial processes in the form of steam and can supply district heat networks.

## Slide 26: Bioelectricity Applications
Co-generation: Combustion followed by a water vapor cycle driven turbine engine is the main technology at present
Microbial Fuel Cells (MFCs): Direct conversion of biomass to electricity
Notes:   Heat can also be produced on a medium or large scale through cogeneration which provides heat for industrial processes in the form of steam and can supply district heat networks.

## Slide 27: Microbial fuel cells (MFCs)
Electrons flow from an anode through a resistor to a cathode where electron acceptors are reduced. Protons flow across a proton exchange membrane (PEM) to complete the circuit.
PEM
Notes: In this regard, microbial fuel cells, in which biomass fuels are directly converted to electrical energy by undergoing oxidation-reduction (redox) reactions at an anode and a cathode is a promising technology.

## Slide 28
Bio-electro-chemical devices
Bacteria as biocatalysts convert the biomass “fuel” directly to electricity
Oxidation-Reduction reaction switches from normal electron acceptor (e.g., O2, nitrate, sulfate) to a solid electron acceptor: Graphite anode
It’s all about REDOX CHEMISTRY!

## Slide 29: Microbial fuel cells in the lab
Two-compartment MFC
Proton exchange membrane:
Nafion 117 or Ultrex
Electrodes: Graphite plate
84 cm2
Working volume: 400 ml
ANODE CATHODE
Membrane
Anode
Cathode
Notes: Voltage was measured across a 1000 ohm resistor and data was logged into a computer using a data acquisition unit. Power density was calculated as :current times voltage divided by area of the electrode. Current was voltage times resistant

## Slide 30
Anode
Proton Exchange
Membrane
Cathode
Anode
compartment
Cathode
compartment
Cellulose
β-Glucan
(n≤7)
β-Glucan (n ≤7)
Glucose
Cellodextrin
β- Glucan (n-1)
n≥2
n=1
6CO2 + 24e- + 24H+
Butyrate
4CO2 + 18e- + 18H+
Propionate
Acetate
3CO2 + 28e- + 28H+
2CO2 + 8e- + 8H+
O2
H2O
e-
e-
Not to Scale
Bacteria Cell
Bacteria
Cell Wall
H+
e-
H+
e-
H+
e-
e-
H+
Notes: Here is a short cartoon that shows how the substrate enters the bacteria cell, and you can see the biochemical reactions that lead to the production of electrons and hydrogen ions inside and then the transfer of these ions across the cell wall to the anode electrode and through the PEM which leas to the electricity production

## Slide 31: Thank You