## Slide 2: SUB TOPIC
Introduction
Principles of air-conditioning
Type of of air-conditioning
Cooling cycle / refrigeration cycle
The coolant

## Slide 3: INTRODUCTION
Definition - Air conditioning is the process of altering the properties
of air (primarily temperature and humidity) to more favorable conditions.
The control of these conditions may be desirable to maintain the health and comfort of the occupants, or to meet the requirements of industrial processes irrespective of the external climatic conditions

## Slide 4: PRINCIPLES OF AIR-CONDITIONING  The goal is to keep it more comfortable inside the house than it is outside.

## Slide 5: TYPE OF AIR-CONDITIONING
Window air-conditioning system
Split air-conditioning system
Centralised air-conditioning system
Package air-conditioning system

## Slide 6: 1) Windows Air-conditioning System
Window air conditioners are one of the most commonly used and cheapest type of air conditioners.
To install one of these units, you need the space to make a slot in the wall, and there should also be some open space behind the wall.
Window air-conditioner units are reliable and simple-to-install solution to keep a room cool while avoiding the costly construction of a central air system.
Better yet, when the summer heat dies down, these units can be easily removed for storage, and you can use the window sill for other purpose

## Slide 8: 2) Split Air-Conditioning System
The split air conditioner comprises of two parts: the outdoor unit and the indoor unit.
The outdoor unit, fitted outside the room, houses components like the compressor, condenser and expansion valve.
The indoor unit comprises the evaporator or cooling coil and the cooling fan. For this unit you don’t have to make any slot in the wall of the room.
Further, the present day split units have aesthetic looks and add to the beauty of the room. The split air conditioner can be used to cool one or two rooms

## Slide 10: 3) Centralised Air-Conditioning System
The central air conditioning plants or the systems are used when large buildings, hotels, theaters, airports, shopping malls etc. are to be air conditioned completely.
The window and split air conditioners are used for single rooms or small office spaces.
If the whole building is to be cooled it is not economically viable to put window or split air conditioner in each and every room.
Further, these small units cannot satisfactorily cool the large halls, auditoriums, receptions areas etc.

## Slide 12: 4) Packaged Air-Conditioning System
The window and split air conditioners are usually used for the small air conditioning capacities up to 5 tons.
The central air conditioning systems are used for where the cooling loads extend beyond 20 tons.
The packaged air conditioners are used for the cooling capacities in between these two extremes.
The packaged air conditioners are available in the fixed rated capacities of 3,5, 7, 10 and 15 tons.
These units are used commonly in places like restaurants, telephone exchanges, homes, small halls, etc.

## Slide 14: New Invented Technology for Air-Conditioning System
DISTRICT COOLING SYSTEM
CHILLED BEAM
SYSTEM

## Slide 15: District Cooling System
 District Cooling Systems (DCS) is a system which distribute chilled water or other media, usually provided from a dedicated cooling plant, to multiple buildings for air conditioning or other uses.

## Slide 16: District Cooling System
The Objectives :
To centralized production of chilled water by using district cooling plant. The generated chilled water will then be channeled to various building blocks thru pre- insulated seamless underground pipes.

## Slide 17: District Cooling System
The Advantages
Improve energy efficiency
Protect environment
Save spaces
Improve urban view
Reduce manpower for operation and maintenance

## Slide 18: District Cooling System
How The System Work ?
DC means the centralized production and distribution of cooling energy. Chilled water is delivered via an underground insulated pipeline to office, industrial and residential buildings to cool the indoor air of the buildings within a district. Specially designed units in each building then use this water to lower the temperature of air passing through the buildings ACS.
The output of one cooling plant is enough to meet the cooling-energy demand of dozens of buildings. DC can be run on electricity or natural gas, and can use either regular water or seawater. Along with electricity and water, DC constitute a new form of energy service.

## Slide 19: District Cooling System
Why It Is Environmental Friendly ? District cooling helps the environment by increasing energy
efficiency and reducing environmental emissions including air pollution, the greenhouse gas (GHG) carbon dioxide(CO2) and ozone-destroying refrigerants.
District cooling can reduce annual CO2emissions by about 1 ton for every ton of district cooling refrigeration demand served

## Slide 20: DCS Network Diagram

## Slide 21: DCS Network Diagram

## Slide 22: DCS- APPLICATION IN MALAYSIA
PUTRAJAYA
KUALA LUMPUR
INTERNATIONAL AIRPORT
BANGSAR
UKM

## Slide 23: DCS - COMPONENTS
Central Chiller Plant – generate chilled water for cooling purposes
Distribution Network – distribute chilled water to building
User Station – interface own building air-conditioning circuit

## Slide 24: CHILLED BEAM SYSTEM
It is a type of convection HVAC system designed to heat or cooled high rise building such as commercial building.
It’s primarily gives off its cooling effect through convection by using water to remove heat from a room.
Pipes of water passed through the beam suspended short distance from the ceiling of a room.
As the beam chills the air around it, the air becomes denser and falls to the floor.
It is replaced by warmer air moving up from
below, causing a constant floe of convection and cooling the room.

## Slide 26: ADVANTAGES
Simple to design and control
Smaller ductwork
Less mechanical space
Less maintenance
Increase comfort

## Slide 27: disadvantages
Not well known in our industry
Higher construction cost
Many engineers aren’t familiar with this technology
Dew point concerns, building must have a good control of humidity to prevent condensation on chilled beam surface.

## Slide 28: DEFINITION– a cycle that shows how the refrigerant vapor is inhaled and discharged by the compressor to the condenser.

## Slide 29: Compressor -Inhaling the refrigerant from the suction channel
- Compressing to the discharge channel.
Condenser
-Remove heat from condenser
-Refrigerant vapor turn to liquid.
Expansion Valve
-Low the temperature and
pressure of liquid
-Control the flow rate in
-to the evaporator.
Evaporator
-Liquid turns to vapor
-Cold air flows out room

## Slide 31
COMPRESSOR
CONDENSER
EVAPORATOR
EXPANSION VALVE

## Slide 32: THE COOLANT
Heat is removed from the cooling by coolant.
Functions as a heat absorber from the evaporator
Good coolant must have features ;
Non toxic
Not explosive
Non-corrosive components

## Slide 33: THE COOLANT
Not explosive
Soluble in oil to lubricate effectively
Harmless when responding to oil even in the presence of moisture
Have a high resistance to electricity.

## Slide 34: CAN YOU FIND WHERE TO USED EACH OF THIS COOLANT?
Type of coolant
R-22
MONOKLORODIFLUOROMETANA
R-12 DIKLORODIFLUOROMETANA
R-11 TRIKLOROMONOFLUROMETANA