## Slide 1
CENTRAL AIR-CONDITIONING SYSTEM

## Slide 2: CONTENTS
INTRODUCTION
HISTORY
WORKING PRINCIPLE OF AC
TYPES OF AIR CONDITIONING SYSTEM
CENTRAL AIR CONDITIONING SYSTEM
WORKING OF CENTRAL AC
TYPES OF CENTRAL AC
COMPONENTS OF CENTRAL AC
ADVANTAGES
DISADVANTAGES
SUMMARY

## Slide 3: INTRODUCTION
DEFINITION OF AIR-CONDITIONING:-
Air conditioning is the process of altering the properties
of air (primarily temperature and humidity) to more favorable conditions.
The control of these conditions may be desirable to maintain the health and comfort of the occupants, or to meet the requirements of industrial processes irrespective of the external climatic conditions.

## Slide 4: HISTORY
In 1902, the first modern electrical air conditioning unit was invented by Willis Carrier in Bufallo, Newyork.
The first air conditioner, designed and built in Buffalo by Carrier, began working on 17 July 1902.

## Slide 5: WORKING PRINCIPLE OF AC
Air conditioners and refrigerators work the same way.
Air conditioners use refrigerant that easily convert from a gas to a liquid and
back again.
The machine has four main parts. They are a compressor, a condenser, an expansion device and an evaporator.
The working fluid arrives at the compressor as a cool, low pressure gas. The compressor compresses this refrigerant resulting into high temperature and pressure gas.
The working fluid leaves the compressor and flows into the condenser. The condenser condenses the refrigerant and change the hot gas into high pressure liquid.
The liquid goes into the expansion device where it expands and its pressure drops.
Now it goes to evaporator where the liquid changes to gas and evaporates, it extracts heat from the air around it.
By the time the working fluid leaves the evaporator, it is a cool, low pressure

## Slide 6: BLOCK DIAGRAM OF AC

## Slide 7: TYPES OF AIR CONDITIONING SYSTEM
Depending upon the need or application, the AC system is designed in different way but the working principle remains the same.
Types of AC
1) Window air-conditioning system 2)Split air-conditioning system 3)Package air-conditioning system 4)Central air-conditioning system

## Slide 8: CENTRAL AC SYSTEM
The central air conditioning plants or the systems are used when large buildings, hotels, theaters, airports, shopping malls etc. are to be air conditioned completely.
A method of structural cooling in which a centralized unit cools and dehumidifies air before circulating it throughout the building.
The main unit is located outdoors or in isolated area of a building.

## Slide 9: LAYOUT OF CENTRAL AC

## Slide 10: WORKING OF CENTRAL AC
Central air conditioners circulates cool air through a system of supply and return ducts. Supply ducts and registers (i.e., openings in the walls, floors, or ceilings covered by grills) carry cooled air from the air conditioner to the home. This cooled air becomes warmer as it circulates through the home, then it flows back to the central air conditioner through return ducts and registers.

## Slide 11: TYPES OF CENTRAL AC
An outdoor metal cabinet contains the condenser and compressor, and an indoor cabinet contains the evaporator
A central air conditioner is either a split-system unit or a packaged unit.
Split-system Packaged Unit
The evaporator, condenser, and compressor are all located in one cabinet, which usually is placed on a roof or on the ground

## Slide 12: SPLIT-SYSTEM CENTRAL AC
In a split-system central air conditioner, an outdoor metal cabinet contains the condenser and compressor, and an indoor cabinet contains the evaporator.
In many split-system air conditioners, this indoor cabinet also contains a furnace or the indoor part of a heat pump. The air conditioner's evaporator coil is installed in the cabinet or main supply duct of this furnace or heat pump.
If your home already has a furnace but no air conditioner, a split-system is the most economical central air conditioner to install.

## Slide 13: PACKAGED UNIT CENTRAL AC
In a packaged central air conditioner, the evaporator, condenser, and compressor are all located in one cabinet, which usually is placed on a roof or on a concrete slab next to the house's foundation.
This type of air conditioner is also used in small commercial buildings.
Air supply and return ducts come from indoors through the home's exterior wall or roof to connect with the packaged air conditioner, which is usually located outdoors.
Packaged air conditioners often include electric heating coils or a natural gas furnace. This combination of air conditioner and central heater eliminates the need for a separate furnace indoors

## Slide 14: COMPONENTS OF CENTRAL AC
Air handling unit(AHU)
Supplying duct
Return duct
Diffusers/Registers
Compressor
Condenser
Expansion device
Evaporator
Thermostat

## Slide 15: AIR HANDLING UNIT
The function of AHU is to suck air from the rooms through return duct and let it pass through air filters, then discharging the conditioned air back to the rooms.
It is shaped like a box that contain some equipments such as filter,blower etc.
It is located at the top of building and the door of room is always closed.

## Slide 16: SUPPLYING DUCT
It supplies the conditioned air from air handling unit (AHU) to the space or room.
It is also called as main duct.
From main duct a number of duct branches are provided for the each room.

## Slide 17: RETURN AIR INLET(DUCT)
This component is to regulate and extract air from a room and recycle it.
Use of any ventilating, heating and air conditioning.
The air will force air process which blows through the duct.
Located either in hallway or in the ceiling at AHU Rooms.

## Slide 18: DIFFUSERS/REGISTERS/G RILLS
It distributes and directs the conditioned air to the occupied space.
It has a rectangular or square face incorporated with vanes,blades etc.
It controls the amount of conditioned air and deflects into the space.
Located at the top of ceiling and it will come in several types.

## Slide 19: THERMOSTAT
It controls the temperature and maintains a constant temperature in the fixed range throughout the room.
It automatically switches the compressor ON or OFF as the temperature rises or falls .

## Slide 20: TYPE OF GAS THAT USED AS REFRIGERANT
Chlorodifluoromethane also known hydrochlorofluorocarbon (HCFC).
Usually known as R22 gas.
Very high quality and competitive price.

## Slide 21: ADVANTAGES
Improves indoor air quality.
Level of indoor noise is almost negligible.
Maintains a constant temperature and humidity throughout the conditioned space.

## Slide 22: DISADVANTAGES
The size for the AC unit is large.
The cost of installing the system is high.

## Slide 23: SUMMARY
Very large buildings, hotels, theaters, airports, shopping malls can be air conditioned completely and economically.
Central AC system provides uniform distribution of conditioned air throughout the whole building or space.

## Slide 24: THANK YOU