## Slide 1: Single Cell Protein

## Slide 2: Introduction
World war I and II – microbial protein
S. cerevisiae and Torula yeast (Candida utilis),
Rapid developments in microbial protein production occurred during the 1960s and 1970s.
Term single cell protein (SCP) was ﬁrst coined at the Massachusetts Institute of Technology
SCP is not pure protein, but refers to the whole cells of bacteria, yeasts, ﬁlamentous fungi or algae, and also contains carbohydrates, lipids, nucleic acids, mineral salts and vitamins

## Slide 4: Advantages of SCP
1 rapid growth rate and high productivity;
2 high protein content, 30–80% on a dry weight basis;
3 the ability to utilize a wide range of low cost carbon sources, including waste materials;
4 strain selection and further development are relatively straightforward, as these organisms are amenable to genetic modiﬁcation;
5 the processes occupy little land area;
6 production is independent of seasonal and climatic variations; and
7 consistent product quality.

## Slide 5: Selection of a suitable strain for SCP
1 Performance (growth rate, productivity and yields) on the speciﬁc, preferably low-cost, substrates to be used;
2 Temperature and pH tolerance;
3 Oxygen requirements, heat generation during fermentation and foaming characteristics;
4 Growth morphology and genetic stability in the fermentation;
5 Ease of recovery of SCP and requirements for further downstream processing; and
6 Structure and composition of the ﬁnal product, in terms of protein content, amino acid proﬁle, RNA level, ﬂavour, aroma, colour and texture

## Slide 6: Carbon substrates for SCP
1 the cost of the substrate;
2 biomass yield;
3 oxygen requirement during fermentation
4 heat produced and the level of fermenter cooling required; and
5 downstream processing costs, including the removal of possible toxic components.

## Slide 7: Microbial metabolism
1 The dissimilation pathway of the carbon source, i.e. an estimate of adenosine triphosphate (ATP) produced per unit of substrate oxidized;
2 The assimilation pathway, i.e. an estimate of ATP required for the synthesis of a unit of cell biomass;
3 The maintenance requirement for the organism, i.e. the quantity of ATP required in order to maintain cell integrity; and
4 The extent of uncoupling, i.e. non-productive uses of ATP

## Slide 9: SCP production Process
Physiological Problems;
1 oxygen requirements and oxygen transfer rates;
2 nutrient and temperature gradients;
3 effects of CO, as high levels may inhibit respiration in certain microorganisms; and
4 hydraulic pressure in deep fermenters.

## Slide 10: How to improve production
1 Use of cheaper substrates;
2 Improvements in the efﬁciency of the organism;
3 Enhanced nutritional value/composition of the microbial protein;
4 Marketing the protein as a premium product for human rather than animal consumption;
5 Production of other valuable byproducts, i.e. development of a multiproduct process; and
6 Lowering downstream processing costs, e.g. by reducing endogenous RNA levels.

## Slide 11: Basic Stages of Production
Media preparation
Fermentation
Separation and downstream processing