## Slide 1: Current electricity

## Slide 2: cell
In current electricity a cell means an electrochemical cell. Cell is a device by which chemical energy is converted into electrical energy.

## Slide 3: Battery
Main type: storage battery
Date: 1881
a cell or connected group of cells that converts chemical energy into electrical energy by reversible chemical reactions and that may be recharged by passing a current through it in the direction opposite to that of its discharge -- called also storage cell.

## Slide 4: Type of batteries
  The primary battery converts chemical energy to electrical energy directly, using the chemical materials within the cell to start the action.
  The secondary battery must first be charged with electrical energy before it can convert chemical energy to electrical energy.
  The secondary battery is frequently called a storage battery, since it stores the energy that is supplied to it.

## Slide 5: Lead acid battery
Electrolyte for the most part distilled (pure) water, with some sulfuric acid mixed with the water.
Electrodes must be of dissimilar metals.
An active electrolyte.

## Slide 6: Series Connected Batteries/cells
Positive terminal of one cell is connected to the negative terminal of the next and so on…, is called a series connected battery.
External circuit is taken from –ve terminal of 1st cell and +ve terminal of last cell.
All current pass through each cell,
The voltage/EMF of this type of battery is the sum of a individual cell voltages.
V= v1+v2+v3…….vn
internal resistance of battery is sum of internal resistance of individual cells.

## Slide 7: Parallel Connected Batteries/cell
Connect the negative terminal from one cell to the negative of the next cell & so on.
Connect the positive terminal to the positive terminal of next & so on, is parallel connected.
The current pass through the external circuit from a common point where the negative terminal are connected together to a common point of junction of +ve terminals.
Voltage/EMF remains constant as that of single cell and the current is cumulative.
V= v1= v2= v3…… vn
Internal resistance of battery reduced to less than that of one cell.

## Slide 8: Series-Parallel Connections
PARALLEL
SERIES
SERIES-PARALLEL
SERIES
SERIES

## Slide 9: Series and Parallel Batteries
Parallel connection
  increases the energy capacity of the battery set.
  Cells must be matched for voltage
  unmatched cells result in voltage with only internal resistance.
Series-Parallel connections
  combination of series and parallel calculations

## Slide 10: Serial and Parallel batteries
In series, the voltage is increased - the sum of the cells in series
  Energy capacity is the same as that of a single cell (current = electrons/second
  if unmatched cells are connected in series, the capacity will be that of the weakest cell.

## Slide 11: Cells
Positive electrode
Negative electrode
Electrolyte
Separator

## Slide 12: Basic primary wet cell
The metals in a cell are called the electrodes, and the chemical solution is called the electrolyte.
The electrolyte reacts oppositely with the two different electrodes
It causes one electrode to lose electrons and develop a positive charge; and it causes one other electrode to build a surplus of electrons and develop a negative charge.
The difference in potential between the two electrode charges is the cell voltage.

## Slide 13: Dry cell
Uses An electrolytic paste.
The electrolytic paste reacts with the electrodes to produce a negative charge on one electrode and a positive charge on the other.
The difference of potential between the two electrodes is the output voltage.

## Slide 14
DRY-CELLS
Not Rechargeable
As the reactants inside them become used up in chemical reactions, the output from these batteries gradually falls.
Once all the reactants have been used up, these batteries go “flat” and cannot supply electrical energy anymore.

## Slide 15
RECHARGEABLE
Usually maintain a constant output until just before they go flat.
Once flat, it can be connected to a recharger. This uses electrical energy to reverse the chemical reactions that happened in the battery while it was in use.
E.g. Car batteries: they are constantly recharged while the car is moving, so the lights and horn will always work.
E.g. Mobile phones, MP3 players etc: must be recharged at regular intervals. It is usually recommended that such batteries should almost be flat before recharging. This allows the battery to be fully charged again.

## Slide 16
Which are best?
Non-rechargeable | Rechargeable
cheap to buy | often expensive to buy
can only be used once | can be used many times
expensive to use in the long run as more are needed (high cost / performance ratio) | cheap in the long run as they can be re-used (low cost / performance ratio)
output falls gradually with time | output stays constant until almost flat
disposal of many batteries creates a lot of chemical pollution | disposal of fewer batteries creates less chemical pollution

## Slide 17: The Leclanche dry cell
There are various type of cell, different types made from different materials and giving different EMFs, but that in common use is the dry Leclanche cell.
This consists of zinc and carbon electrodes in a solution of ammonium chloride. The carbon replaces the second metal and is surrounded by a mixture of powdered carbon and meganese dioxide.
The ionic movement within cell results in zinc acquiring a negative and carbon a positive charge, the p.d between them being 1.5 volts.
in dry Leclanche cell zinc forms the outer case of cell and wire coming it is negative terminal.
The carbon electrode is a rod in the center of cell and its summit forms positive terminal.

## Slide 18: electrolytes
When charging first started, electrolysis broke down each water molecule (H2O) into two hydrogen ions (H+) and one oxygen ion (O-2).
The positive hydrogen ions attracted negative sulfate ions (SO4-2) from each electrode.
These combinations produce H2SO4, which is sulfuric acid.

## Slide 19: Electrolysis
    The producing of chemical changes by passage of an electric current through an electrolyte. Electrolysis
When charging fist starts, the current flowing through the battery causes electrolysis of the water.
The water molecules (H2O) begin to break down into their constituent ions.
For each negative oxygen ion (O-2) that is produced, there are two positive hydrogen ions (H+), so that the electrolyte is neutral.