## Slide 1: Chemical oxygen demand (COD)
Noor-us-Sabah
Lecturer
Dept. Soil & Environmental Sciences

## Slide 2: COD
The COD (Chemical Oxygen Demand) test represents the amount of chemically digestible organics (food).
COD measures all organics that are biochemically digestible as well as all the organics that can be digested by heat and sulfuric acid.
It is used in the same applications as BOD.
COD has the advantage over BOD in that the analysis can be completed within a few hours whereas BOD requires 5 days.
The major drawback of the COD test is the presence of hazardous chemicals and toxic waste disposal.

## Slide 3
The standard method for indirect measurement of the amount of pollution (that cannot be oxidized biologically) in a sample of water.
The chemical oxygen demand test procedure is based on the chemical decomposition of organic and inorganic contaminants, dissolved or suspended in water.
The result of a chemical oxygen demand test indicates the amount of water-dissolved oxygen (expressed as parts per million or milligrams per liter of water) consumed by the contaminants, during two hours of decomposition from a solution of boiling potassium dichromate.
The higher the chemical oxygen demand, the higher the amount of pollution in the test sample.

## Slide 4
Oxygen-Demanding Wastes:
Oxygen dissolved in water is indicator of water quality. 6 ppm O2 or more supports desirable aquatic life.
BOD: Biochemical oxygen demand: measures the amount of dissolved oxygen consumed by aquatic microorganisms. Sewage, paper pulp, or food wastes can cause an Oxygen sag, where few fish survive.

## Slide 7
In environmental chemistry, the chemical oxygen demand (COD) test is commonly used to indirectly measure the amount of organic compounds in water.
Most applications of COD determine the amount of organic pollutants found in surface water (e.g. lakes and rivers) or wastewater, making COD a useful measure of water quality.
It is expressed in milligrams per liter (mg/L), which indicates the mass of oxygen consumed per liter of solution.

## Slide 8
The basis for the COD test is that nearly all organic compounds can be fully oxidized to carbon dioxide with a strong oxidizing agent under acidic conditions.
COD is again a relative measure:
Higher COD = dirtier water.
COD can be used with BOD – they are not a replacement for each other.