## Slide 1: Strategies for pollution control
Noor-us-Sabah
Lecturer
Dept. Soil & Environmental Sciences

## Slide 2: Air pollution control
Air pollution abatement programs can be divided into two categories:
1. Long-term control
2. Short-term control (episode control)
Long-term control strategies involve a legislated set of measures to be adopted over a multiyear period. Short-term (or episode) control involves shutdown and slowdown procedures that are adopted over periods of several hours to several days under impending adverse meteorological conditions.

## Slide 3
Some examples of long-term air pollution control policies are:
Enforcing standards that restrict the pollutant content of combustion exhaust
Requiring used motor vehicles to be outfitted with exhaust control devices
Requiring new motor vehicles to meet certain emissions standards
Prohibiting or encouraging the use of certain fuels in power plants
Establishing zoning regulations for the emission of pollutants
Encouraging the use of vehicles powered by electricity or natural gas

## Slide 4
Short-term controls are of an emergency nature and are more stringent than long-term controls that are continuously in effect. Examples of short-term control strategies are:
Prohibiting automobiles with fewer than three passengers
Prohibiting the use of certain fuels in some parts of the city
Prohibiting certain activities, such as incineration of refuse

## Slide 5
Different techniques are used for controlling air pollution caused by 'gaseous pollutants' and that caused by 'particulate pollutants'.
Methods of controlling gaseous pollutants:
The air pollution caused by gaseous pollutants like hydrocarbons, sulphur dioxide, ammonia, carbon monoxide, etc can be controlled by using three different methods- Combustion, Absorption and Adsorption.
Combustion: This technique is applied when the pollutants are organic gases or vapours. The organic air pollutants are subjected to 'flame combustion or catalytic combustion' when they are converted to less harmful product carbon dioxide and a harmless product water.

## Slide 6
Absorption: In this method, the polluted air containing gaseous pollutants is passed through a scrubber containing a suitable liquid absorbent. The liquid absorbs the harmful gaseous pollutants present in air.
Adsorption: In this method, the polluted air is passed through porous solid adsorbents kept in suitable containers. The gaseous pollutants are adsorbed at the surface of the porous solid and clean air passes through.
Methods of controlling particulate emissions: The air pollution caused by particulate matter like dust, soot, ash, etc, can be controlled by using fabric filters, wet scrubbers, electrostatic precipitators and certain mechanical devices.

## Slide 7
1. Mechanical Devices: It works on the basis of following:
Gravity: In this process, the particulate settle down by the action of gravitational force and get removed.
Sudden change in the direction of air flow: It brings about separation of particles due to greater momentum.
2. Fabric Filters: The particulate matter is passed through a porous medium.
The particulate present in the polluted air are filtered and gets collected in the fabric filters ,while the gases are discharged.
The process of controlling air pollution by using fabric filters is called 'bag filtration'.

## Slide 8
Wet Scrubbers: They are used to trap SO2, NH3 and metal fumes by passing the fumes through water.
4. Electrostatic Precipitators: When the polluted air containing particulate pollutants is passed through an electrostatic precipitator, it induces electric charge on the particles and then the aerosol particles get precipitated on the electrodes.

## Slide 9
Some other methods of controlling Air Pollution:
Tall chimneys should be installed in factories.
Better designed equipment and smokeless fuels should be used in homes and industries.
Renewable and non- polluting sources of energy like solar energy, wind energy, etc. should be used.
Automobiles should be properly maintained and adhere to emission control standards.
More trees should be planted along roadsides and houses.

## Slide 10: Control of water pollution
Reducing the effluent concentration of the waste input by:
a. Wastewater treatment
b. Industrial in-plant process control
c.Eliminating effluent constituents by pretreatment prior to discharge to sewer systems or by different product manufacturing for an industry.

## Slide 11
Reducing the upstream concentration by upstream point and non – point source controls.
Reducing the effluent volume by:
(a) Reduction of direct industrial discharge volumes into the municipal sewer system.
(b) Reduction in infiltration into municipal sewer systems.
(c) Reduction of waste volumes through process modifications in industries.

## Slide 12
Increase the Environmental, In-Stream Degradation Rate of the Substance:
This can be accomplished by a redesign of the chemical to result in a more rapid breakdown of the chemical by the natural heterotrophic bacteria in the stream. For example, redesign of synthetic detergents to reduce foaming and downstream transport through increased biodegradation rate. In manufacturing of potentially toxic chemicals also an attempt may be made to increase biodegradation rates so that a chemical build-up does not occur.

## Slide 13
Environmental Controls:
The three broad categories, for control of pathogenic bacteria, viruses and parasites are –
control at the input source of the micro-organism,
control at the area of water use, and
control of the product that is affected by contamination
Municipal wastes causing point pollution are the usual principal inputs of communicable disease organisms.
Such inputs can be reduced by treatment of wastes without disinfection and disinfection by chlorination, chlorine dioxide and ultraviolet radiation.

## Slide 14
Harversting of Biomass:
Water hyacinth and other aquatic weeds are used to upgrade wastewater treatment and treat chemical wastewaters. The water hyacinth has been used for purifying not only domestic wastewater but also industrial wastewater. It can readily absorb, accumulate and concentrate heavy metals such as lead, cadmium, mercury and nickel. Other studies have evaluated the potential of water hyacinth to absorb various organic chemicals like phenols and toxaphene. Water hyacinth can remove even radioactive metals from effluents, which is very difficult otherwise.
As the metals are extracted from the effluents, it causes considerable cleaning of the effluent. The pH of effluent after treatment has been found to be between 6.8 and 7.8, which is an ideal range for freshwater. Further, it does not allow the algal bloom to develop and the BOD and COD are lowered to the level at which the effluent can be allowed to mix with freshwater without causing any bad effect.

## Slide 15
Wastewater reclamation:
The sewage treatment yields irrigation water that contains a number of essential nutrients like nitrogen, phosphorus and potassium to make it a fertilizer.
In west Bengal, the practice of irrigating fish ponds with sewage for raising fish is common.
Another interesting aspect is the reuse or reclamation of sewage effluents for industrial purposes. This holds good for coping with ever increasing demand for water by industrial establishments in big cities.

## Slide 16: Control of soil pollution
Remediation techniques
Transfer of contaminated solid wastes to common landfills or possible options for utilization of the waste removed.
Capping the waste in a secured landfill (SLF).
Confinement of the contaminated area by concrete side walls and capping.
Contaminated soil excavation, soil washing and refilling.
Physical and chemical remediation techniques like Soil vapour extraction pump & treat, chemical precipitation etc.
Bioremediation of contaminated sites
Phytoremediation of contaminated sites

## Slide 17
Biological Treatment
Phytoremediation especially suited for heavy metals
Bioremediation for organic pollutants
Land farming as extended application of Bioremediation.
Land farming is a bioremediation treatment process that is performed in the upper soil zone or in biotreatment cells. Contaminated soils, sediments, or sludges are incorporated into the soil surface and periodically turned over or tilled to aerate the mixture.

## Slide 18: outcomes
Bioremediation technology
Cost-effective
Eliminate problem to a greater extant
Generate no or low waste
High Public acceptance

## Slide 19
Reduce the amount of plastic you use. Researchers fear that such plastic bags may never fully decompose; instead, they gradually just turn into smaller and smaller pieces of plastic. How to reduce the amount of plastic you use in your home:
Don’t use garbage bags—just empty your trash into the garbage bin.
If you don’t like that approach, get yourself some recycled or biodegradable, compostable garbage bags.

## Slide 20
Reduce your garbage amount
Properly maintain all underground storage tanks, like oil, septic, and sewer lines. Have your septic tank pumped on schedule and look for signs of leakage, such as soggy areas in the yard, odor, slowing and backups in the home, and excessive plant growth over a particular area. Most septic systems need pumped every three to five years.
Be diligent about picking up and disposing of trash. Dispose of animal waste into a septic or sewage system as promptly as possible--do not leave it on the lawn or place it in a storm drain.
Do not burn trash, particularly plastics or tires, because the residue in the smoke will settle and pollute the soil.