## Slide 1
BISMILLAH

## Slide 2
Solute Transport

## Slide 3: Contents
Definitions
Introduction
SOLUTE TRANSPORT PROCESS
Microscopic Mixing
Fick`s Law
Transport Equations
Breakthrough Curves
Dispersion Process
Land use effects on flow and transport

## Slide 4
A substance dissolved in solvent, both forming of solution called solute.
The soil water that contains various solutes called soil solutions.
Group of processes by which solute are transported called solute transport or solute movement.
SOLUTE
SOIL SOLUTION
SOLUTE TRANSPORT

## Slide 5
INTODUCTION
When water flows on soil surface as overland flow and/or through the soil matrix, it also dissolves solutes (e.g salts, fertilizers, pesticides).
These solutes not only move with soil water but also within
the soil matrix mainly due to the concentration gradients.

## Slide 6
In agricultural ecosystems, solutes may be categorized on the basis of their function(e.g., nutrients, pesticides, waste compounds, salts, organic chemicals, heavy metals,viruses, and bacteria). Understanding transport of solutes in soil is important to many management problems in agriculture. It can help when developing procedures for maximizing the effective use of fertilizers or pesticides and other chemicals within the root zone while minimizing their movement into groundwater.

## Slide 7
TYPES OF
SOLUTE
Depending upon chemical stability and reactivity.
The solutes are broadly classified
into two categories:
CONSERVATIVE SOLUTES
NON-CONSERVATIVE SOLUTES

## Slide 8
Conservative solutes
Those solutes which remain unchanged physically and
chemically, and do not undergo irreversible reactions, such as chloride (Cl) and bromide(Br);
Non-Conservative solutes
Those solutes which can undergo irreversible reactions and change their physical or chemical phase.

## Slide 9
The labile solutes
The labile solutes can undergo reversible or irreversible physiochemical,biochemical, or microbial reactions and can change theirphysical or chemical phase with time.
The examplesof labile solutes are: nitrate, sulfate,and ammonia, which are involved in mineralization, immobilization, or redox reactions.Some pesticides are also labile and their lability is quantified by their half-life
The non conservative solutes can be divided into
labile solutes and reactive solutes.

## Slide 10
Reactive solutes
solutes that undergo reversible or irreversible reactions with soil constituents by way of adsorption (adsorption of cations, e.g., Ca+, Mg++, on clay particles),precipitation or dissolution (e.g., precipitation of calcium as calcium sulfate

## Slide 11
SOLUTE TRANSPORT PROCESS

## Slide 12
Basically solute transport within a soil matrix occurs by two physical processes:
diffusion and convective flow.
Several simple and complicated mathematical models have been developed in the past, which can reproduce the experimental results very well.

## Slide 13
The movement of solutes inside the soil matrix is caused by “mass flow” or“convection.” This type of flow is also called Darcian flow
Darcian flow
pore water
velocity
The velocity at which solutes travel through soil matrix is generally known as “pore water velocity” and is the ratio of volumetric flow of solute through a unit cross-sectional area and volumetric moisture content of the soil matrix. In other words, the pore watervelocity is the ratio of Darcian velocity and moisture content..

## Slide 14
In general, pore water velocity accounts for the straight-line length of path traversed in the soil in a given time.
In reality, the flow paths are not always straight but are irregular or tortuous. This property is known as “tortuosity” of soil pores.
Solutes do not always flow with water but sometimes go ahead of it due to the twin process of diffusion and dispersion or exclusion, lag behind due to adsorption or retardation, or get precipitated or volatilized
tortuosity
The movement of solute from the higher concentration to the lower concentration gradient is also known as the process of “diffusion.” This process commonly occurs within gaseous and liquid phases in the soil matrix due to the random thermal motion, also called “Brownian movement.”

## Slide 15
Hydrodynamic dispersion.”
There is another simultaneous process that tries to mix and eventually even out the concentration gradients known as “hydrodynamic dispersion
Diffusion is an active process, whereas dispersion is a passive process.
However, in most practical applications these two solute transport processes are considered additive.

## Slide 16
The total solute resident concentration (C, g cm−3) in a soil matrix can be mathematically expressed as
Mathematically
Where
ρb is the soil bulk density (gcm−3),
Ca is adsorbed concentration (g g−1),
θ is volumetric soil moisture content (cm3cm−3),
C1 is dissolved solute concentration (gcm−3),
fa is the volumetric air content (cm3 cm−3), and
Cg is gaseous solute concentration (gcm−3).
C=ρbCa+θC1+faCg

## Slide 17
MACROSCOPIC MIXING
Several different mechanisms operating in the porous media during transport of solute are responsible for the mixing at macroscopic level. Some of these include the following(Greenkorn, 1983):

## Slide 18
Molecular diffusion:
If the process is stationary or slow moving and the time required for the solute to move through the porous media is sufficiently long (i.e., forsufficiently long time scale) molecular diffusion is the primary source of macroscopic
mixing.
2. Tortuosity.
The tourtuous flow paths inside the soil profile causes the fluid element to remain at different distances from the same starting position even when they travel at the same pore water velocity (ratio of Darcy velocity and soil moisture content).
3. Connectivity of pores:
If the pores are not well interconnected or if some of the pores in the porous media are not accessible to the fluid element flowing through that pore,they cause macroscopic mixing and dispersion.

## Slide 19
4. Hydrodynamic dispersion:
The solute element near the wall of pore travels at a different velocity than the element at the center of pore (Fig. 16.1a). This results in a velocity gradient inside the pore and solute elements move relative to each other at
different velocity.
5. Immobile zones:
The immobile water zones normally causes the fluid element to move quicker and out in the effluent solution earlier (early breakthrough), and at the same time, increases the tail of the breakthrough curve mainly due to the slow release of solute element trapped inside immobile water .
6. Turbulence:
If the size of the pore abruptly changes, the flow inside a pore may become turbulent and mixing is caused by eddies.

## Slide 20
7. Adsorption:
When the concentration front looses some ions abruptly as they are removed from solution by the process known as adsorption, the unsteady state flow occurs and the concentration profiles becomes flat.

## Slide 21
.
FIGURE ; The physical mechanisms for hydrodynamic
dispersion of solutes through soil matrix:
(a) influence of velocity distribution within a soil pore;
(b)influence of size of pore, and
(c)influence of microscopic flow direction.

## Slide 22
FICK’S LAW
There are two Fick’s laws,
which describe diffusion of substances in porous media. The movement of ions from areas of higher concentration to lower concentration is proportional to the concentration gradient, the cross-sectional area available for diffusion, and the elapsed time during the solute transport. The net amount of solute crossing a plane of unit area in unit time is known as the solute flux density (J; gcm−2s−1), which is given by Eq. known as Fick’s first law (1855) for steady state one-dimensional solute transport:

## Slide 23
EQUATION
Where:
Dm is the ionic or molecular diffusion coefficient of the porous media (cm2s−1),
C is the solute concentration (gcm−3) and x is the distance (cm).
The concentration gradient (∂C/∂x) in Eq. is the driving force and the minus sign indicates that solute moves from areas of higher concentration to lower concentration.

## Slide 24
TRANSPORT EQUATIONS

## Slide 25
When a solute enters a soil matrix (which can be in a soil core, repacked soil column, or agricultural soil in a field) the initial sharp boundary between the resident and displacing solute starts diminishing mainly due to the twin processes of diffusion and dispersion.
The transport of a solution through soil matrix consists of three main components:
convection, diffusion, and dispersion, which are briefly described below.

## Slide 26
Convective or advective transport of a solution inside a soil matrix is known as the passive movement with flowing soil water.
If the transport process has only convective transport without any diffusion, the water and solute move at the same average flow rate
Mathematically convective transport (Jm) can be expressed as.
1- Convection or Mass Transport
Jm=qsC
Where
Jm is the flux density for convective or mass transport (ML−2T−1),
qs is the volumetric fluid flux density with dimensions of velocity (LT−1), and
C is the volume averaged solute concentration (ML−3).

## Slide 27
2- Diffusive Transport
Diffusion is a spontaneous process resulting from the random thermal motion of dissolved ions and molecules. In general, the diffusion is an active process and diffusive transport tends to decrease the existing concentration gradients and moves the process towards homogeneity rather rapidly.
Fick’s law defines the diffusive transport and for
one-dimensional steady state transport is given as:

## Slide 28
Where
JD is solute flux density for diffusive transport of solute (ML−2T−1),
θ is the volumetric moisture content (L3L−3).
The diffusion coefficient in soils (Dm) is slightly
less than the diffusion coefficient in pure water (D0) mainly due to the tortuous flow paths in soils.
Dm=D0θξ
Where
ξ is the dimensionless tortuosity factor ranging roughly from 0.3 to 0.7 for most soils.

## Slide 29
3- Dispersive Transport
The soil matrix consists of pores of different shapes, sizes, and orientation. This heterogeneity of pore structure causes a large deviation of local pore water velocities inside each individual pore.
Dispersive transport occurs because of the velocity variations in soil matrix with respect to average pore water velocity. The velocity variations in a soil matrix is caused by several factors such as zero velocity at the particle surface, which increases gradually and is the maximum at the center of pore or at air water interface under unsaturated conditions,

## Slide 30
Pore sizes also create velocity gradients with the velocity in
larger pores greater than the velocity in smaller pores .
The other possible reason is the fluctuation of flow paths of an element of water with respect to the mean direction of flow.
EQUATION
Where
Dh is the mechanical dispersion coefficient (Bear, 1972) and is assumed to be a function of fluid velocity as follows:
Dh=λvn
n= exponent

## Slide 31
BREAKTHROUGH CURVES

## Slide 32
Breakthrough curves
The graphical representation of the concentration of these solutes with respect to time or cumulative effluent volume or pore volume is known as “breakthrough curves” (BTC).
Pore volume is the ratio of cumulative effluent volume (cm3) at a specified time and total volumetric moisture content of soil (cm3). Pore volume is a non dimensional number and is zero at time zero.
Pore volume

## Slide 33
BTCs can have different shapes depending upon the solute application.
with respect to time of effluent arrival,
volume of effluent, and pore volumes,
(a) Chloride application as a step input
through a 10 cm loam soil column
(pore water velocity=0.11 cm.h−1);
(b) chloride application as a pulse input through a 10 cm loam soil col umn(pore water velocity=0.1 cm.h−1); and
(c) schematic for a Dirac and square pulse input and output. (Modified from Shukla et al., 2002.)

## Slide 36
DISPERSION PROCESSES

## Slide 37
There are several mechanisms that cause macroscopic mixing and are generally accounted for in the dispersion coefficient.
Some of them are mixing due to tortuosity, inaccessibility of pore water, recirculation due to flow restrictions, macroscopic and hydrodynamic dispersion, and turbulence in flow paths (Greenkorn, 1983).
The hydrodynamic dispersion coefficient (D) is proportional to the pore water velocity of a solute under steady state flow conditions (Biggar and Nielsen, 1967; Bear, 1972).
D=λv

## Slide 38
The proportionality constant, A,, in Eq. is known as dispersivity.
The value of dispersivity depends upon the scale over which water flux and solute convection is averaged.
Dispersivity is also dependent on the moisture content of the porous media (Krupp and Elrick, 1968) and decreases rapidly as moisture content decreases from saturation.

## Slide 39
Some typical values of dispersivity for laboratory soil columns range from 0.5 to 2 cm (Jury et al., 1991), 0.11 to
0.37 cm (for loam soil) and 0.14 to 0.22 cm (for sandy loam soil; Shukla et al., 2003).
The dispersion processes are site specific and depend upon the subtler factors, which are related to the experimental conditions (Flury et al., 1998). The
longitudinal dispersivity values are measured in field soils by placing a suction cup at different depths and
measuring solute breakthough as a function of time. The dispersivity calculated for field
soils by one-dimensional convective dispersion or method of moments (Jury and Roth, 1990) are given in following Table.

## Slide 40
Soil | Tracer | Application rate cmd -1 | Dispersivity cm | Refrance
Clay, silty.clay | Cl,triticum | 2 | 9.4 | Van de Pol et al. (1977)
Clay loam | Cl.No3 | - | 8.3 | Biggar and Nielsen (1976)
Clay loam | Br | 96 | 5.2-23 | Fleming and Butters (1995
Clay loam | Br | 30,33,41,67 | 16-38 | Jaynes (1991)
loam | Cl | 9.6,19.2 | 29 | Roth et al. (1991)
Loamy sand | Cl,No3,Br | 1.1 | 3.2-15.8 | Ellsworth et al. (1996)
sand | Cl | 84,132 | 0.7-1.6 | Hamlen
sand | Cl | 84,112 | 17,2.7 | Van Wesenbeck and Kachanowski (1991)

## Slide 41
RELATIONS BETWEEN DISPERSION COEFFICIENT AND
PORE WATER VELOCITY
The effective dispersion coefficient generally varies with mean microscopic flow velocity.
Based upon the magnitude of the Peclet number (P, defined as vL/D, where L is a characteristic length), within the range of average pore water velocities, molecular diffusion dominates the dispersion of the solute at smaller displacement velocities and gives way to convective dispersion at greater velocities.

## Slide 42
The five dispersion regimes can be identified in Fig. as
pure molecular diffusion;
(ii) molecular diffusion and kinematic dispersion;
(iii) predominant kinematic dispersion and
(iv) and (v) as pure kinematic dispersion regimes (Shukla et al., 2002).
The relationship between DD0−1 and Peclet number for:
field soil (A) (from Biggar and Nielsen, 1976),
(B) loam,
(C) Sandy loam (from Shukla et al., 2002), and
(D) single grain material (from Pfannkuch, 1963). (Redrawn from Shukla et al., 2002.)

## Slide 44
The relations between D/Do and Peclet number (vd/Do) given as
where
Do=0.66θ Dm
With Dm being the diffusion coefficient for free solution.
The D0 in Eq. can be obtained from known values of θ and Dm

## Slide 45
MATHEMATICAL REPRESENTATION OF THE SOLUTE TRANSPORT PROCESS
The simplest form of one dimensional convective-dispersive equation (CDE), assuming macroscopic steady state water flow, constant soil– moisture content, and no interactions between the chemical and the solid phase was developed by Lapidus and Amundson, (1952), which is similar

## Slide 46
EQUILIBRIUM ANION EXCLUSION MODEL
Certain anions interact with the negatively charged solid surfaces of the soil and are excluded from the liquid region adjacent to the soil particle surfaces. This phenomenon is known as anion exclusion or negative adsorption
NONEQUILIBRIUM TRANSPORT
The physical non equilibrium is caused by a heterogeneous flow regime and chemical none equilibrium by the kinetic adsorption.

## Slide 47
Aggregate Geometry Models
The non dimensional mass transfer parameter is not directly related to any specific soil characteristic or property and is difficult to determine.
There is a function of time of diffusion, sphere radius (particules constitution the porous medium), molecular diffusion coefficient, intra aggregate water content macro porosity (fraction of total porosity);therefore, apart (16.78) and (16.79), the α can be calculated for the known or assumed geometry of aggregates.

## Slide 48
De is the effective diffusion coefficient, r is the radius of sphere, and α* is time dependent variable.
The α values of cubic aggregates can be obtained by replacing “a” with an equivalent spherical radius “r=0.6203l”, where
f is the length of the side of the cube

## Slide 49
Land Use Effects on Flow and Transport
The flow and transport properties of soils often vary with time due to the influence of land use and soil management practices.
The soil remains mostly undisturbed under no till, which enhances the organic matter accumulation at the soil surface and development of macro pores (cracks between aggregates and pores).
The macro pore channels in no-till system increase the leaching of nutrients and pesticides by bypassing the water-filled micro pores unless the sources are located within the soil micro pores.

## Slide 50
These cracks increase the hydraulic conductivity of soil and decrease reactivity of dissolved chemicals due to the low pore surface area and short residence time.
The increase in organic matter increases the reactivity of chemicals in the soil matrix and the soils start behaving as a multi reaction, multi region soil.
It is important to know this shift in flow and transport processes due to macro pores as failure to take these into account can lead to erroneous conclusion.
CONT….

## Slide 51
Example
Concentration of a solute is 30 mg/g of soil and bulk density is 1.35 Mg/m3. Assuming steady flow conditions, solute free soil profile, and solute diffusion
coefficient3×10−10m2/s, calculate flux density at a vertical distance of 0.1 m and amount of solute in1 ha that diffuses across this boundary in 2 months. (Hint: Use Fick’s first law.)

## Slide 52
Solution
Solute concentration=ρb * Ca=30 * 1.35=40.5 M/gm3 or
4.05×107 mg/m3
Concentration gradient at 0.1 m below soil surface
δC/δz=ΔC/Δz=(0–4.05×107)/(0–0.1)=4.05×108 mg/m4
The flux density of solute is obtained by using equation 7
J=−(3×10−10)*(4.05×108)=−0.122 mg m−2s−1
The negative sign implies that solute is moving downward. The total quantity of solute moved below 0.1 m in one month (Q) can be calculated
asQ=0.122*10000*30*24*3600=3.16×109mgha−1