## Slide 1: Demonstrating the use of MATLAB and perform Signal Plotting.
Signals & Systems
Lab No. 01
Delivered By: Engr. Kiran Arshad

## Slide 2: What is a signal???
Signal is the variation of pattern.
Mathematically, it is the function of two or more variables.
Electrically representation of a signal is:

## Slide 3: Types of Signals:
Continuous Signal : Signals that vary continuously over specified range.
Represented by small parenthesis in SNS. i.e x(t), y(t) etc.
Represented by Amplitude, frequency and phase.
In MATLAB, plot command is used.

## Slide 4
Discrete Signals: Represents discrete or discontinuous quantities.
Represented by large square brackets in SNS. i.e x[t], y[t] etc.
Represented by Amplitude and location of samples. e.g x[2]=??, x[5]=??
In MATLAB, stem command is used.

## Slide 5: What is Matlab?
Matlab is basically a high level language which has many specialized toolboxes for making things easier for us
Case-Sensitive
Assembly
High Level
Languages such as
C, Pascal etc.
Matlab

## Slide 6
Everything in MATLAB is a matrix !

## Slide 7: What are we interested in?
Matlab is too broad for our purposes in this course.
The features we are going to require is
Matlab
Command
Line
m-files
functions
mat-files
Command execution like DOS command window
Data storage/ loading

## Slide 8: MATLAB Screen

## Slide 9: Variables
No need for types. i.e.,
All variables are created with double precision unless specified and they are matrices.
After these statements, the variables are 1x1 matrices with double precision
int a;
double b;
float c;
Example:
>>x=5;
>>x1=2;

## Slide 10: Other MATLAB symbols
, separate statements and data
% start comment which ends at end of line
; (1) suppress output
(2) used as a row separator in a matrix
: specify range
“%” is the neglect sign for Matlab (equaivalent of “//” in C). Anything after it on the same line is neglected by Matlab compiler.

## Slide 11: Array, Matrix
A matrix is a two-dimensional array of numbers. In MATLAB, you create a matrix by entering elements in each row as comma or space delimited numbers and using semicolons to mark the end of each row.
a vector x = [1 2 5 1]
x =
1 2 5 1
a matrix x = [1 2 3; 5 1 4; 3 2 -1]
x =
1 2 3
5 1 4
3 2 -1
transpose y = x’ y =
1
2
5
1

## Slide 12: Long Array, Matrix
t =1:10
t =
1 2 3 4 5 6 7 8 9 10
k =2:-0.5:-1 (Starting value:Interval:Ending Value)
k =
2 1.5 1 0.5 0 -0.5 -1
B = [1:4; 5:8]
x =
1 2 3 4
5 6 7 8

## Slide 13: Generating Vectors from functions
zeros(M,N) MxN matrix of zeros
ones(M,N) MxN matrix of ones
rand(M,N) MxN matrix of uniformly distributed random
numbers on (0,1)
See difference b/w rand, randn and randi by typing help rand, help randn and help randi in command window.
x = zeros(1,3)
x =
0 0 0
x = ones(1,3)
x =
1 1 1
x = rand(1,3)
x =
0.9501 0.2311 0.6068

## Slide 14: Matrix Index
The matrix indices begin from 1 (not 0 (as in C))
The matrix indices must be positive integer
Given:
A(3)=0>>>> Result????
A(2,1:3)=0>>> Result???
A(-2), A(0)
Error: ??? Subscript indices must either be real positive integers or logicals.
A(4,2)
Error: ??? Index exceeds matrix dimensions.

## Slide 15: Concatenation of Matrices
x = [1 2], y = [4 5], z=[ 0 0]
A = [ x y]
1 2 4 5
B = [x ; y]
1 2
4 5

## Slide 16: Basic Functions
There are a lot of built in functions to assist the user:
>> Clc
>> Close all
>> Clear all
>>Who
>>Whos

## Slide 17: Operators (arithmetic)
+ addition
- subtraction
* multiplication
/ division
^ power

## Slide 18: Matrices Operations
Given A and B:
Addition
Subtraction
Product
Transpose

## Slide 19: Matrix Addition
X=[1 2 4]; Y=[1 2 3; 1 1 1; 1 1 1]; Z=[1 1 1; 2 2 2; 3 2 1];
X and Y cannot be added… Dimension must agree in matrix addition.
Y and Z can be added

## Slide 20: Matrix Multiplication
X=[1 2 4]; Y=[1 2 3; 1 1 1; 1 1 1]; Z=[1 1 1; 2 2 2; 3 2 1];
X and Y can be multiplied… Inner Dimension must agree in matrix multiplication.

## Slide 21: Operators (Element by Element or Point to Point)
.* element-by-element multiplication
./ element-by-element division
.^ element-by-element power

## Slide 22: The use of “.” – “Element” Operation
For point to point multiplication, matrix dimension must agree.
K= x^2
Error:
??? Error using ==> mpower Matrix must be square.
B=x*y
Error:
??? Error using ==> mtimes Inner matrix dimensions must agree.
A = [1 2 3; 5 1 4; 3 2 1]
A =
1 2 3
5 1 4
3 2 1
y = A(3 ,:)
y=
3 2 1
b = x .* y
b=
3 4 3
c = x . / y
c=
0.33 1 3
d = x .^2
d=
1 4 9
x = A(1,:)
x=
1 2 3

## Slide 23: SYMMETRIC VECTOR DEFINITION
linspace is used to specify a vector with a given number of equally-spaced elements between specified start and finish point
linspace(X1, X2) generates a row vector of 100 linearly equally spaced points between X1 and X2.
linspace(X1, X2, N) generates N points between X1 and X2.
logspace has a similar effect — except that the points are spaced on a logarithmic scale

## Slide 24: MATLAB Relational Operators
MATLAB supports six relational operators.
Less Than <
Less Than or Equal <=
Greater Than >
Greater Than or Equal >=
Equal To ==
Not Equal To ~=

## Slide 25: Use of M-File
Click to create a new M-File
Extension “.m”
A text file containing script or function or program to run

## Slide 26: Writing User Defined Functions
Functions are m-files which can be executed by specifying some inputs and supply some desired outputs.
The code telling the Matlab that an m-file is actually a function is
You should write this command at the beginning of the m-file and you should save the m-file with a file name same as the function name
function out1=functionname(in1)
function out1=functionname(in1,in2,in3)
function [out1,out2]=functionname(in1,in2)

## Slide 27: Writing User Defined Functions
Examples
  Write a function : y=lab11 (a,b)
    Which takes the values a and b and outputs the sum of a and b i.e a+b
    Calling a function in command window for execution.

## Slide 28: Writing User Defined Functions
Another function which takes x and y and returns the sum and product of its elements as outputs
The function lab12 can be called from command window or an m-file as

## Slide 29: MATLAB PLOTTING: Basic Task: Plot the function sin(x) between 0≤x≤4π
Create an x-array of 100 samples between 0 and 4π.
Calculate sin(.) of the x-array
Plot the y-array
>>x=linspace(0,4*pi,100);
>>y=sin(x);
>>plot(y)

## Slide 30: Display Facilities
plot(.)
stem(.)
Example:
>>x=linspace(0,4*pi,100);
>>y=sin(x);
>>plot(x,y)
Example:
>>stem(x,y)

## Slide 31: Display Facilities
title(.)
xlabel(.)
ylabel(.)
>>title(‘This is the sinus function’)
>>xlabel(‘x (secs)’)
>>ylabel(‘sin(x)’)

## Slide 32: Sub plotting
subplot(m,n,p), or subplot(mnp), breaks the Figure window into an m-by-n matrix of small axes, selects the p-th axes for the current plot, and returns the axes handle.
x = linspace(-5,5);
y1 = sin(x);
subplot(2,2,1)
plot(x,y1)
y2 = sin(2*x);
subplot(2,2,2)
plot(x,y2)
y3 = sin(4*x);
subplot(2,2,3)
plot(x,y3)
y4 = sin(6*x);
subplot(2,2,4)
plot(x,y4)

## Slide 33: Useful Commands
The two commands used most by Matlab
users are
>>help functionname
>>lookfor keyword

## Slide 34: Lab Tasks…
Write a MATLAB function of your name that inputs two variables x and y. Call these variables x and y in command window to plot the sine and cosine waves. (Range of x and y can be from 0 to 2*pi)
Write a MATLAB function that inputs two variables x and y. Call these variables x and y in command window that performs the following operation x2+y2. (Use x=left digit of your registration number and y=right digit of your registration number)

## Slide 35: MATRIX MANIPULATION COMMANDS
A(:,2)
A(2,:)
A(2:3,2)
A([2 3],2)
A(3,4)=454
length(A)
size(A)
eye (n,m)
disp(‘signals’)
who
whos
min(b)
max(a)
sum(a,b)
axis[2 3 4 5]
loglog
semilogx
semilogy
abs(x)
real(x)
imag(x)
conj(x)
ceil(x)
floor(x)
round(x)
syms x
det(a)
A’
inv(a)
pretty(s)
Xlabel
Ylabel
Diff b/w subplot 211,212 and 221,222.
(NOTE: n,m are real valued numbers)

## Slide 36: Thank You…