## Slide 1: (a) Demonstrate the use of MATLAB Graphics (b)Implementation of basic Signals in MATLAB
Signals & Systems
Lab No. 02
Delivered By: Engr. Kiran Arshad

## Slide 2: Specifying Line Style
This example shows how to create a plot using a dashed line. Add the optional line specification, '--', to the x,y pair.
The general syntax is Plot(x,y,’linestyle’,….)

## Slide 3: Specifying different lines for different colors and styles
The general syntax is Plot(x,y,’linestylelinecolor’,….)

## Slide 4
The plot is same as previous cos and sine.. Identify the line color and line style …

## Slide 5: Specifying different lines for different colors, styles and markers
x=0:0.1:2*pi;
y=sin(x)
z=cos(x)
plot(x,y,'-g.',x,z,'--r*')
The general syntax is
Plot(x,y,’linestylelinecolorlinemarker,….)

## Slide 7: Legend
Add a legend to the graph identifying each data set using the legend function. Specify legend descriptions in the order that you plot the lines.
x=0:0.1:2*pi;
y=sin(x)
z=cos(x)
plot(x,y,'-g.',x,z,'--r*')
legend('y=sin(x)','z=cos(x)')

## Slide 8: Data Exploration…
Display Data Values Interactively:
  Data cursors enable you to read data directly from a graph by displaying the values of points you select on plotted lines, surfaces, images, and so on. You can place multiple data tips in a plot and move them interactively. If you save the figure, the data tips in it are saved, along with any other annotations present.
  Enabling Data Cursor Mode :
  Once you have enabled data cursor mode, clicking the mouse on a line or other graph object displays data values of the point clicked. Clicking elsewhere does not create or update data tips

## Slide 10: Creating Multiple Data Tips
Normally, there is only one data tip displayed at one time. However, you can display multiple data tips simultaneously on a graph. This is a simple way to annotate a number of points on a graph.
Use the following procedure to create multiple data tips.
Enable data cursor mode from the figure toolbar. The cursor changes to a cross.
Click on the graph to insert a data tip.
Right-click to display the context menu. Select Create New Data tip.
Click on the graph to place the second data tip. e way to annotate a number of points on a graph.

## Slide 11: Input command
input >>>Prompt for user input.
R = input('How many apples') gives the user the prompt in the text string and then waits for input from the keyboard.
The input can be any MATLAB expression, which is evaluated, using the variables in the current workspace, and the result returned in R.

## Slide 12: (b) Implementation of basic signals in MATLAB
Unit Step Signal: (Also called as Heaviside Step function) is a discontinuous function whose value is zero for negative argument and one for positive argument
clc;
clear all;
N=input('Number of Samples = ');
n=-N:1:N
x=[zeros(1,N) 1 ones(1,N)]
stem(n,x);
xlabel('Time');
ylabel('Amplitude');
title('Unit Step');

## Slide 13: Unit Impulse Function
A function δ[n] that has the value zero everywhere except at x = 0 where its value is infinitely large in such a way that its total integral is 1. In signal processing it is referred to as the unit impulse function
N=input('Number of Samples = ');
n=-N:1:N
x=[zeros(1,N) 1 zeros(1,N)]
stem(n,x);
xlabel('Time');
ylabel('Amplitude');
title(‘Unit Impulse');

## Slide 14: Exponential Signal
Exponential signals are of the form x(t)=Ceat
If a>0, x(t) is increasing/growing function, if a<0, x(t) is decreasing/decaying function. If t=0 then x(t)=C
Plot the signal x(t)=3e0.4t and y(t)=2e-0.9t in the time interval -2≤ t ≤ 5.
t=-2:0.01:5;
x=3*exp(0.4*t);
y=2*exp(-0.9*t);
plot(t,x)
hold on
plot(t,y)

## Slide 15: Representation of Signal as sum of impulse
Any discrete time signal can be broken down into a series of individual impulses which when added together give back the original discrete time signal.

## Slide 16: Lab Tasks…
Lab Task 1: Create a function of your name ‘name(a,n)’ which acquires amplitude (a) and index sequence (n) as a function argument and plots unit step u[n] and unit impulse δ[n] functions in same window using subplot. All functions must have same amplitude value a and index range [n].
Lab Task 2: Write a MATLAB program to generate a sinusoidal sequence. x[n] = Acos( wn + φ )and plot the sequence using the stem function. The input data specified by the user is the n, amplitude A, the angular frequency w, and the phase φ where 0 < w <π and 0 < φ < 2 π.
Lab Task 3: Write a MATLAB function with name expsignal(A,a) that generates and plots the real exponential sequence given as x[n]= Aan Where A is the amplitude and n is the time indexing value. Solve it for the following cases
(i) Growing exponential when a>1
(ii) Decaying exponential when a<1
(iii) a=-1 and (iv) a=1, observe the output and comment about them

## Slide 17
Lab Task 4: Plot each of the following signals in the interval 0 ≤ n ≤ 20:

## Slide 18: Thank You…