## Slide 1: Lecture 2: Binary arithmetic & Binary code
Engr. Muhammad Saad Ullah

## Slide 2: Digital Design
By M. Morris Mano

## Slide 3: Out Line
Binary Arithmetic
Complements of the Number (1’s Complement & 2’s Complement )
Signed Number
Arithmetic Operation with Signed Number
BCD (Binary Coded Decimal)
Binary Codes
Question & Answers

## Slide 4: Binary Arithmetic
Add Binary Numbers
Subtract Binary Numbers
Multiply Binary Numbers
Divide Binary Numbers

## Slide 5: Binary Addition
The four Basic Rules for adding binary digits (bits) as follows:
0 + 0 = 0 Sum of Zero with a carry of 0
0 + 1 = 1 Sum of 1 with a carry of 0
1 + 0 = 1 Sum of 1 with a carry of 0
1 + 1 = 10 Sum of 0 with a carry of 1
In the fourth rule the addition of two 1s yields a binary two (10).
When a binary numbers are added the last condition creates a sum of 0 in a given column and a carry of 1 over to the next to the left.

## Slide 6: Binary Addition example

## Slide 7: Rules of Binary Subtraction
0 - 0 = 0
0 - 1 = 1, and borrow 1 from the next more significant bit
1 - 0 = 1
1 - 1 = 0

## Slide 8: Binary Multiplication

## Slide 9: Example of Binary Multiplication

## Slide 10: Binary Division

## Slide 11: C O M P L E M E N T S O F N U M B E R S
Complements are used in digital computers to simplify the subtraction operation and for logical manipulation.
There are two types of complements for each base‐r system: the radix complement and the diminished radix complement. The first is referred to as the r’s complement and the second as the (r - 1)’s complement
1. Diminished Radix Complement (1,s complement ).
Change each bit in a number to get the 1’s complement.

## Slide 12: 1’s Complement
diminished radix complement, is defined as (r n - 1) - N
For decimal numbers, r = 10 and r - 1 = 9, so the 9’s complement of N is (10 n - 1) - N
For binary numbers, r = 2 and r - 1 = 1, so the 1’s complement of N is (2n - 1) - N. Again, 2n is represented by a binary number that consists of a 1 followed by n 0’s. 2n – 1 is a binary number represented by n 1’s. For example, if n = 4, we have 24 = (10000)2 and 24 - 1 = (1111)2. Thus, the 1’s complement of a binary number is obtained by subtracting each digit from 1.
Therefore, the 1’s complement of a binary number is formed by changing 1’s to 0’s and 0’s to 1’s

## Slide 13: 2. Radix Complement ( 2’s Complement)
Add 1 to the 1’s complement to get the 2’s complement
= [(r n - 1) - N] + 1.
The 2’s complement of binary 101100 is 010011 + 1 = 010100 and is obtained by adding 1 to the 1’s‐complement value.
Another Method
Change all bits to the left of the least significant 1 to get 2’s complement
1. Start at the right with LSB and write the bits as they are up to and including the first 1.
Take the 1’ complement of the remaining bits.

## Slide 14: 2’s complement example
the 2’s complement of 1101100 is 0010100
and
the 2’s complement of 0110111 is 1001001

## Slide 15: Signed Binary Numbers
Computer must be able to handle both positive & negative numbers
Positive integers (including zero) can be represented as unsigned numbers
represent negative integers, we need a notation for negative value
In ordinary arithmetic, a negative number is indicated by a minus sign and a positive number by a plus sign
Because of hardware limitations, computers must represent everything with binary digits

## Slide 16: Signed Binary Numbers
A signed Binary number consist of both sign and magnitude information.
Sign indicate number is +ve or –ve
The magnitude is the value of the number
The Sign Bit
The left most bit in a signed binary number is the sign bit. Which tells the number is +ve or –ve.
0 sign bit indicate a Positive number &
1 sign bit indicate a negative number

## Slide 17: Signed Binary Numbers
For example, the string of bits 01001 can be considered as 9 (unsigned binary) or as +9 (signed binary) because the leftmost bit is 0
The string of bits 11001 represents the binary equivalent of -9 when considered as a signed number
the number consists of a magnitude and a symbol (+ or -) or a bit (0 or 1) indicating the sign

## Slide 18: Positive & Negative numbers 1’s complement & 2’s Complement
In the 1’s complement form, a negative number is the 1’s complement of the corresponding positive number
+25 ( 00011001) as 11100110
2’s complement
Same way as in sign magnitude
In the 2’s complement form, a negative number is the 2’s complement of the corresponding positive number.
i.e +25 ( 0011001 )
-25 as 11100111

## Slide 19: Signed Binary Numbers

## Slide 20: Arithmetic Operation with Signed Number
The addition of two signed binary numbers with negative numbers represented in signed‐2’s‐complement form is obtained from the addition of the two numbers, including their sign bits. A carry out of the sign‐bit position is discarded.

## Slide 21: Arithmetic Operation with Signed Number
Note that negative numbers must be initially in 2’s‐complement form and that if the sum obtained after the addition is negative, it is in 2’s‐complement form. For example, -7 is represented as 11111001, which is the 2s complement of +7
In each of the four cases, the operation performed is addition with the sign bit included. Any carry out of the sign‐bit position is discarded, and negative results are automatically in 2’s‐complement form
In order to obtain a correct answer, we must ensure that the result has a sufficient number of bits to accommodate the sum. If we start with two n‐bit numbers and the sum occupies n + 1 bits, we say that an overflow occurs

## Slide 22: Arithmetic Operation with Signed Number
Arithmetic Subtraction
Subtraction of two signed binary numbers when negative numbers are in 2’s‐complement form is simple and can be stated as follows: Take the 2’s complement of the subtrahend (including the sign bit) and add it to the minuend (including the sign bit). A carry out of the sign‐bit position is discarded.

## Slide 23: Example
To see this, consider the subtraction (-6) - (-13) = +7. In binary with eight bits, this operation is written as (11111010 - 11110011). The subtraction is changed to addition by taking the 2’s complement of the subtrahend (-13), giving (+13). In binary, this is 11111010 + 00001101 = 100000111. Removing the end carry, we obtain the correct answer: 00000111 (+7).

## Slide 24: Binary Codes
Digital systems use signals that have two distinct values and circuit elements that have two stable states
A binary number of n digits, for example, may be represented by n binary circuit elements, each having an output signal equivalent to 0 or 1.
The codes must be in binary because, in today’s technology, only circuits that represent and manipulate patterns of 0’s and 1’s can be manufactured economically for use in computers.

## Slide 25: Binary Codes
An n‐bit binary code is a group of n bits that assumes up to 2n distinct combinations of 1’s and 0’s, with each combination representing one element of the set that is being coded.
A set of four elements can be coded with two bits, with each element assigned one of the following bit combinations: 00, 01, 10, 11.
The bit combination of an n‐bit code is determined from the count in binary from 0 to 2n - 1

## Slide 26: Binary-Coded Decimal Code
binary‐coded decimal and is commonly referred to as BCD. A number with k decimal digits will require 4k bits in BCD. Decimal 396 is represented in BCD with 12 bits as 0011 1001 0110, with each group of 4 bits representing one decimal digit

## Slide 27: Extra Information

## Slide 28
THANK YOU!