## Slide 2: Definition
Bench terraces are a series of level or virtually level strips running across the slope at vertical intervals, supported by steep banks or risers.
It is an engineering soil conservation practice
It is also called bench terracing.

## Slide 4: History
Concept of bench terracing is old as agriculture itself.
Philippines started bench terracing 2500 years ago. US soil conservation services collected evidences:
In Israel, citrus orchard in southern France, ShanSi province(China) and Lebanon hill side.

## Slide 5: Objectives
To reduce run-off or its velocity and to minimize soil erosion.
To conserve soil moisture and fertility and to facilitate cropping operations.
To promote intensive land use and permanent agriculture on slopes and reduce shifting cultivation

## Slide 6: Applicability
This practice can:
Be manage on soil having slopes up to 30 %.
Be done where there is deep heavy clay soil rather than in very sandy soil.
Typically not applicable for slopes of decomposed granitic material, or any significantly sandy soil, because of excessive sloughing of material and construction difficulties.

## Slide 7: Locations and conditions for use
Bench terraces are particularly suited to countries or communities with the following macro conditions:
Severe erosion hazards
Areas with small holdings and a dense population.
Areas where there are food shortages or high unemployment rates.
Areas where crops require flood irrigation

## Slide 8: Cont..
For micro or site conditions, bench terracing is suitable in the following cases:
Where there are relatively deep soils.
On slopes not exceeding 25 degrees.
On sites which are not dissected by gullies and not too stony.

## Slide 9: Cut and Fill method

## Slide 10: Types of Bench Terracing
Level or Table top bench terrace
Sloping inwards bench terrace
Sloping outwards bench terrace
Conservation type bench terrace

## Slide 11: Level or Table top bench terrace
Table top bench terrace are suitable for:
Areas receiving medium rainfall
Areas having highly permeable and deep soils

## Slide 13: Sloping inwards bench terrace
Sloping inwards bench terrace are suitable for:
Areas receiving heavy rainfall.
It is useful for crops susceptible to water lodging.
Runoff towards hillside.

## Slide 15: Sloping outwards bench terrace:
Sloping outwards bench terrace are suitable for:
Areas receiving low rainfall & permeable soil of medium depth. at lower ends graded channels are provided for safe disposal of runoff

## Slide 17: Conservation type bench terrace
In this type of terrace:
Modified form of level terrace
Use moisture of uncropped area
Barrier is established across the land at suitable interval and the terrace is developed by pushing soil downhill and subsequent natural leveling.

## Slide 19: Advantages
Reduces the soil erosion.
Aesthetical value
Intensive land use.
Economically beneficial.
Availability of food for local area.
Flood chances can be reduce.
Improves the condition of the slope for plant establishment.
Reduces runoff velocities and increases infiltration.

## Slide 20: Disadvantages
Highly labor demand and time consuming.
Increased cost relative to alternative slope stabilization techniques.
Can be complicated to design and install, and may fail if not properly designed and installed

## Slide 21: Some examples over the world

## Slide 22
Terraces in northern Luzon Philippines 2000-B.C

## Slide 23: Citrus Orchard in southern France

## Slide 24: Lebanon hill side

## Slide 25: Level bench terracing in Japan

## Slide 26: Tea on bench terraces, Bhutan

## Slide 27
Outward bench terrace in Korea

## Slide 28
Terraces on eroded soils of Israel

## Slide 29
Terraced Fields in Sa Pa, Vietnam

## Slide 30
Rice Terrace Panorama in Bali

## Slide 31
Swat Valley, Pakistan

## Slide 32: Grassy Terraces in Chitral, Pakistan

## Slide 33: Kashmir, Pakistan

## Slide 34: Thank You