## Slide 1: Introduction to Remote Sensing

## Slide 2
Remote Sensing
Part I

## Slide 3: What is Remote Sensing ?
Remote sensing is the measurement or acquisition of data and information about objects or phenomenon on the Earth’s surface, by sensors that are mounted on platforms located at a distance and are not in physical contact with the object or phenomenon under study (formal definition of the ASPRS )
These sensors make measurements (usually multispectral) of interactions between the targets and the electromagnetic radiation.
Notes: Remote Sensing is both an art and a science
Science: Using sophisticated sensors to measure the amount of em energy exiting an object or geographic area from a distance and then extracting valuable information from the data using mathematically and statistically based algorithms – is a scientific activity
Art: Process of visual photo or image interpretation brings to bear not only scientific knowledge but all of the background that a person has obtained through a lifetime. Such learning cannot be measured, programmed, or completely understood.
  Information about an object or area
    Electromagnetic energy emitted or reflected from an object or geographic area turned into information using visual and/or digital image processing techniques
  Instrument (Sensor)
    Remote sensing is performed using an instrument, often referred to as a sensor.
    Our emphasis is on instruments that record electromagnetic radiation (emr) that travels at 3x108 m/s
    EMR represents an extremely efficient high-speed communications link between the sensor and the remotely located phenomenon
    Changes in the amount and properties of emr become, upon detection by the sensor, a valuable source of data for interpreting important properties of the phenomenon
  Distance (How far is remote?)
    No clear distinction about how great this distance should be.
    Our emphasis this semester is on orbital satellite platforms placed in the vacuum of space
Other sensors use other mediums such as magnetic fields, sound waves, etc. (E.g., gravity anomalies)

## Slide 4
History of Remote Sensing
Notes: With this oblique view, we can visualize Southern California's dramatic topography. This image of Southern California, from the desert at Mojave to the ocean at Ventura, shows a variety of landscapes and environments. This perspective view was generated by draping a Landsat satellite image over a preliminary topographic map from the Shuttle Radar Topography Mission. It shows the Tehachapi Mountains in the right foreground, the city of Ventura on the coast at the distant left, and the easternmost Santa Ynez Mountains forming the skyline at the distant right.

## Slide 5
Paris, 1859
Notes: Gaspard Felix Tournachon, also known as Nadar, was a famous French photographer and balloonist who carried his bulky cameras aloft. His goal was to make land surveys from aerial photographs. Although Nadar set the stage for the future of remote sensing as we know it, he was not a success at aerial surveying. His photographic observations did, however, catch the attention of the military.

## Slide 6
Notes: In April 1861 Professor Thaddeus Lowe went up in a balloon near Cincinnati, Ohio, to make a weather observation. Unfortunately, strong winds carried him all the way to South Carolina, where he was arrested as a Union spy. Eventually released, he believed that tethered balloons could be useful for reconnaissance. After viewing a demonstration, President Lincoln agreed and authorized the US Army Balloon Corps, with Lowe in charge. Despite its advantage to the North during the American Civil War, the unit was deactivated in 1863. Balloons had a not-surprising tendency to draw enemy fire.
One of the most famous of the Civil War balloons was made by the Confederacy of donated undergarments of the ladies of the South. These were all silk and the only source of silk the South had at the time. It was hoped that it would counter the shocking success of Union balloons which were providing airborne intelligence of opposing troop movements that was proving devastating. The southern patchwork balloon only flew once before it was captured by the Union, a disappointment and an afront for which General Longstreet claimed he never found it in his heart to forgive the Union.

## Slide 8
Notes: The Bavarian Pigeon Corps: 1903 An innovative attempt to avoid dangerous balloons or uncertain kites was to attach a very light camera to a carrier pigeon. These cameras took a picture every thirty seconds as the pigeon winged its way along a straight course to its home shelter. Releasing the birds behind enemy lines presented no small problem. In addition, the pigeons were rather tasty to hungry troops who shot them down.

## Slide 9
Actual Pigeon Pictures

## Slide 10
Post-quake San Francisco,
1906
Notes: These photographs, taken from a balloon, were taken after the earthquake of 1906. It illustrates the synoptic view and the historical record factor of remote sensing.

## Slide 11
Wilbur Wright and his first aerial photograph of France.
Notes: Wilbur Wright was the pilot for two notable events in remote sensing history. The first photographs from an aircraft were taken by Wilbur's passenger, L. P. Bonvillain, on a demonstration flight in France in 1908. The next year, the first aerial motion pictures were taken in Italy when another photographer accompanied Wright. Soon everyone was enjoying pictures of peaceful countryside scenes from the air.

## Slide 12
The remote Sensing System Requirements
1. Energy Source or Illumination (A) - which illuminates or provides electromagnetic energy to the target of interest.
2. Radiation and the Atmosphere (B) - as the energy travels from its source to the target, it will come in contact with and interact with the atmosphere it passes through.
3. Interaction with the Target (C) - once the energy through the atmosphere, it interacts with the target depending on the properties of both the target and the radiation.

## Slide 13
4. Recording of Energy by the Sensor (D) - after the energy has been scattered by, or emitted from the target, we require a sensor (remote - not in contact with the target) to collect and record the electromagnetic radiation.
5. Transmission, Reception, and Processing (E) - the energy recorded by the sensor has to be transmitted, often in electronic form, to a receiving and processing station where the data are processed into an image (hardcopy and/or digital).
The remote Sensing System Requirements (continued)

## Slide 14
6. Interpretation and Analysis (F) - the processed image is interpreted, visually and/or digitally or electronically, to extract information about the target which was illuminated.
7. Application (G) - the final element of the remote sensing process is achieved when we apply the information we have been able to extract from the imagery about the target in order to better understand it, reveal some new information, or assist in solving a particular problem.
The remote Sensing System Requirements (continued)

## Slide 15
Maps
GIS
Layers
Information
and
Reports
Processing
Analysis
Interpretation
Results, Output
And
Applications
Decision
Making
E
E
F
G
G
The remote Sensing System Requirements

## Slide 16: Electromagnetic Energy and Electromagnetic Radiation EME & EMR

## Slide 17: Electromagnetic Radiation
ElectroMagnetic Energy EM
Methods of energy transfer
ElectroMagnetic Radiation EMR
ElectroMagnetic spectrum
Radiation-matter interactions
EMR-atmosphere interactions
EM-surface interactions

## Slide 18: Electromagnetic Energy
Electromagnetic energy – a dynamic form of energy that is caused by the oscillation or acceleration of an electrical charge.
All natural and synthetic substances above absolute zero (0o K, or Kelvin = - 273.16oc) emit a range of electromagnetic energy.
Practically all the natural electromagnetic energy injected into the earth system is produced by the SUN.
Sun

## Slide 19: Methods of Energy transfer
Energy is defined as the capacity of a physical system to perform work :
    mechanical,
    chemical,
    electrical,
    heat, Electromagnetic, …. etc.
The result of the work being done is: energy transfer.
Energy transfer can be accomplished by one of three methods:
    conduction
    convection and
    Radiation
Types of Energy

## Slide 20: Conduction
Direct transfer of energy with physical contact.
The efficiency of energy transmission is related to the area of surface contacts.
Most important in solids, of intermediate importance in liquids and least important in gasses.

## Slide 21: Convection
Energy transfer by the physical movement of molecules.
Possible only in liquids and gasses.
Hot molecules move up
Cold molecules move down

## Slide 22: Radiation
This is energy transfer with which we are primarily concerned in remote sensing.
Energy transferred from one body to another in the absence of an intervening material medium.
The medium (if any) must be sufficiently transparent.
The only method that solar energy reaches the earth.

## Slide 23: Electromagnetic Radiation (EMR)
Electromagnetic energy in transit can be detected when it interacts with matter.
In the absence of matter (in a vacuum) EMR travels at the speed of light (299,792.8km/sec=3x108m/sec).
In matter the speed is slightly slower
  – the denser the matter, the slower the speed.
EMR can be described by wave and particle models.

## Slide 24: The wave model of EMR
EMR is carried by a series of continuous waves that are equally and repetitively space in time.
Two fluctuating fields
  one Electric and
  the other Magnetic.
They are perpendicular to each other and both are perpendicular to the direction of propagation (transverse waves).

## Slide 25
Two important characteristics of electromagnetic radiation for understanding remote sensing:
1. The wavelength () is the length of one wave cycle, which can be measured as the distance between successive wave crests.
  Wavelength is measured in metres (m)
  or some factor of metres such as:
    nanometres (nm, 10-9 metres), or
    micrometres (mm, 10-6 metres) or
    centimetres (cm, 10-2 metres).
2. Frequency (n) refers to the number
of cycles of a wave passing a fixed point per unit of time.
  - Frequency is normally measured in hertz (Hz), equivalent to one cycle per second, and various multiples of hertz.
Electromagnetic Radiation (EMR)

## Slide 26: The Wave Nature of EMR
Wavelength and frequency are related by the following formula:
C = l n
Where l = wavelength (m)
n = frequency (cycles per second, Hz)
c = speed of light (3x108 m/s)

## Slide 27: Wavelength and Frequency
Four different type of electromagnetic waves, illustrating the inverse relationship between wavelength and frequency

## Slide 28: Electromagnetic Spectrum
The range of wavelengths known as the electromagnetic spectrum. Our eyes can only see a small part of this energy known as visible light (see zone marked “visible light”).
green
red
blue
0.4 0.5 0.6 0.7 micrometers
1 m = 109 nanometer = 1000 000 000 nanometer
1 m = 106 micrometer = 1000 000 micrometer
1 mm = 1000 micrometer
1 cm = 10000 micrometer

## Slide 29: Colors of visible Spectrum
Colours of the visible spectrum produced when a beam of white light is passed through a glass prism. White light can also be divided into the three primary colours – blue, green and red.

## Slide 30: Color Mixing
Color mixing processes:
(a) Color additive process, operative when lights of different colors are superimposed;
(b) Color subtractive process, operative when dyes of different colors are superimposed. (Courtesy Eastman Kodak Company.)

## Slide 32: The additive primary colors
RED
BLUE
GREEN
Blue + Red Magenta
Blue + Green Cyan
Red + Green Yellow
Blue + Green + Red White

## Slide 34: RED GREEN BLUE
Normal Colors
Composite

## Slide 35: The Particle Model of EMR
Emphasises the behaviour of EMR as if EMR were composed of a collection of discrete, particle-like objects.
They are called quanta or photons.
They carry particle-like properties such as energy and momentum from source, but have no mass.
E.g. industrial laser, light meter and film.

## Slide 36: The Particle Nature of EMR
The intensity of EMR is directly related to the number of photons present, and the energy of a quantum is given as:
Q = h n = h c / l
  Where
    Q = Energy of a photon in Joules
    h = Planck’s constant = 6.626 x 10-34 Joules sec.
    n = Frequency (Hz)
    l = Wavelength (m)

## Slide 37: Common Sources of Artificial Electromagnetic Energy
Source | Primary Energy Type
Pet (Position emission Tomography) scanner | Gamma
X-ray tube | X ray
CAT (Computer-Assisted Tomography) Scanner | X ray
Sunlamp | Ultraviolet
Blacklamp | Ultraviolet
Electronic flash (camero | Visible
Laser | Visible
Internal combustion engine | Infrared
Heat lamp | Infrared
Microwave oven | Microwave
Weather radar | Microwave
Maser | Microwave
UFF Television Broadcast | Microwave
VHF Television Broadcasts | Radio
AM and FM radio broadcasts | Radio

## Slide 38: Sun’s Radiant Energy Distribution at 6,000oK
Spectral Region | Wavelength (μm) | % Total Energy
Gamma and X rays | <0.01 | 0.02 %
Far UV | 0.01 – 0.2 | 
Middle UV | 0.2 – 0.3 | 1.95 %
Near UV | 0.3 – 0.4 | 5.32 %
Visible | 0.4 – 0.7 | 43.50 %
Near IR | 0.7 – 1.5 | 36.80 %
Middle IR | 1.5 – 5.6 | 12.00 %
Far IR | 5.6 – 1,000 | 0.41 %
Microwave and radio waves | > 1,000 | 
Total |  | 100.00 %
92%

## Slide 39: Stefan – Boltzman Law
M = σT 4
Where
  M = Total radiant exitance from surface (W/m2)
  σ = Stefan – Boltzmannn constant = 5.6697 x 10-8 Wm-2K-4
  T = Absolute temperature (K) of the surface
  The law is expressed for a blackbody

## Slide 40: Blackbody
A blackbody is a hypothetical, ideal radiator that totally absorbs and re-emits all energy incident upon it. Actual objects only approach this ideal (Lillesand and Kiefer, 1994)

## Slide 41: The Source of EMR
All matter in the universe that is warmer than 0o K (-273.16oC) emit electromagnetic energy.
Molecular motion stops at 0o K thus it is called absolute zero.
All objects in our life are warmer than the absolute zero, thus, everything is a source of EMR.
The amount and type of the emitted energy depends on the temperature of the object.
The hotter objects emit more energy with shorter wavelengths (e.g. stove).
High temperature
Low temperature

## Slide 42: Spectral Distribution of Energy Radiated from Blackbodies of various Temperatures
Spectral distribution of energy radiated from blackbodies of various temperatures. (Note that Spectral radiant exitance M is the energy emitted per unit wave length. Total radiant exitance M is given by the area under the spectral radiant exitance curves.)

## Slide 43: Dominant Wavelength
Wien’s displacement law:
l m = A / T
Where:
l m = Wavelength of maximum emittance (μm)
A = 2898 μm K
T = Temperature (in oKalvin)

## Slide 44: Blackbody, Greybody and Selective Radiator
A Blackbody
B Greybody
C Selective Radiator
l

## Slide 45: Electromagnetic Spectrum
The entire range of EMR comprises the Electromagnetic Spectrum.
From the sun, the electromagnetic spectrum stretches from biological lethal gamma rays to passive radio waves.
Spectral bands – named divisions

## Slide 46
Electromagnetic Spectrum

## Slide 47: Radiation-Matter Interactions
EMR that impinges upon matter is called incident radiation.
When incident radiation hit the earth, it may be transmitted, reflected, scattered or absorbed, depending on:
  Properties of the medium.
  The wavelength of the incident radiation
  Incident angle

## Slide 48: Transmission, Reflection, Scattering, and Absorption
Depends on :
1- Properties of medium
2- Incident angle
3- Wavelength

## Slide 49: Effects of the Atmosphere
EM radiation used for remote sensing has to travel through some distance of the particles and gases in the atmosphere which can affect the incoming light and radiation.
These effects are caused by the mechanisms of scattering and absorption.
Scattering occurs when particles or large gas molecules in the atmosphere interact with the electromagnetic radiation and redirects it from its original path.
How much scattering takes place depends on several factors including:
  The wavelength of the radiation,
  The abundance of particles or gases,
  The distance the radiation travels through the atmosphere.
There are three (3) types of scattering which take place.
Scattering

## Slide 50: Rayleigh Scattering
Rayleigh scattering occurs when particles are very small compared to the wavelength of the radiation.
These could be particles such as small specks of dust or nitrogen and oxygen molecules.
Rayleigh scattering causes shorter wavelengths of energy to be scattered much more than longer wavelengths.
Rayleigh scattering is the dominant scattering mechanism in the upper atmosphere.
The fact that the sky appears “blue” during the day is because of this phenomenon.

## Slide 51: Mie Scattering
Occurs when the particles are just about the same size as the wavelength of the radiation.
Dust, pollen, smoke and water vapor are common causes of Mie scattering which tends to affect longer wavelengths than those affected by Rayleigh scattering.
Occurs mostly in the lower portions of the atmosphere where larger particles are more abundant, and dominates when cloud conditions are overcast.

## Slide 52: Nonselective Scattering
This occurs when the particles are much larger than the wavelength of the radiation.
Water droplets and large dust particles can cause this type of scattering.
Nonselective scattering gets its name from the fact that all wavelengths are scattered about equally.
This type of scattering causes fog and clouds to appear white to our eyes because blue, green, and red light are all scattered in approximately equal quantities (blue+green+red light = white light).

## Slide 53: EMR-Atmosphere Interaction
Diversions and depletions occurs as solar and terrestrial radiation interact with the earth’s atmosphere.
Wavelength selective.
  Transmission bands (atmospheric windows)
  Absorption bands (atmospheric blinds)

## Slide 54: Absorption
Absorption is the other main mechanism at work when electromagnetic radiation interacts with the atmosphere.
In contrast to scattering, this phenomenon causes molecules in the atmosphere to absorb energy at various wavelengths.
Ozone, carbon dioxide, and water vapor are the three main atmospheric constituents, which absorb radiation.
Absorption

## Slide 55
Atmospheric Windows
Gases absorb electromagnetic energy in very specific regions of the spectrum  they influence where (in the spectrum) we can "look" for remote sensing purposes
Those areas of the spectrum which are not influenced by atmospheric absorption and thus, are useful to remote sensors, are called atmospheric windows
VISIBLE المجال المرئي

## Slide 56: Spectral radiation of the Sun and the Earth
Atmospheric Windows
Wavelength
النوافـذ الطيفية
ATMOSPHERIC
SPECTRAL WINDOWS

## Slide 57: Major Windows of the Gaseous Atmosphereأهم النوافذ الطيفية للغلاف الجوي
* No absorption bands, but scattering can be very troublesome for UV wave lengths and the shorter wavelengths of visible light.
Atmospheric Window | Radiation Type
0.3 – 1.1 μm * | UV, visible, reflected IR
1.5 – 1.8 μm | Reflected IR
2.0 – 2.4 μm | Reflected IR
3.0 – 5.0 μm | Thermal IR
8.0 – 14.0 μm (below ozone layer) | Thermal IR
10.5 – 12.5 μm (above ozone layer) | Thermal IR
>0.5 cm | Microwave

## Slide 58: Radiation – Target Interaction
Radiation that is not absorbed or scattered in the atmosphere can interact with the Earth’s surface.
There are number of interactions that can take place when energy strikes, or is incident (I) upon the surface.
These are: absorption (A); transmission (T); and reflection (R).
The total incident energy will interact with the surface in one or more of these three ways.
The proportions of each will depend on the wavelength of the energy and the material and condition of the feature.
Absorption (A) occurs when radiation is absorbed into the target.
Transmission (T) occurs when radiation passes through a target.
Reflection (R) occurs when radiation “bounces” off the target and is redirected.
In remote sensing, we are most interested in the radiation reflected from targets.
We refer to two types of reflection, which represent the two extreme ends of the way in which energy is reflected from a target:
  Specular reflection and
  Diffuse reflection

## Slide 59: Illustrative Examples
Diffuse Reflection
Specular Reflection

## Slide 60: Reflectance Properties
When a surface is smooth we get specular or mirror-like reflection where all (or almost all) of the energy is directed away from the surface in a single direction.
Diffuse reflection occurs when the surface is rough and the energy is reflected almost uniformly in all directions. Most earth surface features lie somewhere between perfectly specular or perfectly diffuse reflectors.
Whether a particular target reflects specularly or diffusely, or somewhere in between, depends on the surface roughness of the feature in comparison to the wavelength of the incoming radiation.
If the wavelengths are much smaller than the surface variations or the particle sizes that make up the surface, diffuse reflection will dominate.
For example, fine-grained sand would appear fairly smooth to long wavelength microwaves, but would appear quite rough to the visible wavelengths.

## Slide 61: Basic Interactions between Electromagnetic Energy and an Earth Surface Feature
EI(l) = ER(l) + EA(l) + ET(l)
EI(l) = Incident Energy
ER(l) = Reflected Energy
EA(l) = Absorbed Energy
ET(l) = Transmitted Energy

## Slide 62: EMR – Surface Interaction
Albedo – spectral reflectance R (l): the average amount of incident radiation reflected by an object at some wavelength interval.
    R(l) = ER (l) / EI (l) x 100
Where
ER (l) = Reflected radiant energy
EI (l) = Incident radiant energy

## Slide 63: Target Properties - Vegetation
Leaves: Chlorophyll strongly absorbs radiation in the red and blue wavelengths but reflects green wavelengths.
Leaves appear “greenest” to us in the summer, when chlorophyll content is maximum.
In autumn, there is less chlorophyll in the leaves, so there is less absorption and more reflection of the red wavelengths, making the leaves appear red or yellow as a combination of red and green wavelengths).
The internal structure of healthy leaves act as excellent diffuse reflectors of near-infrared wavelengths.
If our eyes were sensitive to near-infrared, trees would appear extremely bright to us at these wavelengths. In fact, measuring and monitoring the near-IR reflectance is one way that scientists can determine how healthy (or unhealthy) vegetation.
B
G
R
IR
G
IR
B
G
R
IR
G
IR

## Slide 64: Target Properties - Water
Water: Longer wavelength of visible and near infrared radiation is absorbed more by water than shorter visible wavelengths.
Water, looks blue or blue-green due to stronger reflectance at these shorter wavelengths.
Water looks darker if viewed at red or near infrared wavelengths.
If there is suspended sediment present in the upper layers of the water body, then this will allow better reflectivity and a brighter appearance of the water.
The apparent color of the water will show a slight shift to longer wavelengths. Suspended sediment (S) can be easily confused with shallow (but clear) water, since these two phenomena appear very similar.
Chlorophyll in algae absorbs more of the blue wavelengths and reflects the green, making the water appear more green in color when algae is present.
The topography of the water surface (rough, smooth, floating materials, etc.) can also lead to complication for water related interpretation due to potential problems of specular reflection and other influences on color and brightness.
B
G
R
IR
B
G
R
IR
B
G
R
IR
Sand (S)