## Slide 1: Chapter 4 The Components of the System Unit

## Slide 2: Chapter 4 Objectives
Differentiate among various styles of system units
Identify chips, adapter cards, and other components of a motherboard
Describe the components of a processor and how they complete a machine cycle
Identify characteristics of various personal computer processors on the market today
Define a bit and describe how a series of bits represents data
Explain how programs transfer in and out of memory
Differentiate among the various types of memory
Describe the types of expansion slots and adapter cards
Explain the differences among a serial port, a parallel port, a USB port, a FireWire port, and other ports
Describe how buses contribute to a computer’s processing speed
Identify components in mobile computers and mobile devices
Next
Understand how to clean a system unit

## Slide 3: The System Unit
What is the system unit?
p. 184 Fig. 4-1
Next
  Case that contains electronic components of the computer used to process data
    Sometimes called the chassis

## Slide 4: The System Unit
What are common components inside the system unit?
p. 185 Fig. 4-2
Next
  Memory
  Adapter cards
    Sound card
    Video card
  Drive bays
  Power supply
  Processor

## Slide 5: The System Unit
What is the motherboard?
p. 186 Fig. 4-3
Next
  Main circuit board of the system unit
  Contains expansion slots, processor chips, and memory slots
  Also called system board
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click Motherboards below Chapter

## Slide 6: The System Unit
What is a chip?
p. 186
Next
  Small piece of semi-conducting material on which integrated circuits are etched
    Integrated circuits contain many microscopic pathways capable of carrying electrical current
  Chips are packaged so that they can be attached to a circuit board

## Slide 7: Processor
Processor
Control Unit
Arithmetic Logic Unit (ALU)
Arithmetic Logic Unit (ALU)
What is the central processing unit (CPU)?
p. 186 - 187 Fig. 4-4
Next
Input Devices
Storage Devices
Output Devices
  Interprets and carries out basic instructions that operate a computer
Memory
Data
Information
Instructions Data Information
Instructions Data Information
Control Unit
    Control unit directs and coordinates operations in computer
    Arithmetic logic unit (ALU) performs arithmetic, comparison, and logical operations
  Also called the processor

## Slide 8: Processor
What are multi-core processors?
p. 187
Next
A multi-core processor is a chip with two or more separate processors
A dual-core processor is a single chip that contains two separate processors
A quad-core processor is a single chip that contains four separate processors
Each processor on a multi-core chip generally runs at a slower clock speed, but increases overall performance
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click Quad-Core Processors below Chapter 4

## Slide 9: Processor
Processor
Control Unit
Memory
ALU
What is a machine cycle?
p. 188 Fig. 4-5
Next
Step 1. Fetch Obtain program instruction or data item from memory
Step 2. Decode Translate instruction into commands
Step 4. Store Write result to memory
Step 3. Execute Carry out command
  Four operations of the CPU comprise a machine cycle

## Slide 10: Processor
What is pipelining?
p. 189 Fig. 4-6
Next
  Processor begins fetching second instruction before completing machine cycle for first instruction
  Results in faster processing

## Slide 11: Processor
Stores location from where instruction was fetched
Stores instruction while it is being decoded
What is a register?
p. 189
Next
Stores data while ALU computes it
Stores results of calculation
  Temporary high-speed storage area that holds data and instructions

## Slide 12: Processor
What is the system clock?
p. 189 - 190
Next
Each tick is a clock cycle
Pace of system clock is clock speed
Most clock speeds are in the gigahertz (GHz) range (1 GHz = one billion ticks of system clock per second)
Processor speed can also be measured in millions of instructions per second (MIPS)
  Controls timing of all computer operations
  Generates regular electronic pulses, or ticks, that set operating pace of components of system unit

## Slide 13: Processor
What are the guidelines for selecting a processor?
p. 192 Fig. 4-8
Next

## Slide 14: Processor
What are heat sinks, heat pipes, and liquid cooling?
p. 193 Fig. 4-9
Next
  Heat sink—component with fins that cools processor
  Heat pipee—smaller device for notebook computers
  Liquid cooling—uses a continuous flow of fluids to transfer heat away

## Slide 15: Processor
What is parallel processing?
p. 194 Fig. 4-10
Next
Control Processor
Processor 1
Memory
Processor 2
Memory
Processor 3
Memory
Processor 4
Memory
results combined
  Using multiple processors simultaneously to execute a program faster
  Requires special software to divide problem and bring results together

## Slide 16: Data Representation
How do computers represent data?
p. 194 - 195 Fig. 4-11
Next
Recognize only two discrete states: on or off
Use a binary system to recognize two states
Use Number system with two unique digits: 0 and 1, called bits (short for binary digits)
  Most computers are digital

## Slide 17: Data Representation
What is a byte?
p. 195 Fig. 4-12
Next
  Eight bits grouped together as a unit
  Provides enough different combinations of 0s and 1s to represent 256 individual characters
    Numbers
    Uppercase and lowercase letters
    Punctuation marks
    Other

## Slide 18: Data Representation
What are three popular coding systems to represent data?
p. 195 Fig. 4-13
Next
  ASCII—American Standard Code for Information Interchange
  EBCDIC—Extended Binary Coded Decimal Interchange Code
  Unicode—coding scheme capable of representing all world’s languages
ASCII Symbol EBCDIC
00110000 0 11110000
00110001 1 11110001
00110010 2 11110010
00110011 3 11110011

## Slide 19: Data Representation
How is a letter converted to binary form and back?
p. 196 Fig. 4-14
Next
Step 3. The system unit converts the scan code for the capital letter T to its ASCII binary code (01010100) and stores it in memory for processing.
Step 1. The user presses the capital letter T (SHIFT+T key) on the keyboard.
Step 2. An electronic signal for the capital letter T is sent to the system unit.
Step 4. After processing, the binary code for the capital letter T is converted to an image, and displayed on the output device.

## Slide 20: Memory
What is memory?
p. 197 Fig. 4-15
Next
  Electronic components that store instructions, data, and results
  Consists of one or more chips on motherboard or other circuit board
  Each byte stored in unique location called an address, similar to seats in a concert hall

## Slide 21: Memory
How is memory measured?
p. 197 Fig. 4-16
Next
Term Abbreviation Approximate Size
Kilobyte KB or K 1 thousand bytes
Megabyte MB 1 million bytes
Gigabyte GB 1 billion bytes
Terabyte TB 1 trillion bytes
  By number of bytes available for storage

## Slide 22: Memory
What is random access memory (RAM)?
p. 198 - 199
Next
The more RAM a computer has, the faster it responds
Also called main memory or primary storage
Most RAM is volatile, it is lost when computer’s power is turned off
Memory chips that can be read from and written to by processor
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click RAM below Chapter

## Slide 23: Memory
How do program instructions transfer in and out of RAM?
p. 198 Fig. 4-17
Next
Step 1. When you start the computer, certain operating system files are loaded into RAM from the hard disk. The operating system displays the user interface on the screen.
Operating system instructions
Web browser instructions
Paint program instructions
Operating system interface
Web browser window
Paint program window
Web browser program instructions are removed from RAM
Web browser window is no longer displayed on desktop
Step 2. When you start a Web browser, the program’s instructions are loaded into RAM from the hard disk. The Web browser window is displayed on the screen.
Step 3. When you start a paint program, the program’s instructions are loaded into RAM from the hard disk. The paint program, along with the Web Browser and certain operating system instructions are in RAM. The paint program window is displayed on the screen.
Step 4. When you quit a program, such as the Web browser, its program instructions are removed from RAM. The Web browser is no longer displayed on the screen.
RAM
RAM

## Slide 24: Memory
Video: The Leopard with a Time Machine
Next
CLICK TO START

## Slide 25: Memory
Must be re-energized constantly
Do not have to be re-energized as often as DRAM
Most common type
Faster and more reliable than DRAM chips
What are two basic types of RAM chips?
p. 199
Next
  Static RAM (SRAM)
Newer Type: Magnetoresistive RAM (MRAM)
Dynamic RAM (DRAM)

## Slide 26: Memory
Where does memory reside?
p. 199 Fig. 4-18
Next
  Resides on small circuit board called memory module
  Memory slots on motherboard hold memory modules

## Slide 27: Memory
p. 199
Next
How much RAM does an application require?
  Depends on the types of software you plan to use
  For optimal performance, you need more than minimum specifications

## Slide 28: Memory
How much RAM do you need?
p. 200 Fig. 4-19
Next
  Depends on type of applications you intend to run on your computer
RAM
Use
1 GB or less
1 GB to 4 GB
4 GB and up
Home and business users managing personal finances
Using standard application software such as word processing
Using educational or entertainment CDs
Communicating with others on the Web
Users requiring more advanced multimedia capabilities
Running number-intensive accounting, financial, or spreadsheet programs
Using voice recognition
Working with videos, music, and digital imaging
Creating Web sites
Participating in video conferences
Playing Internet games
Power users creating professional Web sites
Running sophisticated CAD, 3-D design, or other graphics-intensive software

## Slide 29: Memory
What is cache?
p. 201 Fig. 4-20
Next
    L1 cache built into processor
    L2 cache slower but has larger capacity
    L2 advanced transfer cache is faster, built directly on processor chip
    L3 cache is separate from processor chip on motherboard (L3 is only on computers that use L2 advanced transfer cache)
  Helps speed computer processes by storing frequently used instructions and data
  Also called memory cache
Click to view Web Link, click Chapter 4, Click Web Link from left navigation, then click Windows ReadyBoost below Chapter 4

## Slide 30: Memory
What is read-only memory (ROM)?
p. 201 - 202
Next
Memory chips that store permanent data and instructions
Nonvolatile memory, it is not lost when computer’s power is turned off
Three types:
Firmware— Manufactured with permanently written data, instructions, or information
EEPROM (electrically erasable programmable read-only memory)— Type of PROM containing microcode programmer can erase
PROM (programmable read-only memory)— Blank ROM chip onto which a programmer can write permanently

## Slide 31: Memory
What is flash memory?
p. 202 Fig. 4-21
Next
Step 1. Purchase and download music tracks from a Web site. With one end of a special cable connected to the system unit, connect the other end to the USB port in the portable media player.
Step 2. Instruct the computer to copy the music tracks to the flash memory chip in the portable media player.
Step 3. Plug the headphones into the portable media player, push a button on the portable media player, and listen to the music through the earphones.
  Nonvolatile memory that can be erased electronically and rewritten
  Used with many mobile devices
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click Flash Memory below Chapter 4
MP3 Player
flash memory chips
USB port

## Slide 32: Memory
What is CMOS?
p. 203
Next
Uses battery power to retain information when other power is turned off
Stores date, time, and computer’s startup information
Complementary metal-oxide semiconductor memory
Used in some RAM chips, flash memory chips, and other types of memory chips

## Slide 33: Memory
What is access time?
p. 203 Figs. 4-22-4-23
Next
  Amount of time it takes processor to read data from memory
  Measured in nanoseconds (ns), one billionth of a second
  It takes 1/10 of a second to blink your eye; a computer can perform up to 10 million operations in same amount of time
Term Speed
Millisecond One-thousandth of a second
Microsecond One-millionth of a second
Nanosecond One-billionth of a second
Picosecond One-trillionth of a second

## Slide 34: Expansion Slots and Adapter Cards
What is an adapter card?
p. 204 Fig. 4-24
Next
  Enhances system unit or provides connections to external devices called peripherals
  Also called an expansion card
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click Video Cards below Chapter 4

## Slide 35: Expansion Slots and Adapter Cards
What is an expansion slot?
p. 204 - 205 Fig. 4-25
Next
  An opening, or socket, on the motherboard that can hold an adapter card
  With Plug and Play, the computer automatically configures cards and other devices as you install them

## Slide 36: Expansion Slots and Adapter Cards
What are flash memory cards, PC cards, and ExpressCard modules?
p. 205 Fig. 4-26–4-27
Next
  An ExpressCard module adds memory, storage, sound, fax/modem, communications, and other capabilities to notebook computers
  A flash memory card allows users to transfer data from mobile devices to desktop computers
  USB Flash drive
  An PC card adds various capabilities to computers
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click ExpressCard Modules below Chapter 4

## Slide 37: Ports and Connectors
What are ports and connectors?
p. 206 Fig. 4-28
Next
  Port connects external devices to system unit
  Connector joins cable to peripheral
    Available in one of two genders: male and female

## Slide 38: Ports and Connectors
What are different types of connectors?
p. 207 Fig. 4-29
Next

## Slide 39: Ports and Connectors
What is a serial port?
p. 207 Fig. 4-30
Next
  Transmits one bit of data at a time
  Connects slow-speed devices, such as mouse, keyboard, modem

## Slide 40: Ports and Connectors
What is a parallel port?
p. 208 Fig. 4-31
Next
  Connects devices that can transfer more than one bit at a time, such as a printer

## Slide 41: Ports and Connectors
Third USB device connects to second USB device, and so on
Second USB device connects to first USB device
First USB device connects to USB port on computer
Single USB port can be used to attach multiple peripherals in a daisy chain
PCs typically have six to eight USB ports on front or back of the system unit
What are USB ports?
p. 208
Next
USB (universal serial bus) port can connect up to 127 different peripherals together with a single connector type
USB 2.0

## Slide 42: Ports and Connectors
What are FireWire ports?
p. 208 - 209
Next
  Connects multiple types of devices that require faster data transmission speeds
  Allows you to connect up to 63 devices together
  FireWire 800 is the latest FireWire version
  A FireWire hub is a device that plugs in a FireWire port on the system unit and contains multiple FireWire ports in which you plug cables from FireWire devices

## Slide 43: Ports and Connectors
What are special-purpose ports?
p. 209 - 210 Fig. 4-32
Next
    MIDI (Musical Instrument Digital Interface) port
    eSATA port
    SCSI port
    IrDA (Infrared Data Association) port
    Bluetooth port
  Allow users to attach specialized peripherals or transmit data to wireless devices
Click to view Web Link, click Chapter 4, Click Web Link from left navigation,
then click MIDI Ports below Chapter 4

## Slide 44: Buses
What is a bus?
p. 211 - 212 Fig. 4-35
Next
  Channel that allows devices inside computer to communicate with each other
    System bus connects processor and RAM
    Bus width determines number of bits transmitted at one time
    Word size is the number of bits processor can interpret and execute at a given time

## Slide 45: Buses
PC Card
Bus
What is an expansion bus?
p. 212
Next
  Allows processor to communicate with peripherals
USB
Bus
PCI Bus
PCI Express Bus
AGP Bus

## Slide 46: Bays
What is a bay?
p. 212 Fig. 4-36
Next
  Opening inside system unit used to install additional equipment
  Drive bays typically hold disk drives

## Slide 47: Power Supply
External peripherals might use an AC adapter, which is an external power supply
What is a power supply?
p. 213
Next
Converts AC Power into DC Power
Fan keeps system unit components cool

## Slide 48: Mobile Computers and Devices
What is a mobile computer?
p. 213 - 214 Fig. 4-37
Next
  Notebook, weighing between 2.5 and 10 pounds, or mobile device

## Slide 49: Mobile Computers and Devices
What ports are on a notebook computer?
p. 214 Fig. 4-38
Next

## Slide 50: Mobile Computers and Devices
What ports and slots are on a tablet PC?
p. 214 Fig. 4-39
Next

## Slide 51: Putting It All Together
What are suggested processor and RAM configurations based on the needs of various types of users?
p. 215 Fig. 4-40
Next

## Slide 52: Keeping Your Computer Clean
Over time, the system unit collects dust – even in a clean environment
p. 216 Fig. 4-41
Next
  Preventative maintenance requires a few basic products:

## Slide 53: Summary of the Components of the System Unit
  Components of the system unit
How memory stores data, instructions, and information
Sequence of operations that occur when a computer executes an instruction
Comparison of various personal computer processors on the market today
Chapter 4 Complete
How to clean a system unit