## Slide 1
Principles of Remote Sensing

## Slide 2: Active Sensors
Active Sensor, provide their own energy source for illumination.
The sensor emits radiation which is directed toward the target to be investigated.
The radiation reflected from that target is detected and measured by the sensor.
Advantages for active sensors include:
The ability to obtain measurements anytime, regardless of the time of day or season.
Active sensors can be used for examining wavelengths that are not sufficiently provided by the sun, such as microwaves.
However, active systems require the generation of a fairly large amount of energy to adequately illuminate targets.

## Slide 3: Radar Sensors
SLAR (Side-Looking Airborne Radar)
  Real-Aperture Radar (RAR)
  Synthetic-Aperture Radar (SAR)
SIR (Shuttle Imaging Radar)
Satellite imaging radar systems
  Seasat – NASA
  ERS-1 – European Space Agency
  JERS-1 – Japan
  Radarsat - Canada

## Slide 5: Side Looking Airborne Radar (SLAR) system
11/24/2020
ESR 421 Principles of Remote Sensing
5
Nadir point
river
hill

## Slide 6: Band designations and Radar Wavelengths
11/24/2020
ESR 421 Principles of Remote Sensing
Band designation | Wavelength range (cm) | Common wavelengths for imaging (cm)
Ka | 0.8 - 1.1 | 0.86
K | 1.1 - 1.7 | 
Ku | 1.7 - 2.4 | 
X | 2.4 - 3.8 | 3.0, 3.2
C | 3.8 - 7.5 | 6.0
S | 7.5 - 15.0 | 
L | 15.0 - 30.0 | 23.5, 24.0, 25.0
P | 30.0 - 100.0 | 68.0
03/06/1431
6

## Slide 7
Uses the microwave range of the Electromagnetic spectrum ( wave lengths in cm)
It does not depend on the sun energy because it has its own energy and it can operate day time or at night
It has the ability to penetrate the clouds and dust due to its long wave length
It has the ability to penetrate dry sand to a depth of few meters (4 - 5 m) showing buried channels, wadies, structures, and archeological features.
The shadow effect helps in enhancing the visual appearance of relief and terrain structure making radar imagery excellent for :
  Topographic mapping
  Identifying geologic structures
  Study of sea and ocean waves
Characteristics of RADAR remote sensing systems

## Slide 10: Radarsat-1 SAR image
11/24/2020
ESR 421 Principles of Remote Sensing
10
Radarsat-1 C-band SAR image with horizontal polarization sending/receiving (HH) acquired on 03 August 1996 at Lac Volant, P. Quebec, Canada. The geological structures are clearly seen on this radar image.

## Slide 13: RADARSAT
11/24/2020
ESR 421 Principles of Remote Sensing
13
Launched 1995
1st Canadian Remote Sensing Satellite Canada Space Agency
A cooperative effort:
  The Canadian Government
  The Private Sector
  The United States Government
Sun –synchronous near polar orbit,
Orbit inclination from the equator is 98.6o
It takes ~ 100 min to circle the Earth
793 – 821 km orbit,
repeat every 24 days
Sensor: C-band SAR

## Slide 14: RadarSat- 1 SAR modes of Operation
11/24/2020
14

## Slide 15
RadarSat-2 SAR modes of Operation

## Slide 16
RadarSat-2 SAR modes of Operation

## Slide 17
Paris, France

## Slide 18
Iqaluit, Nunavut, Canada

## Slide 19
Greenland