## Slide 1: Lecture 4: Boolean Algebra & Expressions
Engr. Muhammad SaadUllah

## Slide 2: Out Line
Introduction to Boolean algebra
Theorems and Postulates
Prove of Theorems
Gates circuits
Assignment
Question & Answers

## Slide 3: Boolean Algebra
An algebra that deals with binary number system
George Boole (1815-1864), an English mathematician, developed it for:
Simplifying representation
Manipulation of propositional logic
In 1938, Claude E. Shannon proposed using Boolean algebra in design of relay switching circuits
Provides economical and straightforward approach
Used extensively in designing electronic circuits used in computers

## Slide 4
Boolean algebra, like any other deductive mathematical system, may be defined with a set of elements, a set of operators, and a number of unproved axioms or postulates.
The postulates of a mathematical system from the basic assumptions from which it is possible to deduce the rules, theorems, and properties of the systems.

## Slide 5: AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA
In 1854, George Boole developed an algebraic system now called Boolean algebra
In 1938, Claude E. Shannon introduced a two‐valued Boolean algebra called switching algebra that represented the properties of bistable electrical switching circuits
For the formal definition of Boolean algebra, we shall employ the postulates formulated by E. V. Huntington in 1904.

## Slide 6: Boolean Operations & Expressions
Variable – a symbol used to represent a logical quantity.
Complement – the inverse of a variable and is indicated by a bar over the variable.
Literal – a variable or the complement of a variable

## Slide 7: Fundamental Concept of Boolean Algebra
Use of Binary Digit
Boolean equations can have either of two possible values, 0 and 1
Logical Addition Symbol ‘+’, also known as ‘OR’ operator, used for logical addition. Follows law of binary addition
Logical Multiplication Symbol ‘.’, also known as ‘AND’ operator, used for logical multiplication. Follows law of binary multiplication
Complementation Symbol ‘-’, also known as ‘NOT’ operator, used for complementation. Follows law of binary compliment

## Slide 8: Fundamental Concept of Boolean Algebra
The postulates of a mathematical system form the basic assumptions from which it is possible to deduce the rules, theorems, and properties of the system.
The most common postulates are
1. Closure “A set S is closed with respect to a binary operator if, for every pair of elements of S, the binary operator specifies a rule for obtaining a unique element of S. For example, the set of natural numbers N = {1, 2, 3, 4, } is closed with respect to the binary operator + by the rules of arithmetic addition, since, for any a, b belong to N, there is a unique c belong to N such that
a + b = c.

## Slide 9
Logic Gate Symbols and Behavior
Logic gates have special symbols:
And waveform behavior in time as follows:
X
0
0
1
1
Y
0
1
0
1
X
·
Y
(AND)
0
0
0
1
X
+
Y
(OR)
0
1
1
1
(NOT)
X
1
1
0
0
OR gate
X
Y
Z
=
X
+
Y
X
Y
Z
=
X
·
Y
AND gate
X
Z
=
X
NOT gate or
inverter

## Slide 10
Laws & Rules of Boolean Algebra
The basic laws of Boolean algebra:
  The Commutative laws
  The Associative laws
  The Distributive laws

## Slide 11
Commutative Laws
The commutative law of addition for two variables is written as: A+B = B+A
The commutative law of multiplication for two variables is written as: AB = BA
A
B
A+B
B
A
B+A
A
B
AB
B
A
BA

## Slide 12
Associative Laws
The associative law of addition for 3 variables is written as: A+(B+C) = (A+B)+C
The associative law of multiplication for 3 variables is written as: A(BC) = (AB)C
A
B
A+(B+C)
C
A
B
(A+B)+C
C
A
B
A(BC)
C
A
B
(AB)C
C
B+C
A+B
BC
AB

## Slide 13
Distributive Laws
The distributive law is written for 3 variables as follows: A(B+C) = AB + AC
B
C
A
B+C
A
B
C
A
X
X
AB
AC
X=A(B+C)
X=AB+AC

## Slide 14
2. Associative law.
A binary operator * on a set S is said to be associative whenever (x * y) * z = x * (y * z) for all x, y, z, €S
3. Commutative law.
A binary operator * on a set S is said to be commutative whenever x * y = y * x for all x, y , € S

## Slide 15
4. Identity element.
A set S is said to have an identity element with respect to a binary operation * on S if there exists an element e € S with the property that
e * x = x * e = x for every x € S

## Slide 16
5. Inverse.
A set S having the identity element e with respect to a binary operator * is said to have an inverse whenever, for every x € S, there exists an element y € S such that x * y = e Example:
the inverse of an element a is (-a),
since
a + (-a) = 0.

## Slide 17
6. Distributive law.
If * and . are two binary operators on a set S, * is said to be distributive over . Whenever
x * (y . z) = (x * y) . (x * z)

## Slide 18
The operators and postulates have the following meanings:
1. The binary operator + defines addition. 2. The additive identity is 0. 3. The additive inverse defines subtraction. 4. The binary operator . defines multiplication. 5. The multiplicative identity is 1. For a ≠ 0, the multiplicative inverse of a = 1>a defines division (i.e., a . 1>a = 1 ).
6. The only distributive law applicable is that of . over +: a . (b + c) = (a . b) + (a . c)

## Slide 19
Boolean algebra is an algebraic structure defined by a set of elements, B, together with two binary operators, +and . , provided that the following (Huntington) postulates are satisfied:
(a) The structure is closed with respect to the operator +. (b) The structure is closed with respect to the operator . .
(a) The element 0 is an identity element with respect to +; that is,
x + 0 =0 + x = x. (b) The element 1 is an identity element with respect to . ; that is,
x . 1 = 1 . x = x.
3. (a) The structure is commutative with respect to +; that is,
x + y = y + x. (b) The structure is commutative with respect to . ; that is, x . y = y . x

## Slide 20
4. (a) The operator . is distributive over +; that is,
x . (y + z) = (x . y) + (x . z) (b) The operator + is distributive over . ; that is,
x + (y . z) = (x + y) . (x + z) 5. For every element x € B, there exists an element x € B (called the complement of x) such that (a) x + x’= 1 and (b) x . x’ = 0. 6. There exist at least two elements x, y € B such that
x ≠ y.

## Slide 21: Two-Valued Boolean Algebra
.
These rules are exactly the same as the AND, OR, and NOT operations, respectively, defined in Table above. We must now show that the Huntington postulates are valid for the set B = {0, 1} and
the two binary operators + and .

## Slide 23
We have just established a two‐valued Boolean algebra having a set of two elements, 1 and 0, two binary operators with rules equivalent to the AND and OR operations, and a complement operator equivalent to the NOT operator.

## Slide 24
Theorems

## Slide 29
Operator Precedence
The operator precedence for evaluating Boolean expressions is
parentheses,
NOT
AND, and
OR.
In other words, expressions inside parentheses must be evaluated before all other operations.
Example: F = A(B + C)(C + D)

## Slide 30
Consider an example F(X, Y, Z) = X Y + Y Z

## Slide 31
”
Using Switches
  Inputs:
    logic 1 is switch closed
    logic 0 is switch open
  Outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT input:
    logic 1 is switch open
    logic 0 is switch closed
Logic Function Implementation
Switches in series => AND
Switches in parallel => OR
C
Normally-closed switch => NOT

## Slide 32
Gate implementation of F1 = x+yz

## Slide 34: Boolean Analysis of Logic Circuits
Boolean algebra provides a concise way to express the operation of a logic circuit formed by a combination of logic gates
  so that the output can be determined for various combinations of input values

## Slide 36: Constructing a Truth Table for a Logic Circuit
Once the Boolean expression for a given logic circuit has been determined, a truth table that shows the output for all possible values of the input variables can be developed.
  Let’s take the previous circuit as the example:
  A(B+CD)
  There are four variables, hence 16 (24) combinations of values are possible.

## Slide 38
Assignment
Gates can be combined.
The output of one gate can become the input of another.
Try to determine the logic table for this circuit.
Show that a’b’+ab+a’b = a’+b
Show that (a’b’+c)(a+b)(b’+ac)’ = a’bc

## Slide 39: Assignment

## Slide 40: References
Digital Design by M Morris Mnao
Computer Fundamentals- Pradeep K.Sinha & Proti Shina

## Slide 41
THANK YOU!
QUESTIONS