## Slide 1: Network Design and Management
Course Objective
Learning Outcomes
Syllabous

## Slide 2: Computer Network?
“interconnected collection of autonomous computers connected by a single technology” [Tanenbaum]
What is the Internet?
  “network of networks”
  “collection of networks interconnected by routers”
  “a communication medium used by millions”
  Email, chat, Web “surfing”, streaming media
Internet Web
Notes: Note the stress on “single” in the definition of a Computer Network.
It is important to learn that the Internet is an example of yet another network. Network’s don’t mean the Internet!!!
The Web is not a computer network but a distributed application that runs on top of the Internet.
Next, we will get a very quick overview of the Internet.

## Slide 3: The “nuts and bolts” view of the Internet
Network Edge
millions of connected computing devices: hosts, end-systems
  PCs workstations, servers
  PDAs phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
  Links have different bandwidth
routers: forward packets
Packet: a piece of messg.
local ISP
company
network
regional ISP
router
workstation
server
mobile
Notes: End systems or hosts (e.g., PC, laptop, servers) connect to each other via communications links.
Typically, connections are not direct; they connect to each other via switching devices called routers.
Communication links can have different bandwidths (1 Mbps ~ ADSL, 56Kbps ~ Cable Modem)
End systems and other pieces of the Internet run protocols which control the sending/receiving of information within the Internet.
End systems access the Internet via Internet Service Providers (ISP), e.g., Shaw, Telus.

## Slide 4: Applications (1)
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
Client/server model is applicable in an intranet.
Notes: One should note that client/server applications can be developed for any network (again, recall that the Internet is a type of network).
For example, an office could have an intranet and a tailored made client/server application for its needs.
Should note that growth of network applications has been facilitated to a large extent by the popularity of the WWW.
The WWW provides an interface that hides the complexity of the underlying network from the user.

## Slide 5: Applications (2)
peer-peer model:
  No fixed clients or servers
  Each host can act as both client & server
Examples: Napster, Gnutella, KaZaA

## Slide 6: A Classification of Networks
Local Area Network (LAN)
Metropolitan Area Network (MAN)
Wide Area Network (WAN)
Wireless LANs & WANs
Home Networks

## Slide 7: “internetworking”?
internetwork – interconnection of networks – also called an “internet”
Subnetwork – a constituent of an internet
Intermediate system – a device used to connect two networks allowing hosts of the networks to correspond with each other
  Bridge
  Routers
Internet is an example of an internetwork.
Notes: We just saw that there are various types of networks (e.g., LANs, MANs, WANs, wireless networks etc.)
One might want to connect different networks. Interconnecting networks is called “internetworking” in the networking jargon.
One should note that the Internet is an example of an internet!.

## Slide 8: Layered Architecture: Why?
Networks are complex with many pieces
  Hosts, routers, links, applications, protocols, hardware, software
Can we organize it, somehow?
Let’s consider a Web page request:
  Browser requests Web page from server
  Server should determine if access is privileged
  Reliable transfer page from server to client
  Physical transfer of “bits” from server to client
Notes: The idea of layering is like “data encapsulation”.
Why layering? Reduces design complexity.
Purpose of layering? Provide functionality to higher layers.

## Slide 9: Motivation Continued …
Network
Services
Application
Services
Communication
Service
Network
Services
Application
Services
Communication
Service
Web Server
Web Client
Application logic
Reliable delivery
Transfer “bits”
Notes: Note that there is no physical transfer of data across layers.
The purpose of a layer is to provide functionality to the higher layers.
One key issue is to define primitive operations and services that the lower layer will provide to the upper layer.
A service is a set of primitives (operations) that a layer provides to the layer above it.
A protocol is a set of rules governing the format & meaning of messages exchanged by peer entities within a layer.
A “network architecture” is defined as the collection of layers and protocols.
Key design issues for the layers:
addressing: a process on one machine can talk with a process on another machine
Error control: might be required if medium is not perfect.
Flow control: sender shouldn’t overwhelm the receiver
Multiplexing/demultiplexing: several connections use one logical channel
Routing: select path between source and destrination

## Slide 10: Layers, Protocols, Interfaces
Web Server
Web Client
Application logic
protocol
Reliable delivery
protocol
Transfer “bits”
protocol
Network
Services
Application
Services
Communication
Service
Network
Services
Application
Services
Communication
Service
Layer
Interface
Layer
Interface
Notes: “peer to peer” communication
Each layer is independent => one layer can be changed without affecting others.
Vendor perspective?

## Slide 11: Review
A set of layers & protocols is called a Network Architecture. These specifications enable hardware/software developers to build systems compliant with a particular architecture.
  E.g., TCP/IP, OSI

## Slide 12: Layering: Design Issues
Identify senders/receivers?
  Addressing
Unreliable physical communication medium?
  Error detection
  Error control
  Message reordering
Sender can swamp the receiver?
  Flow control
Multiplexing/Demultiplexing

## Slide 13: Models
Open Systems Interconnection (OSI) Model
TCP/IP Model
Notes: There are two well known network architectures: OSI and TCP/IP

## Slide 14: Reference Models (2)
Notes: OSI has 7 layers while TCP/IP has 4 layers.
Physical layer: transmission of bits
Data link layer: transform a raw transmission facility into a line that appears free of undetected transmission errors
Network layer: how to send data from source to destination; might traverse multiple machines. This functionality is routing.
Transport layer: type of service to the session layer; mechanism for exchange of data between end systems.
Session layer: provides mechanisms for controlling the dialogue between applications in end systems. Might not be required for most applications;
Presentation layer: syntax and semantics of information transmitted
Application layer: FTP, HTTP, Telnet etc.

## Slide 15: TCP/IP Model: History
Originally used in the ARPANET
ARPANET required networks using leased telephone lines & radio/satellite networks to interoperate
Goals of the model are:
  Seamless interoperability
  Wide-ranging applications
  Fault-tolerant to some extent
Application
Transport
Internet
Host-to-
Network

## Slide 16: The Internet Layer
End systems inject datagrams in the networks
A transmission path is determined for each packet (routing)
A “best effort” service
  Datagrams might be lost
  Datagrams might be arrive out of order
Analogy: Postal system

## Slide 17: The Transport Layer
Concerned with end-to-end data transfer between end systems (hosts)
Transmission unit is called segment
TCP/IP networks such as the Internet provides two types of services to applications
  “connection-oriented” service – Transmission Control Protocol (TCP)
  “connectionless” service - User Datagram Protocol (UDP)

## Slide 18: TCP: Connection-oriented Service
Handshaking between client & server programs
  Parameters for ensuing exchange
  Maintain connection-state
Packet switches maintain any connection-state;
  hence “connection-oriented”
Similar to a phone conversation
TCP is bundled with reliability, congestion control, and flow control.

## Slide 19: UDP: Connectionless Service
No handshaking
Send whenever and however you want
A “best effort” service
  No reliability
  No congestion & flow control services
Why is it needed?

## Slide 20: The Application Layer
Residence of network applications and their application control logic
Examples include:
  HTTP
  FTP
  Telnet
  SMTP
  DNS

## Slide 21: The Host-to-Network Layer
Somehow, host has to connect to the network and be able to send IP Datagrams
How?

## Slide 22: Internet protocol stack
application: supporting network applications
  FTP, SMTP, STTP
transport: host-host data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical
Notes: Hybrid model. More like the TCP/IP model with the link & physical layers representing the host-to-network layer.
This protocol stack is important. This book will cover all elements of the task, pretty much top-down.

## Slide 23: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 24: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
take data from app
generate “segment” according to transport protocol
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
data
transport
transport
ack

## Slide 25: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 26: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 27: Roadmap
  What is a Computer Network?
  Applications of Networking
  Classification of Networks
  Layered Architecture
  Network Core
  Delay & loss in packet-switched networks
  Internet Structure
  Transmission Media (self study)
  History (self study)

## Slide 28: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 29: Network Core: Circuit Switching
End-to-end resources reserved for “call”
Link bandwidth, switch capacity
Dedicated resources with no sharing
Guaranteed transmission capacity
Call setup required
“Blocking” may occur

## Slide 30: Network Core: Circuit Switching
Capacity of medium exceeds the capacity required for transmission of a single signal
  How can we improve “efficiency”? Let’s multiplex.
Divide link bandwidth into “pieces”:
  frequency division - FDMA
  time division – TDMA

## Slide 31: Circuit Switching: FDMA and TDMA
FDMA
frequency
time
TDMA
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 32: Network Core: Packet Switching
“store-and-forward” transmission
source breaks long messages into smaller “packets”
packets share network resources
each packet uses full link bandwidth
resource contention
  aggregate resource demand can exceed amount available
  congestion: packets queue, wait for link use

## Slide 33: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern  statistical multiplexing.
In TDM each host gets same slot in revolving TDM frame.
A
B
C
10 Mbs
Ethernet
1.5 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 34: Packet switching versus circuit switching
Great for bursty data
  resource sharing
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
Is packet switching a “slam dunk winner?”

## Slide 35: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L

## Slide 36: Packet Switching: Message Segmenting
Now break up the message into 5000 packets
Each packet 1,500 bits
1 msec to transmit packet on one link
pipelining: each link works in parallel
Delay reduced from 15 sec to 5.002 sec

## Slide 37: Packet-switched networks: forwarding
datagram network:
  destination address in packet determines next hop
  routes may change during session (flexible?)
  no “per flow” state, hence more scalable
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time
  path is not a dedicated path as in circuit switched (i.e., store & forward of packets)
  routers maintain per-call state
datagram networks need per packet routing.

## Slide 38: Network Taxonomy
Telecommunication
networks
Circuit-switched
networks
FDM
TDM
Packet-switched
networks
Networks
with VCs
Datagram
Networks

## Slide 39: Roadmap
  What is a Computer Network?
  Applications of Networking
  Classification of Networks
  Layered Architecture
  Network Core
  Delay & loss in packet-switched networks
  Internet Structure
  Transmission Media (Tutorial)
  History (self study)

## Slide 40: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
if queue is full, arriving packets dropped (Drop-Tail)
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 41: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 42: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 43: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 44: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 45: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 46: Roadmap
  What is a Computer Network?
  Applications of Networking
  Classification of Networks
  Layered Architecture
  Network Core
  Delay & loss in packet-switched networks
  Internet Structure
  Transmission Media (Tutorial)
  History (self study)

## Slide 47: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, BBN/Genuity, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 48: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 49: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 50: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 51: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
Internet/ISP structure
performance: loss, delay
layering and service models
You now have:
context, overview, “feel” of networking
more depth, detail to follow!