## Slide 1: High Performance Liquid Chromatography

## Slide 2: Introduction
Separation and identification of amino acids, carbohydrates, lipids, nucleic acids, proteins, pigments, steroids, pharmaceuticals, and many other biologically active molecules
1. Resolution and speed of analysis far exceed the classical methods.
2. HPLC columns can be reused without repacking or regeneration.
3. Reproducibility is greatly improved because the parameters affecting the efficiency of the separation can be closely controlled.
4. Instrument operation and data analysis are easily automated.
5. HPLC is adaptable to very small sample sizes or large-scale, preparative procedures.

## Slide 3: Instrumentation

## Slide 4
Solvent Reservoir- 500ml, degassed (refluxing, filtration through a vacuum filter, ultrasonic vibration, and purging with an inert gas)
Pumping Systems-
1. It must be capable of pressure outputs of at least 500 psi and preferably up to 5000 psi.
2. It should have a controlled, reproducible flow delivery of about 1 mL/min for analytical applications and up to 100 mL/min for preparative applications.
3. It should yield pulse-free solvent flow.
4. It should have a small holdup volume.

## Slide 5
Injection Port- syringe
Columns- stainless steel or glass-Teflon tubing, inside diameters are 2.1, 3.2, or 4.5 mm for analytical separations and up to 30 mm for preparative applications, 5 to 100 cm, but 10- to 20-cm long
Detector- differential refractometer, photometer (UV), flouriscence
Collection of Eluent-
Analysis of HPLC Data- computer controlled

## Slide 7: Stationary Phases in HPLC
Porous layer beads - outer shell of silica, alumina, or ion-exchange resin, average diameter of the beads ranges from 20 to 45 um.
Microporous particles are available in two sizes: 20 to 40 diameter with longer pores and 5 to 10 with short pores. The microporous beads are prepared from alumina, silica, ion-exchanger resins, and chemically bonded phases

## Slide 8: Liquid-Solid (Adsorption) Chromatography
Solid particles
micro Porasil (Waters Associates), BioSilA (Bio-Rad Laboratories), LiChrosorb Si-100 Partisil, Vydac, ALOX 60D (several suppliers), and Supelcosil (Supelco).

## Slide 9: Liquid-Liquid (Partition) Chromatography
Solid supports were coated with a liquid stationary phase
Chemical bonding
Reverse phase HPLC
Ion exchange HPLC
Gel exclusion HPLC
Chiral chromatography

## Slide 10: The Mobile Phase
Purity
Reactivity
Detector compatability

## Slide 11: Sample Preparation and Selection of HPLC Operating Conditions
1. Chemical nature and proper preparation of the sample.
2. Selection of type of chromatography (partition, adsorption, ion-exchange, gel-exclusion).
3. Choice of solvent system and mode of elution.
4. Selection of column packing.
5. Choice of equipment (type of detector).